TYMETER SECONDS WHEEL LABEL REPLACEMENT

- Either remove the clock from its case, or remove the chassis from the console cabinet as appropriate for the model clock you have.

- Remove the two screws holding the motor to the wheel assembly (white arrows in Figure 1).  The seconds wheel and motor come off together (Figure 2).

- Make sure the old seconds wheel surface is clean and free of any of the old decal flaking to insure best adherence of the new label.

- Start to remove about an inch of the adhesive backing from the new seconds label (Figure 3).

- Using scissors, cut off about a half inch of backing, leaving the sticky surface exposed (Figure 4).

- Align the new label over top of the old decal (Figure 5).  The number “30” should roughly align with the plastic indent on the wheel (red arrow in Figure 5).

- When you are happy with the label positioning, then press down on the portion of the label where you removed the backing (Figure 6).

- You can then peel away the remainder of the backing, and if the label has been aligned properly it should remain that way as you guide it around the wheel Figure 7).

- Reinstall motor (Figure 8).  There should be enough play in the top mounting hole that you can move the motor/seconds wheel to a position where there is no interference between either the shaft or the clock white metal faceplate (white arrows in Figure 8); then tighten motor mounting screws.  Much of the damage to the original decals comes from the wheel rubbing against the front metal bezel or the plastic minutes wheel shaft.

- Reassemble into case/cabinet as appropriate.

For further information, contact N3CW.