## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: General Licensing Class Chapter 10
Your HF Transmitter
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 6: Your HF Transmitter
Amplitude modulation is the type of modulation that varies the instantaneous power level of the RF signal. (G8A05)
A balanced modulator is the circuit used to combine signals from the carrier oscillator and speech amplifier and send the result to the filter in a typical single-sideband phone transmitter. (G7C02)
Circuit inside a Balanced Modulator.

## Slide 7
A filter is used to process signals from the balanced modulator and send them to the mixer in a single-sideband phone transmitter. (G7C01)
The phone emission that uses the narrowest frequency bandwidth is single sideband. (G8A07)
SSB Transmitter Block Diagram
Your HF Transmitter

## Slide 8: Your HF Transmitter
The purpose of a speech processor as used in a modern transceiver is to increase the intelligibility of transmitted phone signals during poor conditions. (G4D01)
The transmit audio or microphone gain control is typically adjusted for proper Automatic Level Control (ALC) setting on an amateur single sideband transceiver. (G2A12)
A speech processor increases average power of a transmitted single sideband phone signal. (G4D02)
Your HF Transmitter

## Slide 9: Your HF Transmitter
If a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode, Improper action of ALC distorts the signal and can cause spurious emissions. (G4A14)
The purpose of using Automatic Level Control (ALC) with a RF power amplifier is to reduce distortion due to excessive drive. (G4A05)
Excessive drive power can lead to permanent damage when using a solid-state RF power amplifier. (G4A07)
Another effect of over-modulation is excessive bandwidth. (G8A08)
An incorrectly adjusted speech processor can cause: (G4D03)
        Distorted speech
        Splatter
        Excessive background pickup
          All of these choices are correct.

## Slide 10: Your HF Transmitter
Flat-topping of a single-sideband phone transmission is signal distortion caused by excessive drive. (G8A10)
Oscilloscope Waveform Showing “Flattopping”

## Slide 11: Your HF Transmitter
One test that is often run on a SSB transmitter is the two-tone test. A two-tone test analyzes the linearity of a transmitter. (G4B15)
Two non-harmonically related audio signals are used to conduct a two-tone test. (G4B07)

## Slide 12: Your HF Transmitter
The MODULATION ENVELOPE of an AM signal is the waveform created by connecting the peak values of the modulated signal. (G8A11)
An oscilloscope is an item of test equipment that contains horizontal and vertical channel amplifiers. (G4B01)

## Slide 13: Your HF Transmitter
An oscilloscope is an item of test equipment that contains horizontal and vertical channel amplifiers. (same statement as previous slide) (G4B01)
V & H Channel Amplifiers

## Slide 14: Your HF Transmitter
An oscilloscope is the best instrument to use when checking the keying waveform of a CW transmitter. (G4B03)
You can use a battery-powered oscilloscope to take measurements in the field, and use it on your workbench as well.

## Slide 15
The attenuated RF output of the transmitter is the signal source that is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal. (G4B04)
One advantage of an oscilloscope versus a digital voltmeter is that complex waveforms can be measured. (G4B02)
Damped oscillation seen on a digital oscilloscope.
Your HF Transmitter

## Slide 16: Your HF Transmitter
A time delay sometimes included in a transmitter keying circuit to allow time for transmit-receive changeover operations to complete properly before RF output is allowed. (G4A09)
The reason for neutralizing the final amplifier stage of a transmitter is to eliminate self-oscillations. (G7B01)
Oscillating amplifier
Your HF Transmitter

## Slide 17: Your HF Transmitter
Frequency modulation is the name of the process which changes the frequency of an RF wave to convey information. (G8A03)
Audio (modulation)
RF with no modulation
AM RF with modulation
FM RF with modulation
Your HF Transmitter

## Slide 18: Your HF Transmitter
The multiplier is the name of the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency. (G8B04)
16 kHz is the total bandwidth of an FM-phone transmission having a 5 kHz deviation and a 3 kHz modulating frequency. (G8B06)
      Total Bandwidth is equal to the peak devation + the highest modulating frequency times 2.
        (because the FM signal is symetrical about the carrier frequency).
      In this example the total bandwidth would be (5 KHz + 3KHz ) * 2 or (8 KHz) *2 or 16 KHz.

## Slide 19: Your HF Transmitter
416.7 Hz is the frequency deviation for a 12.21-MHz reactance-modulated oscillator in a 5-kHz deviation, 146.52-MHz FM-phone transmitter. (G8B07)
  Since the FM deviation is also multiplied, there will be much less than 5 KHz deviation on the oscillator that is being multiplied up to the transmit frequency.
  The multiplier would be 146.52 MHz divided by 12.21 MHz or 12.
  Therefore if we desired 5 KHz of deviation at 146.52 would only need 1/12 of that at 12.21 or the required deviation would be 5,000 Hz divided by 12 or 416.66 Hertz.
The 2-meter rig in a school gym ready to make contact with the licensed ham astronauts aboard the International Space Station.
International Space Station.
Deviation levels must be accurate to insure a solid contact with the hams in space.
Your HF Transmitter

## Slide 20: Your HF Transmitter
Phase modulation is produced by a reactance modulator connected to an RF power amplifier. (G8A04)
Phase modulation is the name of the process that changes the phase angle of an RF wave to convey information. (G8A02)
To determine the efficiency of an RF power amplifier, divide the RF output power by the DC input power. (G7B08)
  Example:
    A 100 watt 2 meter power amplifier that draws 10 amperes from a 13.8 Volt Power supply has an efficiency of 72%.
      Efficiency = 100 watts / (13.8 * 10)
      Efficiency = 100/138
      Efficiency = 72%
Your HF Transmitter

## Slide 21: Your HF Transmitter
The output PEP from a transmitter is 100 watts if an oscilloscope measures 200 volts peak-to-peak across a 50-ohm dummy load connected to the transmitter output. (G5B06)
    PEP =[ (200 / 2) x .707] ² / R
    PEP= [70.7] ² / 50
    PEP= 4,998 / 50
    PEP= 99.97 Watts (close enough to 100)
625 watts is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output. (G5B14)
  PEP =[ (500 / 2) x .707] ² / R
  PEP= [ 250 * .707] ² / 50
  PEP= [176.75] ² / 50
  PEP= 31,240. 56 / 50
  PEP = 624.81 Watts (close enough to 625)
Your HF Transmitter

## Slide 22: Your HF Transmitter
The ratio of peak envelope power to average power for an unmodulated carrier is 1.00. (G5B11)
    An unmodulated carrier is simultaneous peak and average.
1060 watts is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts. (G5B13)
    A steady carrier illustrates both peak power as well as average power.
A two-times increase or decrease in power results in a change of approximately 3 dB. (G5B01)
Signal Strength | Relative Intensity | Received Voltage
S1 | -48 dB | 0.2 µV
S2 | -42 dB | 0.4 µV
S3 | -36 dB | 0.8 µV
S4 | -30 dB | 1.6 µV
S5 | -24 dB | 3.2µV
S6 | -18 dB | 6.3 µV
S7 | -12 dB | 13 µV
S8 | -6 dB | 25 µV
S9 | 0 dB | 50 µV
Your HF Transmitter

## Slide 23
To make the S-meter on a distant receiver rise from S8 to S9, you would have to raise the power output of your transmitter approximately 4 times. (G4D07)
Changing from S8 to S9 is one “S” unit. One “S” unit is 6db, and 6db is a 4-times change.
Assuming a properly calibrated S meter, an S meter reading of 20 dB over S-9 is 100 times stronger compared to an S-9 signal. (G4D05)
0 dB | = | 0 times change
3 dB | = | 2 times change
6 dB | = | 4 times change
9 dB | = | 8 times change
10 dB | = | 10 times change
Your HF Transmitter

## Slide 24: Your HF Transmitter
The Class C amplifier is not linear. A Class C power stage is appropriate for amplifying a FM modulated signal. (G7B11)
Class C amplifiers have the highest efficiency. (G7B02)
Various Classes of Transistorized Amplifiers
Lowest Distortion
Highest Efficiency

## Slide 25
Linear amplifiers are usually Class A amplifiers. Low distortion is a characteristic of a Class A amplifier. A linear amplifier is an amplifier in which the output preserves the input waveform. (G7B10)
    This is because 100 % of the waveform is amplified.
    They are, therefore, most appropriate for amplifying phone signals.
The correct adjustment for the load or coupling control of a vacuum tube RF power amplifier is to adjust for maximum power output without exceeding maximum allowable plate current. (G4A08)
Your HF Transmitter

## Slide 26
A pronounced dip on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control. (G4A04)
    When the plate tuning reaches resonance, the plate current will dip.
    This is because energy is moving back and forth between the Capacitor and the inductor
Your HF Transmitter

## Slide 27
Your HF Transmitter
Element 3 General Class Question Pool
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 28: G8A05 What type of modulation varies the instantaneous power level of the RF signal?
Phase modulation.
Frequency modulation.
Spread Spectrum modulation.
Amplitude modulation.

## Slide 29: G7C02 What output is produced by a balanced modulator?
Frequency modulated RF
Audio with equalized frequency response
Audio extracted from the modulation signal
Double-sideband modulated RF

## Slide 30: G7C03 What is one reason to use an impedance matching transformer at a transmitter output?
To minimize transmitter power output
To present the desired impedance to the transmitter and feed line
To reduce power supply ripple
To minimize radiation resistance

## Slide 31: G7C01 What circuit is used to select one of the sidebands from a balanced modulator?
Carrier oscillator
Filter
IF amplifier
RF amplifier

## Slide 32: G8A07 Which of the following phone emissions uses the narrowest bandwidth?
Single sideband
Vestigial sideband
Phase modulation
Frequency modulation

## Slide 33: G4D01 What is the purpose of a speech processor in a transceiver?
Increase the apparent loudness of transmitted voice signals
Increase transmitter bass response for more natural-sounding SSB signals
Prevent distortion of voice signals
Decrease high-frequency voice output to prevent out-of-band operation

## Slide 34: G4D02 How does a speech processor affect a single sideband phone signal?
It increases peak power
It increases average power
It reduces harmonic distortion
It reduces intermodulation distortion

## Slide 35: G2A12 What control is typically adjusted for proper ALC setting on a single sideband transceiver?
RF clipping level
Transmit audio or microphone gain
Antenna inductance or capacitance
Attenuator level

## Slide 36: G4A05 Why is automatic level control (ALC) used with an RF power amplifier?
To balance the transmitter audio frequency response
To reduce harmonic radiation
To prevent excessive drive
To increase overall efficiency

## Slide 37: G8A08 Which of the following is an effect of overmodulation?
Insufficient audio
Insufficient bandwidth
Frequency drift
Excessive bandwidth

## Slide 38: G4D03 What is the effect of an incorrectly adjusted speech processor?
Distorted speech
Excess intermodulation products
Excessive background noise
All these choices are correct

## Slide 39: G8A10 What is meant by the term “flat-topping,” when referring to an amplitude-modulated phone signal?
Signal distortion caused by insufficient collector current
The transmitter’s automatic level control (ALC) is properly adjusted
Signal distortion caused by excessive drive or speech levels
The transmitter’s carrier is properly suppressed

## Slide 40: G4B08 What transmitter performance parameter does a two-tone test analyze?
Linearity
Percentage of suppression of the carrier and undesired sideband for SSB
Percentage of frequency modulation
Percentage of carrier phase shift

## Slide 41: G4B07 What signals are used to conduct a two-tone test?
Two audio signals of the same frequency shifted 90 degrees
Two non-harmonically related audio signals
Two swept frequency tones
Two audio frequency range square wave signals of equal amplitude

## Slide 42: G8A11 What is the modulation envelope of an AM signal?
The waveform created by connecting the peak values of the modulated signal
The carrier frequency that contains the signal
Spurious signals that envelop nearby frequencies
The bandwidth of the modulated signal

## Slide 43: G4B01 What item of test equipment contains horizontal and vertical channel amplifiers?
An ohmmeter
A signal generator
An ammeter
An oscilloscope

## Slide 44: G4B03 Which of the following is the best instrument to use for checking the keying waveform of a CW transmitter?
An oscilloscope
A field strength meter
A sidetone monitor
A wavemeter

## Slide 45: G4B04 What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
The local oscillator of the transmitter
An external RF oscillator
The transmitter balanced mixer output
The attenuated RF output of the transmitter

## Slide 46: G4B02 Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
An oscilloscope uses less power
Complex impedances can be easily measured
Greater precision
Complex waveforms can be measured

## Slide 47: G7B01 What item of test equipment contains horizontal and vertical channel amplifiers?
An ohmmeter
A signal generator
An ammeter
An oscilloscope

## Slide 48: G8A03 What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
Frequency convolution
Frequency transformation
Frequency conversion
Frequency modulation

## Slide 49: G8B04 What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
Mixer
Reactance modulator
Balanced converter
Multiplier

## Slide 50: G8B06 What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
3 kHz
5 kHz
8 kHz
16 kHz

## Slide 51: G8B07 What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
101.75 Hz
416.7 Hz
5 kHz
60 kHz

## Slide 52: G8A04 What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
Multiplex modulation
Phase modulation
Amplitude modulation
Pulse modulation

## Slide 53: G8A02 What is the name of the process that changes the phase angle of an RF signal to convey information?
Phase convolution
Phase modulation
Phase transformation
Phase inversion

## Slide 54: G7B08 How is the efficiency of an RF power amplifier determined?
Divide the DC input power by the DC output power
Divide the RF output power by the DC input power
Multiply the RF input power by the reciprocal of the RF output power
Add the RF input power to the DC output power

## Slide 55: G5B14 What is the output PEP of 500 volts peak-to-peak across a 50-ohm load?
8.75 watts
625 watts
2500 watts
5000 watts

## Slide 56: G5B11 What is the ratio of PEP to average power for an unmodulated carrier?
0.707
1.00
1.414
2.00

## Slide 57: G1C11 What measurement is specified by FCC rules that regulate maximum power?
RMS output from the transmitter
RMS input to the antenna
PEP input to the antenna
PEP output from the transmitter

## Slide 58: G5B13 What is the output PEP of an unmodulated carrier if the average power is 1060 watts?
530 watts
1060 watts
1500 watts
2120 watts

## Slide 59: G5B01 What dB change represents a factor of two increase or decrease in power?
Approximately 2 dB
Approximately 3 dB
Approximately 6 dB
Approximately 9 dB

## Slide 60: G7B04 In a Class A amplifier, what percentage of the time does the amplifying device conduct?
100%
More than 50% but less than 100%
50%
Less than 50%

## Slide 61: G7B11 For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal?
SSB
FM
AM
All these choices are correct

## Slide 62: G7B02 Which of these classes of amplifiers has the highest efficiency?
Class A
Class B
Class AB
Class C

## Slide 63: G7B10 Which of the following describes a linear amplifier?
Any RF power amplifier used in conjunction with an amateur transceiver
An amplifier in which the output preserves the input waveform
A Class C high efficiency amplifier
An amplifier used as a frequency multiplier

## Slide 64: G4A08 What is the correct adjustment for the LOAD or COUPLING control of a vacuum tube RF power amplifier?
Minimum SWR on the antenna
Minimum plate current without exceeding maximum allowable grid current
Highest plate voltage while minimizing grid current
Desired power output without exceeding maximum allowable plate current

## Slide 65: G4A04 What is the effect on plate current of the correct setting of a vacuum-tube RF power amplifier’s TUNE control?
A pronounced peak
A pronounced dip
No change will be observed
A slow, rhythmic oscillation

## Slide 66: G4A09 What is the purpose of delaying RF output after activating a transmitter’s keying line to an external amplifier?
To prevent key clicks on CW
To prevent transient overmodulation
To allow time for the amplifier to switch the antenna between the transceiver and the amplifier output
To allow time for the amplifier power supply to reach operating level

## Slide 67: Thank You!