## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: Chapter 16
HF Antennas​
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 6
HF Antennas
32 feet is the approximate length for a 1/2-wave dipole antenna cut for 14.250 MHz. (G9B10)
    Calculate ½ wavelength in feet by dividing 468 by the frequency in MHz.
    468 / 14.250
    32.8 Feet (close enough to 33 feet.)
The approximate length for a 1/2-wave dipole antenna cut for 3.550 MHz is 131 feet. (G9B11)
    Calculate ½ wavelength in feet by dividing 468 by the frequency in MHz.
    468 / 3.550 or
    131.8 Feet (close enough to132 feet.)
HF Antennas

## Slide 7
HF Antennas
An advantage of a horizontally polarized as compared to vertically polarized HF antenna is lower ground reflection losses. (G9B09)
  Propagation via multi-hop refraction:
    RF energy is lost each time the radio wave is reflected from the Earth's surface.
  The amount of energy lost depends on:
    Frequency of the wave.
    Angle of incidence.
    Ground irregularities.
    Electrical conductivity of the point of reflection.
Near Vertical Incident Skywave (NVIS) propagation permits short distance MF or HF propagation using high elevation angles. (G3C10)
  Lower your antenna.
  Will develop a “higher elevation angle of radiation.
  This establishes shorter-than-normal skywave communications.
HF Antennas

## Slide 8
HF Antennas
Horizontal dipoles placed between 1/10 and 1/4 wavelength above the ground will be most effective for short-skip communications on 40 meters during the day. (G9D01)
  Antennas used for DXing should have low takeoff angles.
  One thing that affects the takeoff angle of an antenna is its height above ground.
  To have further communications, raise the dipole, lower to receive first hop.
Portable half-wave dipole.
Typical dipole radiation pattern.
Above Ground Level gains in dBi.
HF Antennas

## Slide 9
HF Antennas
As the antenna is lowered from 1/4 wave above ground, the feed-point impedance of a 1/2 wave dipole antenna steadily decreases. (G9B07)
  Antenna height affects the feed point impedance.
The feed-point impedance of a 1/2 wave dipole steadily increases as the feed-point location is moved from the center toward the ends. (G9B08)
A common name for a dipole with a single central support is a Inverted V. (G9D12)
HF Antennas

## Slide 10
HF Antennas
The feed-point impedance of an end-fed half-wave antenna is very high. (G9D02)
    A resonant dipole has an impedance at the center of about 72 ohms.
    End-fed impedance typically will be something on the order of 2500 ohms.
The radiation pattern of a dipole antenna in free space in a plane containing the conductor will be a figure-eight at right angles to the antenna. (G9B04)
    Reception and transmission are minimal off the ends of the wire.
HF Antennas

## Slide 11
HF Antennas
The maximum direction radiation from a portable/mobile VHF/UHF “halo” antenna is omnidirectional in the plane of the halo. (G9D03)
Antenna height affects the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna in that if an antenna is less than ½ wavelength high, the azimuthal pattern is almost omnidirectional. (G9B05)
HF Antennas

## Slide 12
HF Antennas
Omnidirectional in azimuth best describes the radiation pattern of a quarter-wave ground-plane vertical antenna. (G9B03)
The approximate length for a ¼-wave vertical antenna cut for 28.5 MHz is 8 feet. (G9B12)
Vertical radiation pattern showing elevation of signal from a horizontal dipole ½ wavelength above the ground.
8.2 Feet (close enough to 8 feet.)
HF Antennas

## Slide 13
HF Antennas
The radial wires of a ground-mounted vertical antenna system should be placed on the surface or buried a few inches below the ground. (G9B06)
Ground wire kit.
Surface mounted ground wires.
Ground wire blank plate.
HF Antennas

## Slide 14
HF Antennas
A directional antenna would be the best HF antenna to use for minimizing interference. (G9C11)
  By definition: An antenna that has a single well-defined direction of maximum gain.
    An antenna can only increase signal strength in one direction at the expense of a decrease somewhere else.
      This applies to a Yagi or a beam.
In a three-element Yagi, the reflector is longer, and the director is shorter, than the driven element. (G9C03)
  Typically the reflector is 5% longer and the director is 5% shorter than the driven element.
HF Antennas

## Slide 15
The approximate length of the driven element of a Yagi antenna is 1/2 wavelength. (G9C02)
Increasing the length of the boom and adding more directors will increase the gain of a Yagi antenna. (G9C05)
The “main lobe” or “major lobe” of a directive antenna is the direction of maximum radiated field strength from the antenna. (G9C08)
HF Antennas

## Slide 16
The “front-to-back ratio” of a Yagi antenna is the power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction. (G9C07)
In a Yagi antenna design, the following variables that could be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth: (G9C10)
  The physical length of the boom.
  The number of elements on the boom.
  The spacing of each element along the boom.
All of these choices are correct
The larger your antennas and the higher they are mounted on your tower, the better your range to distance DX stations!
HF Antennas

## Slide 17
HF Antennas
Larger diameter elements increase the bandwidth of a Yagi antenna. (G9C01)
An advantage of using a gamma match with a Yagi antenna is that it does not require that the driven element be insulated from the boom. (G9C12)
HF Antennas

## Slide 18
HF Antennas
A beta or hairpin match is a shorted transmission line stub placed at the feed point of a Yagi antenna to provide impedance matching. (G9C16)
HF Antennas

## Slide 19
HF Antennas
The advantage of vertical stacking of horizontally polarized Yagi antennas is that it narrows the main lobe in elevation. (G9D05)
Yagi antennas spaced vertically 1/2 wavelength apart typically is approximately 3 dB higher than the gain of a single 3-element Yagi. (G9C09)
    Remember, 2 times the gain is 3dB.
Vertical Stacking of Horizontally polarized.
Horizontal Stacking of Vertically polarized.
HF Antennas

## Slide 20
HF Antennas
The primary purpose of antenna traps is to permit multiband operation. (G9D04)
A disadvantage of multiband antennas is that they have poor harmonic rejection. (G9D11)
HF Antennas

## Slide 21
HF Antennas
One disadvantage of a directly fed random-wire antenna is that you may experience RF burns when touching metal objects in your station. (G9B01)
  As the name implies, random-wire antennas are a random-length.
  To match the antenna to the transmitter, you’ll need an antenna tuner.
  Because of this, there may be high RF levels in the shack when you are transmitting.
An antenna coupler is often used to enable matching the transmitter output to an impedance other than 50 ohms. (G4A06)
Auto Tuner
Tuner Schematic
Manual Tuner
HF Antennas

## Slide 22
HF Antennas
The terms dBi and dBd when referring to antenna gain, dBi refers to an isotropic antenna and dBd refers to a dipole antenna. (G9C15)
  dBi: decibels referenced to an isotropic radiator.
    The isotropic antenna doesn’t exist in real life, if it did its gain would be 0 when measured in dBi.
  dBd: decibels referenced to a dipole.
    The dipole antenna has a gain of 2.15 dB over the isotropic radiator, and it has a gain of 0 when measured in dBd.
  Isotropic radiators are used as reference radiators.
  An isotropic radiator is a theoretical point source of electromagnetic or sound waves.
Equal power radiated in all directions; i.e., equipotential electric field at constant radii surface from the center of sphere where point source is located.
HF Antennas

## Slide 23
HF Antennas
Comparing gain for the same antenna between dBi and dBd will show dBi gain figures are 2.15 dB higher than dBd gain figures. (G9C04)
  dBi is dB isotropic.
  An isotropic radiator is a theoretical point source of electromagnetic waves which radiates the same intensity of radiation in all directions.
  It has no preferred direction of radiation.
  It radiates uniformly in all directions over a sphere centered on the point source.
Nulls in the radiation pattern of a small loop antenna (less than 1/3 wavelength in circumference) will be broadside to the loop. (G9D10)
  This small loop works well even low to the ground and is easy to hide.
The combined vertical and horizontal polarization pattern of a multi-wavelength horizontal loop antenna is virtually omnidirectional with a lower peak vertical radiation angle than a dipole. (G9D13)
HF Antennas

## Slide 24
HF Antennas
The elements of a quad antenna are square loops. Each side of a quad antenna driven element is approximately 1/4 wavelength. (G9C13)
  Each side of the cubical quad is ¼ wavelength.
The forward gain of a two-element quad antenna is about the same as the forward gain of a three-element Yagi antenna. (G9C14)
Driven Element for each side (in feet) =
1005
f (MHz)
/
4
Horizontal polarization feed-point
HF Antennas

## Slide 25
HF Antennas
The reflector element must be approximately 5% longer than the driven element for a two-element quad antenna when the antenna is meant to operate as a beam antenna, assuming one of the elements is used as a reflector. (G9C06)
For a log periodic antenna, the element length and spacing vary logarithmically along the boom. (G9D07)
The gain of a log periodic antenna is less than that of a Yagi, but an advantage of a log periodic antenna is wide bandwidth. (G9D06)
290 – 2000 MHz
0.15 – 300 MHz
EW8DQ, and his rotatable HF log-periodic beam antenna in Belarus
HF Antennas

## Slide 26
HF Antennas
The primary use for a Beverage antenna is as directional receiving for low HF bands. (G9D09)
  A beverage antenna is not used for transmitting due to high losses compared to other types of antennas.
HF Antennas

## Slide 27
HF Antennas
Efficiency of an electrically short antenna limits HF mobile installations. (G4E05)
  It is not possible to put a full ¼ wavelength 75-meter antenna on a mobile.
  On 40-meters and lower frequencies, no mobile antenna is efficient.
  Any antenna for these frequencies would be inefficient.
One disadvantage of using a shortened mobile antenna as opposed to a full size antenna is that the operating bandwidth may be very limited. (G4E06)
HF Antennas

## Slide 28
HF Antennas
A “screwdriver” mobile antenna adjusts its feed-point impedance by varying the base loading inductance. (G9D08)
From transmitter.
HF Antennas

## Slide 29
HF Antennas
A "capacitance hat" on a mobile antenna is a device to electrically lengthen a physically short antenna. (G4E01)
  The home-brew capacity hat helps improve mobile HF antenna efficiency.
The purpose of a "corona ball" on a HF mobile antenna is to reduce high voltage discharge from the tip of the antenna. (G4E02)
  They dissipate static build up from movement through the air caused by vehicle movement.
HF Antennas

## Slide 30
HF Antennas
The antenna and feed line must be connected to an antenna analyzer when it is being used for SWR measurements. (G4B11)
A use for an antenna analyzer, other than measuring the SWR of an antenna system, is determining the impedance of an unknown or unmarked coaxial cable. (G4B13)
Strong signals from nearby transmitters can affect the accuracy of measurements when making measurements on an antenna system with an antenna analyzer. (G4B12)
MFJ-259B
Comet CAA-500
HF Antennas

## Slide 31
HF Antennas
A field-strength meter may also be used to monitor relative RF output when making antenna and transmitter adjustments. (G4B08)
The radiation pattern of an antenna can be determined with a field strength meter. (G4B09)
  One other use for a field strength meter is close-in radio direction-finding.
HF Antennas

## Slide 32: Element 3 General Class Question Pool
In An Emergency
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 33
8 feet.
16 feet.
24 feet.
33 feet.
G9B10
What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz?

## Slide 34
G9B11 What is the approximate length for a 1/2-wave dipole antenna cut for 3.550 MHz?
42 feet.
84 feet.
132 feet.
263 feet.
G9B11
What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz?

## Slide 35
G9B11 What is the approximate length for a 1/2-wave dipole antenna cut for 3.550 MHz?
Lower ground losses
Lower feed point impedance
Shorter radials
Lower radiation resistance
G9B09
Which of the following is an advantage of using a horizontally polarized as compared to a vertically polarized HF antenna?

## Slide 36
Propagation near the MUF
Short distance MF or HF propagation at high elevation angles
Long path HF propagation at sunrise and sunset
Double hop propagation near the LUF
G3C10
What is near vertical incidence skywave (NVIS) propagation?

## Slide 37
A horizontal dipole placed between 1/10 and 1/4 wavelength above the ground
A vertical antenna placed between 1/4 and 1/2 wavelength above the ground
A horizontal dipole placed at approximately 1/2 wavelength above the ground
A vertical dipole placed at approximately 1/2 wavelength above the ground
G9D01
Which of the following antenna types will be most effective as a near vertical incidence skywave (NVIS) antenna for short-skip communications on 40 meters during the day?

## Slide 38
It steadily increases
It steadily decreases
It peaks at about 1/8 wavelength above ground
It is unaffected by the height above ground
G9B07
How does the feed point impedance of a horizontal 1/2 wave dipole antenna change as the antenna height is reduced to 1/10 wavelength above ground?

## Slide 39
It steadily increases
It steadily decreases
It peaks at about 1/8 wavelength from the end
It is unaffected by the location of the feed point
G3B08
How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends?

## Slide 40
Inverted V
Inverted L
Sloper
Lazy H
G9D12
What is the common name of a dipole with a single central support?

## Slide 41
Very low
Approximately 50 ohms
Approximately 300 ohms
Very high
G9D02
What is the feed point impedance of an end-fed half-wave antenna?

## Slide 42
It is a figure-eight at right angles to the antenna
It is a figure-eight off both ends of the antenna
It is a circle (equal radiation in all directions)
It has a pair of lobes on one side of the antenna and a single lobe on the other side
G9B04
What is the radiation pattern of a dipole antenna in free space in a plane containing the conductor?

## Slide 43
Broadside to the plane of the halo
Opposite the feed point
Omnidirectional in the plane of the halo
On the same side as the feed point
G9D03
In which direction is the maximum radiation from a VHF/UHF “halo” antenna?

## Slide 44
If the antenna is too high, the pattern becomes unpredictable
Antenna height has no effect on the pattern
If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional
If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated
G9B05
How does antenna height affect the azimuthal radiation pattern of a horizontal dipole HF antenna at elevation angles higher than about 45 degrees?

## Slide 45
Bi-directional in azimuth
Isotropic
Hemispherical
Omnidirectional in azimuth
G9B03
Which of the following best describes the radiation pattern of a quarter-wave ground-plane vertical antenna?

## Slide 46
G9B09 Which of the following is an advantage of a horizontally polarized as compared to vertically polarized HF antenna?
8 feet
11 feet
16 feet
21 feet
G9B12
What is the approximate length for a 1/4 wave monopole antenna cut for 28.5 MHz?

## Slide 47
As high as possible above the ground
Parallel to the antenna element
On the surface or buried a few inches below the ground
At the center of the antenna
G9B06
Where should the radial wires of a ground-mounted vertical antenna system be placed?

## Slide 48
G9B07 How does the feed-point impedance of a ½ wave dipole antenna change as the antenna is lowered below ¼ wave above ground ?
The reflector is longer, and the director is shorter
The reflector is shorter, and the director is longer
They are all the same length
Relative length depends on the frequency of operation
G9C03
How do the lengths of a three-element Yagi reflector and director compare to that of the driven element?

## Slide 49
G9D01 Which of the following antenna types will be most effective as a Near Vertical Incidence Skywave (NVIS) antenna for short- skip communications on 40 meters during the day ?
1/4 wavelength
1/2 wavelength
3/4 wavelength
1 wavelength
G9C02
What is the approximate length of the driven element of a Yagi antenna?

## Slide 50
G9D12 What is the common name of a dipole with a single central support?
Gain increases
Beamwidth increases
Front-to-back ratio decreases
Resonant frequency is lower
G9C05
What is the primary effect of increasing boom length and adding directors to a Yagi antenna?

## Slide 51
G9B04 What is the radition pattern of a dipole antenna is free space in a plane containing the conductor ?
The magnitude of the maximum vertical angle of radiation
The point of maximum current in a radiating antenna element
The maximum voltage standing wave point on a radiating element
The direction of maximum radiated field strength from the antenna
G9C08
What is meant by the “main lobe” of a directive antenna?

## Slide 52
G9D02 What is the feed-point impedance of a end-fed half wave antenna ?
The number of directors versus the number of reflectors
The relative position of the driven element with respect to the reflectors and directors
The power radiated in the major lobe compared to that in the opposite direction
The ratio of forward gain to dipole gain
G9C07
What does “front-to-back ratio” mean in reference to a Yagi antenna?

## Slide 53
G9B05 How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna?
The physical length of the boom
The number of elements on the boom
The spacing of each element along the boom
All these choices are correct
G9C10
Which of the following can be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth of a Yagi antenna?

## Slide 54
G3C10 What is Near Vertical Incidence Skywave (NVIS) propagation ?
Larger-diameter elements
Closer element spacing
Loading coils in series with the element
Tapered-diameter elements
G9C01
Which of the following would increase the bandwidth of a Yagi antenna?

## Slide 55
G9B12 What is the approximate length for a ¼ wave vertical antenna cut for 28.5 MHZ?
It does not require the driven element to be insulated from the boom
It does not require any inductors or capacitors
It is useful for matching multiband antennas
All these choices are correct
G9C12
Which of the following is a characteristic of using a gamma match with a Yagi antenna?

## Slide 56
G9B03 Which of the following best describes the radiation pattern of a quarter-wave ground plane vertical antenna?
A shorted transmission line stub placed at the feed point of a Yagi antenna to provide impedance matching
A 1/4 wavelength section of 75-ohm coax in series with the feed point of a Yagi to provide impedance matching
A series capacitor selected to cancel the inductive reactance of a folded dipole antenna
A section of 300-ohm twin-lead transmission line used to match a folded dipole antenna
G9C11
What is a beta or hairpin match?

## Slide 57
It allows quick selection of vertical or horizontal polarization
It allows simultaneous vertical and horizontal polarization
It narrows the main lobe in azimuth
It narrows the main lobe in elevation
G9D05
What is an advantage of vertically stacking horizontally polarized Yagi antennas?

## Slide 58
G9D03 In which direction is the maximum radiation from a portable VHF/UHF “halo” antenna?
Approximately 1.5 dB higher
Approximately 3 dB higher
Approximately 6 dB higher
Approximately 9 dB higher
G9C09
In free space, how does the gain of two three-element, horizontally polarized Yagi antennas spaced vertically 1/2 wavelength apart typically compare to the gain of a single three-element Yagi?

## Slide 59
To enable multiband operation
To notch spurious frequencies
To provide balanced feed point impedance
To prevent out-of-band operation
G9D04
What is the primary function of antenna traps?

## Slide 60
They present low impedance on all design frequencies
They must be used with an antenna tuner
They must be fed with open wire line
They have poor harmonic rejection
G9D11
Which of the following is a disadvantage of multiband antennas?

## Slide 61
It must be longer than 1 wavelength
Station equipment may carry significant RF current
It produces only vertically polarized radiation
It is more effective on the lower HF bands than on the higher bands
G9B01
What is a characteristic of a random-wire HF antenna connected directly to the transmitter?

## Slide 62
Reduce the SWR in the feed line to the antenna
Reduce the power dissipation in the feedline to the antenna
Increase power transfer from the transmitter to the feed line
All these choices are correct
G4A06
What is the purpose of an antenna tuner?

## Slide 63
G9B08 How does the feed point impeadance of a ½ wave dipole change as the feed point is moved from the center toward the ends?
Gain in dBi is 2.15 dB lower
Gain in dBi is 2.15 dB higher
Gain in dBd is 1.25 dBd lower
Gain in dBd is 1.25 dBd higher
G9C04
How does antenna gain in dBi compare to gain stated in dBd for the same antenna?

## Slide 64
In the plane of the loop
Broadside to the loop
Broadside and in the plane of the loop
Electrically small loops are omnidirectional
G9D10
In which direction or directions does an electrically small loop (less than 1/10 wavelength in circumference) have nulls in its radiation pattern?

## Slide 65
Element length and spacing vary logarithmically along the boom
Impedance varies periodically as a function of frequency
Gain varies logarithmically as a function of frequency
SWR varies periodically as a function of boom length
G9D07
Which of the following describes a log-periodic antenna?

## Slide 66
Wide bandwidth
Higher gain per element than a Yagi antenna
Harmonic suppression
Polarization diversity
G9D06
Which of the following is an advantage of a log-periodic antenna?

## Slide 67
Directional receiving for MF and low HF bands
Directional transmitting for low HF bands
Portable direction finding at higher HF frequencies
Portable direction finding at lower HF frequencies
G9D09
What is the primary use of a Beverage antenna?

## Slide 68
“Picket fencing”
The wire gauge of the DC power line to the transceiver
Efficiency of the electrically short antenna
FCC rules limiting mobile output power on the 75-meter band
G4E05
Which of the following most limits an HF mobile installation?

## Slide 69
Short antennas are more likely to cause distortion of transmitted signals
Q of the antenna will be very low
Operating bandwidth may be very limited
Harmonic radiation may increase
G4E06
What is one disadvantage of using a shortened mobile antenna as opposed to a full-size antenna?

## Slide 70
By varying its body capacitance
By varying the base loading inductance
By extending and retracting the whip
By deploying a capacitance hat
G9D08
How does a “screwdriver” mobile antenna adjust its feed point impedance?

## Slide 71
To increase the power handling capacity of a whip antenna
To reduce radiation resistance
To electrically lengthen a physically short antenna
To lower the radiation angle
G4E01
What is the purpose of a capacitance hat on a mobile antenna?

## Slide 72
To narrow the operating bandwidth of the antenna
To increase the “Q” of the antenna
To reduce the chance of damage if the antenna should strike an object
To reduce RF voltage discharge from the tip of the antenna while transmitting
G4E02
What is the purpose of a corona ball on an HF mobile antenna?

## Slide 73
Standing wave ratio
Antenna front-to-back ratio
RF interference
Radio wave propagation
G4B10
Which of the following can be determined with a directional wattmeter?

## Slide 74
Receiver
Transmitter
Antenna and feed line
All these choices are correct
G4B11
Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?

## Slide 75
Front-to-back ratio of an antenna
Power output from a transmitter
Impedance of coaxial cable
Gain of a directional antenna
G4B13
Which of the following can be measured with an antenna analyzer?

## Slide 76
Desensitization which can cause intermodulation products which interfere with impedance readings
Received power that interferes with SWR readings
Generation of harmonics which interfere with frequency readings
All these choices are correct
G4B12
What effect can strong signals from nearby transmitters have on an antenna analyzer?

## Slide 77: Thank You!