## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: Chapter 17
Coax Cable​
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 6: Coax Cable
50 and 75 ohms are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations. (G9A02)
The attenuation of coaxial cable increases as the frequency of the signal it is carrying increases. (G9A05)
RF feed line losses usually expressed in decibels per 100 ft. (G9A06)

## Slide 7
Coax Cable
Coax Cable
Notes: 7

## Slide 8: Coax Cable
The percentage of power loss that would result from a transmission line loss of 1 dB would be approx. 20.5 percent. (G5B10)
The distance between the centers of the conductors and the radius of the conductors determine the characteristic impedance of a parallel conductor antenna feed line. (G9A01)
450 ohms is the characteristic impedance of “window line” parallel transmission line. (G9A03)
450 Ohm Window line
Air Dielectric Coaxial Cable
Parallel two-wire line

## Slide 9: Coax Cable
To prevent standing waves (SWR) on an antenna feed line, the antenna feed-point impedance must be matched to the characteristic impedance of the feed line. (G9A07)
  Typically an antenna tuner is used to help the matching.
Standing wave ratio can also be determined with a directional wattmeter. (G4B10)
Dual needle.
Bird 43 Watt Meter
Slug for Bird Watt Meter
Single needle.
Daiwa CN-801
Kenwood SW-2000

## Slide 10: Coax Cable
A difference between feed-line impedance and antenna feed-point impedance is the reason for the occurrence of reflected power at the point where a feed line connects to an antenna. (G9A04)
A ferrite bead or core reduces common-mode RF current on the shield of a coaxial cable by creating an impedance in the current path. (G6B10)

## Slide 11: Coax Cable
A standing wave ratio of 1:1 will result from the connection of a 50-ohm feed line to a non-reactive load having a 50-ohm impedance. (G9A11)
SWR = Z1 / Z2
50 / 50
1 : 1 VSWR

## Slide 12: Coax Cable
There is an interaction between high (SWR) and transmission line loss in that if the transmission line is lossy, having high SWR will increase the loss. (G9A12)
If SWR is measured at the input to the line, with higher transmission line loss, the more the SWR will read artificially low. (G9A13)
  SWR will always be lower at the input end of a lossy transmission line.
  If possible, SWR should be measured at the antenna.
  If the transmission line is lossy, the reflected power will be attenuated, just like the forward power.
A common way to adjust the feed point impedance of a quarter wave ground-plan vertical to approximately 50 ohms is to slope the radials downward. (G9B02)

## Slide 13: Coax Cable
Connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance will result in a SWR of 4:1. (G9A09) 200/50=4 which creates a mismatch of 4:1.
Connecting a 50 ohm feed line to a non-reactive load having 10 ohm impedance results in a 5:1 SWR mismatch. (G9A10) 50/10=5 which creates a mismatch of 5:1.
Forward and reflected cross in the ‘less than 2.0’ area which is good.
Red arcs where forward and reflected needles cross show SWR.
Forward and reflected cross near infinite area which is BAD.
SWR is determined only by the load impedance. (The impedance your transmitter sees.)

## Slide 14: Coax Cable
The SWR on an antenna feed line is 5 to 1. The matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR. The resulting SWR on the feed line is 5 to 1. (G9A08)
    SWR is determined by the load impedance.
An ‘N’ connector is a moisture-resistant RF connector useful to 10 GHz. (G6B07)
BNC Connector
PL-259 Connector
N Connector
SMA Connector
F Connector

## Slide 15: Coax Cable
The SMA connectors are small threaded connectors suitable for signals up to several GHz. (G6B11)
PL-259 connectors are commonly used for RF connections at frequencies up to 150 MHz. (G6B13)

## Slide 16: Element 3 General Class Question Pool
Coax Cable
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 17: Thank You!

## Slide 18
Attenuation is independent of frequency
Attenuation increases
Attenuation decreases
Attenuation follows Marconi’s Law of Attenuation
G9A05
How does the attenuation of coaxial cable change with increasing frequency?

## Slide 19
Ohms per 1,000 feet
Decibels per 1,000 feet
Ohms per 100 feet
Decibels per 100 feet
G9A06
In what units is RF feed line loss usually expressed?

## Slide 20
10.9 percent
12.2 percent
20.6 percent
25.9 percent
G5B10
What percentage of power loss is equivalent to a loss of 1 dB?

## Slide 21
The distance between the centers of the conductors and the radius of the conductors
The distance between the centers of the conductors and the length of the line
The radius of the conductors and the frequency of the signal
The frequency of the signal and the length of the line
G9A01
Which of the following factors determine the characteristic impedance of a parallel conductor feed line?

## Slide 22
50 ohms
75 ohms
100 ohms
450 ohms
G9A03
What is the nominal characteristic impedance of “window line” transmission line?

## Slide 23
The antenna feed point must be at DC ground potential
The feed line must be an odd number of electrical quarter wavelengths long
The feed line must be an even number of physical half wavelengths long
The antenna feed point impedance must be matched to the characteristic impedance of the feed line
G9A07
What must be done to prevent standing waves on a feed line connected to an antenna?

## Slide 24
A moisture-resistant RF connector useful to 10 GHz
A small bayonet connector used for data circuits
A low noise figure VHF connector
A nickel plated version of the PL-259
G6B07
Which of the following describes a type N connector?

## Slide 25
Operating an antenna at its resonant frequency
Using more transmitter power than the antenna can handle
A difference between feed line impedance and antenna feed point impedance
Feeding the antenna with unbalanced feed line
G9A04
What causes reflected power at an antenna’s feed point?

## Slide 26
By creating an impedance in the current’s path
It converts common-mode current to differential mode current
By creating an out-of-phase current to cancel the common-mode current
Ferrites expel magnetic fields
G6B10
How does a ferrite bead or core reduce common-mode RF current on the shield of a coaxial cable?

## Slide 27
There is no relationship between transmission line loss and SWR
High SWR increases loss in a lossy transmission line
High SWR makes it difficult to measure transmission line loss
High SWR reduces the relative effect of transmission line loss
G9A02
What is the relationship between high standing wave ratio (SWR) and transmission line loss?

## Slide 28
Higher loss reduces SWR measured at the input to the line
Higher loss increases SWR measured at the input to the line
Higher loss increases the accuracy of SWR measured at the input to the line
Transmission line loss does not affect the SWR measurement
G9A11
What is the effect of transmission line loss on SWR measured at the input to the line?

## Slide 29
Slope the radials upward
Slope the radials downward
Lengthen the radials beyond one wavelength
Coil the radials
G9B02
Which of the following is a common way to adjust the feed point impedance of an elevated quarter-wave ground-plane vertical antenna to be approximately 50 ohms?

## Slide 30
4:1
1:4
2:1
1:2
G9A09
What standing wave ratio results from connecting a 50-ohm feed line to a 200-ohm resistive load?

## Slide 31
2:1
1:2
1:5
5:1
G9A10
What standing wave ratio results from connecting a 50-ohm feed line to a 10-ohm resistive load?

## Slide 32
1:1
5:1
Between 1:1 and 5:1 depending on the characteristic impedance of the line
Between 1:1 and 5:1 depending on the reflected power at the transmitter
G9A08
If the SWR on an antenna feed line is 5:1, and a matching network at the transmitter end of the feed line is adjusted to present a 1:1 SWR to the transmitter, what is the resulting SWR on the feed line?

## Slide 33
A type-S to type-M adaptor
A small threaded connector suitable for signals up to several GHz
A connector designed for serial multiple access signals
A type of push-on connector intended for high-voltage applications
G6B11
What is an SMA connector?

## Slide 34
50 MHz
500 MHz
4 GHz
40 GHz
G6B04
What is a typical upper frequency limit for low SWR operation of 50-ohm BNC connectors?