## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: Chapter 18
RF & Electrical Safety
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 6: RF & Electrical Safety
Turn off the transmitter and disconnect the feed line whenever you make adjustments or repairs to an antenna. (G0B14)
Any person preparing to climb a tower that supports electrically powered devices should make sure all circuits that supply power to the tower are locked out and tagged. (G0B08)
One of the practices that should be observed for safety when climbing on a tower using a safety belt or harness is to always attach the belt safety hook to the belt D-ring with the hook opening away from the tower. (G0B07)
Always disconnect the feedline from the transmitter before going up a tower to work on antenna…prevents accidental RF radiation exposure.

## Slide 7: RF & Electrical Safety
An amateur operator must perform a routine RF exposure evaluation to ensure compliance with RF safety regulations when transmitter power exceeds levels specified in FCC Part 97.13. (G0A08)
If you install an indoor transmitting antenna, make sure that MPE limits are not exceeded in occupied areas. (G0A11)
    MPE = Maximum Permissible Exposure
One way that RF energy can affect human body tissue is that it heats body tissue. (G0A01)
Never stand in front of a microwave feedhorn antenna
On transmit, it radiates a highly concentrated beam of RF energy

## Slide 8: RF & Electrical Safety
You can determine that your station complies with FCC RF exposure regulations: (G0A03)
    By calculation based on FCC OET Bulletin 65.
    By calculation based on computer modeling.
    By measurement of field strength using calibrated equipment.
"Time averaging" in reference to RF radiation exposure means the total RF exposure averaged over a certain time. (G0A04)
The general equation for time averaging exposure equivalence is:
Sexp texp = Slimit tavg
All of these choices are correct.

## Slide 9: RF & Electrical Safety
When evaluating RF exposure, a lower transmitter duty cycle permits greater short-term exposure levels. (G0A07)
The following properties are important in estimating whether an RF signal exceeds the maximum permissible exposure (MPE) (G0A02)
      Its duty cycle
      Its frequency
      Its power density
Duty Cycle
All of these choices are correct.

## Slide 10: RF & Electrical Safety
If an evaluation of your station shows RF energy radiated from your station exceeds permissible limits you must take action to prevent human exposure to the excessive RF fields. (G0A05)
A calibrated field-strength meter with a calibrated antenna can be used to accurately measure an RF field. (G0A09)
Jerrod Model 704B
Homebrew by KA7OEI of Utah Amateur Radio Club
Patomac FIM-71
WiNRADiO WR-G33WSM

## Slide 11: RF & Electrical Safety
When installing a ground-mounted antenna, it should be installed so no one can be exposed to RF radiation in excess of maximum permissible limits. (G0A06)
If an evaluation shows that a neighbor might receive more than the allowable limit of RF exposure from the main lobe of a directional antenna, take precautions to ensure that the antenna cannot be pointed in their direction. (G0A10)
Notice wood safety fence.
Keep a safe distance away from antenna during all transmissions.

## Slide 12: RF & Electrical Safety
Electrical safety inside the ham shack is covered by the National Electrical Code. (G0B06)
RF exposure limits to the human body are covered by ANSI, not by the NEC.

## Slide 13: RF & Electrical Safety
Current flowing from one or more of the hot wires directly to ground will cause a Ground Fault Circuit Interrupter (GFCI) to disconnect the 120 or 240 Volt AC line power to a device. (G0B05)

## Slide 14: RF & Electrical Safety

## Slide 15: RF & Electrical Safety
Bonding all equipment enclosures together helps to minimize RF “hot spots” in an amateur ham radio station. (G4C11)
    RF bonding an be very effective even if a true earth ground is not available.
    Grounding ensures that hazardous voltages cannot appear on the chassis.
    Bonding and grounding are actually two different but related disciplines.
Only the wires carrying voltage in a four-conductor line cord should be attached to fuses or circuit breakers in a device operated from a 240-VAC single-phase source. (G0B01)

## Slide 16: RF & Electrical Safety
15 amperes is the size of fuse or circuit breaker that would be appropriate to use with a circuit that uses AWG number 14 wiring. (G0B03)
According to the code, AWG number 12 is the minimum wire size that may be safely used for a circuit that draws up to
20 amperes of continuous current. (G0B02)
  Thick or thin insulation can be misleading about the actual wire size! Strip off insulation from unmarked wire to determine which gauge wire you have.

## Slide 17: RF & Electrical Safety
The purpose of a transmitter power supply interlock is to ensure that dangerous voltages are removed if the cabinet is opened. (G0B12)
One danger from lead-tin solder is that lead can contaminate food if hands are not washed carefully after handling. (G0B10)

## Slide 18: RF & Electrical Safety
Good engineering practice for lightning protection grounds includes bonding them together with all other grounds. (G0B11)
Soldered joints should not be used with the wires that connect the base of a tower to a system of ground rods because a soldered joint will likely be destroyed by the heat of a lightning strike. (G4C07)
Notice green cable as common ground under floor and connected to building column.
Notice wide copper straps

## Slide 19: RF & Electrical Safety
Danger of carbon monoxide poisoning is a primary reason for not placing a gasoline-fueled generator inside an occupied area. (G0B04)
Carbon Monoxide is serious stuff, don’t take it lightly!

## Slide 20: RF & Electrical Safety
When powering your house from an emergency generator, you must disconnect the incoming utility power feed. (G0B13)
For an emergency generator installation, the generator should be located in a well ventilated area. (G0B09)
    Gasoline-powered generators may emit exhaust gases that could be hazardous.
    Portable generators must be placed well away from an operating position.
    They must have good ventilation, and never be operated with a container of gasoline nearby.

## Slide 21
Notify the electric company that a person will be working on the tower
Make sure all circuits that supply power to the tower are locked out and tagged
Unground the base of the tower
All these choices are correct
G0B08
What should be done before climbing a tower that supports electrically powered devices?

## Slide 22
Always hold on to the tower with one hand
Confirm that the harness is rated for the weight of the climber and that it is within its allowable service life
Ensure that all heavy tools are securely fastened to the harness
All these choices are correct
G0B07
Which of these choices should be observed when climbing a tower using a safety harness?

## Slide 23
Post a copy of FCC Part 97.13 in the station
Notify neighbors within a 100-foot radius of the antenna of the existence of the station and power levels
Perform a routine RF exposure evaluation and prevent access to any identified high exposure areas
All these choices are correct
G0A08
Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations?

## Slide 24
Locate the antenna close to your operating position to minimize feed-line radiation
Position the antenna along the edge of a wall to reduce parasitic radiation
Make sure that MPE limits are not exceeded in occupied areas
Make sure the antenna is properly shielded
G0A11
What precaution should be taken if you install an indoor transmitting antenna?

## Slide 25
It heats body tissue
It causes radiation poisoning
It causes the blood count to reach a dangerously low level
It cools body tissue
G0A01
What is one way that RF energy can affect human body tissue?

## Slide 26
All commercial stations; amateur radio stations are exempt
Only stations with antennas lower than one wavelength above the ground
Only stations transmitting more than 500 watts PEP
All stations with a time-averaged transmission of more than one milliwatt
G0A12
What stations are subject to the FCC rules on RF exposure?

## Slide 27
By calculation based on FCC OET Bulletin 65
By calculation based on computer modeling
By measurement of field strength using calibrated equipment
All these choices are correct
G0A03
How can you determine that your station complies with FCC RF exposure regulations?

## Slide 28
Perform an RF Exposure Evaluation in accordance with FCC OET Bulletin 65
Contact the FCC for permission to transmit
Perform an RF exposure evaluation in accordance with World Meteorological Organization guidelines
Use an FCC-approved band-pass filter
G0A06
What must you do if your station fails to meet the FCC RF exposure exemption criteria?

## Slide 29
The average amount of power developed by the transmitter over a specific 24-hour period
The average time it takes RF radiation to have any long-term effect on the body
The total time of the exposure
The total RF exposure averaged over a certain period
G0A04
What does “time averaging” mean when evaluating RF radiation exposure?

## Slide 30
A lower duty cycle permits greater power levels to be transmitted
A higher duty cycle permits greater power levels to be transmitted
Low duty cycle transmitters are exempt from RF exposure evaluation requirements
High duty cycle transmitters are exempt from RF exposure requirements
G0A07
What is the effect of modulation duty cycle on RF exposure?

## Slide 31
Its duty cycle
Its frequency
Its power density
All these choices are correct
G0A02
Which of the following is used to determine RF exposure from a transmitted signal?

## Slide 32
Take action to prevent human exposure to the excessive RF fields
File an Environmental Impact Statement (EIS-97) with the FCC
Secure written permission from your neighbors to operate above the controlled MPE limits
All these choices are correct
G0A05
What must you do if an evaluation of your station shows that the RF energy radiated by your station exceeds permissible limits for possible human absorption?

## Slide 33
A receiver with digital signal processing (DSP) noise reduction
A calibrated field strength meter with a calibrated antenna
An SWR meter with a peak-reading function
An oscilloscope with a high-stability crystal marker generator
G0A09
What type of instrument can be used to accurately measure an RF field strength?

## Slide 34
Change to a non-polarized antenna with higher gain
Use an antenna with a higher front-to-back ratio
Take precautions to ensure that the antenna cannot be pointed in their direction when they are present
All these choices are correct
G0A10
What should be done if evaluation shows that a neighbor might experience more than the allowable limit of RF exposure from the main lobe of a directional antenna?

## Slide 35
Acceptable bandwidth limits
Acceptable modulation limits
Electrical safety of the station
RF exposure limits of the human body
G0B06
Which of the following is covered by the National Electrical Code?

## Slide 36
Current flowing from one or more of the hot wires to the neutral wire
Current flowing from one or more of the hot wires directly to ground
Overvoltage on the hot wires
All these choices are correct
G0B05
Which of the following conditions will cause a ground fault circuit interrupter (GFCI) to disconnect AC power?

## Slide 37
Building all equipment in a metal enclosure
Using surge suppressor power outlets
Bonding all equipment enclosures together
Placing low-pass filters on all feed lines
G4C11
What technique helps to minimize RF “hot spots” in an amateur station?

## Slide 38
Only the hot wires
Only the neutral wire
Only the ground wire
All wires
G0B01
Which wire or wires in a four-conductor 240 VAC circuit should be attached to fuses or circuit breakers?

## Slide 39
30 amperes
25 amperes
20 amperes
15 amperes
G0B03
Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring?

## Slide 40
AWG number 20
AWG number 16
AWG number 12
AWG number 8
G0B02
According to the National Electrical Code, what is the minimum wire size that may be used safely for wiring with a 20-ampere circuit breaker?

## Slide 41
To prevent unauthorized changes to the circuit that would void the manufacturer’s warranty
To shut down the unit if it becomes too hot
To ensure that dangerous voltages are removed if the cabinet is opened
To shut off the power supply if too much voltage is produced
G0B12
What is the purpose of a power supply interlock?

## Slide 42
Lead can contaminate food if hands are not washed carefully after handling the solder
High voltages can cause lead-tin solder to disintegrate suddenly
Tin in the solder can “cold flow,” causing shorts in the circuit
RF energy can convert the lead into a poisonous gas
G0B10
Which of the following is a danger from lead-tin solder?

## Slide 43
They must be bonded to all buried water and gas lines
Bends in ground wires must be made as close as possible to a right angle
Lightning grounds must be connected to all ungrounded wiring
They must be bonded together with all other grounds
G0B11
Which of the following is required for lightning protection ground rods?

## Slide 44
As close to the station equipment as possible
Outside the building
Next to the closest power pole
Parallel to the water supply line
G0B04
Where should the station’s lightning protection ground system be located?

## Slide 45
A soldered joint will likely be destroyed by the heat of a lightning strike
Solder flux will prevent a low conductivity connection
Solder has too high a dielectric constant to provide adequate lightning protection
All these choices are correct
G4C07
Why should soldered joints not be used in lightning protection ground connections?

## Slide 46
Where the feed lines enter the building
On the antenna, opposite the feed point
In series with each ground lead
At the closest power pole ground electrode
G0B13
Where should lightning arrestors be located?

## Slide 47
The generator should be operated in a well-ventilated area
The generator must be insulated from ground
Fuel should be stored near the generator for rapid refueling in case of an emergency
All these choices are correct
G0B09
Which of the following is true of an emergency generator installation?

## Slide 48: Element 3 General Class Question Pool
RF & Electrical Safety​
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 49: Thank You!

## Slide 51
The generator should be operated in a well-ventilated area
The generator must be insulated from ground
Fuel should be stored near the generator for rapid refueling in case of an emergency
All these choices are correct
G0B09
Which of the following is true of an emergency generator installation?

## Slide 52
Where the feed lines enter the building
On the antenna, opposite the feed point
In series with each ground lead
At the closest power pole ground electrode
G0B13
Where should lightning arrestors be located?

## Slide 53
8 feet.
16 feet.
24 feet.
33 feet.
G9B10
What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz?

## Slide 54
G9B11 What is the approximate length for a 1/2-wave dipole antenna cut for 3.550 MHz?
42 feet.
84 feet.
132 feet.
263 feet.
G9B11
What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz?

## Slide 55
G9B09 Which of the following is an advantage of a horizontally polarized as compared to vertically polarized HF antenna?
8 feet
11 feet
16 feet
21 feet
G9B12
What is the approximate length for a 1/4 wave monopole antenna cut for 28.5 MHz?

## Slide 56
G3C10 What is Near Vertical Incidence Skywave (NVIS) propagation ?
Larger-diameter elements
Closer element spacing
Loading coils in series with the element
Tapered-diameter elements
G9C01
Which of the following would increase the bandwidth of a Yagi antenna?

## Slide 57
G9D01 Which of the following antenna types will be most effective as a Near Vertical Incidence Skywave (NVIS) antenna for short- skip communications on 40 meters during the day ?
1/4 wavelength
1/2 wavelength
3/4 wavelength
1 wavelength
G9C02
What is the approximate length of the driven element of a Yagi antenna?

## Slide 58
G9B07 How does the feed-point impedance of a ½ wave dipole antenna change as the antenna is lowered below ¼ wave above ground ?
The reflector is longer, and the director is shorter
The reflector is shorter, and the director is longer
They are all the same length
Relative length depends on the frequency of operation
G9C03
How do the lengths of a three-element Yagi reflector and director compare to that of the driven element?

## Slide 59
G9B08 How does the feed point impeadance of a ½ wave dipole change as the feed point is moved from the center toward the ends?
Gain in dBi is 2.15 dB lower
Gain in dBi is 2.15 dB higher
Gain in dBd is 1.25 dBd lower
Gain in dBd is 1.25 dBd higher
G9C04
How does antenna gain in dBi compare to gain stated in dBd for the same antenna?

## Slide 60
G9D12 What is the common name of a dipole with a single central support?
Gain increases
Beamwidth increases
Front-to-back ratio decreases
Resonant frequency is lower
G9C05
What is the primary effect of increasing boom length and adding directors to a Yagi antenna?

## Slide 61
G9D02 What is the feed-point impedance of a end-fed half wave antenna ?
The number of directors versus the number of reflectors
The relative position of the driven element with respect to the reflectors and directors
The power radiated in the major lobe compared to that in the opposite direction
The ratio of forward gain to dipole gain
G9C07
What does “front-to-back ratio” mean in reference to a Yagi antenna?

## Slide 62
G9B04 What is the radition pattern of a dipole antenna is free space in a plane containing the conductor ?
The magnitude of the maximum vertical angle of radiation
The point of maximum current in a radiating antenna element
The maximum voltage standing wave point on a radiating element
The direction of maximum radiated field strength from the antenna
G9C08
What is meant by the “main lobe” of a directive antenna?

## Slide 63
G9D03 In which direction is the maximum radiation from a portable VHF/UHF “halo” antenna?
Approximately 1.5 dB higher
Approximately 3 dB higher
Approximately 6 dB higher
Approximately 9 dB higher
G9C09
In free space, how does the gain of two three-element, horizontally polarized Yagi antennas spaced vertically 1/2 wavelength apart typically compare to the gain of a single three-element Yagi?

## Slide 64
G9B05 How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna?
The physical length of the boom
The number of elements on the boom
The spacing of each element along the boom
All these choices are correct
G9C10
Which of the following can be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth of a Yagi antenna?

## Slide 65
G9B03 Which of the following best describes the radiation pattern of a quarter-wave ground plane vertical antenna?
A shorted transmission line stub placed at the feed point of a Yagi antenna to provide impedance matching
A 1/4 wavelength section of 75-ohm coax in series with the feed point of a Yagi to provide impedance matching
A series capacitor selected to cancel the inductive reactance of a folded dipole antenna
A section of 300-ohm twin-lead transmission line used to match a folded dipole antenna
G9C11
What is a beta or hairpin match?

## Slide 66
G9B12 What is the approximate length for a ¼ wave vertical antenna cut for 28.5 MHZ?
It does not require the driven element to be insulated from the boom
It does not require any inductors or capacitors
It is useful for matching multiband antennas
All these choices are correct
G9C12
Which of the following is a characteristic of using a gamma match with a Yagi antenna?

## Slide 67
A horizontal dipole placed between 1/10 and 1/4 wavelength above the ground
A vertical antenna placed between 1/4 and 1/2 wavelength above the ground
A horizontal dipole placed at approximately 1/2 wavelength above the ground
A vertical dipole placed at approximately 1/2 wavelength above the ground
G9D01
Which of the following antenna types will be most effective as a near vertical incidence skywave (NVIS) antenna for short-skip communications on 40 meters during the day?

## Slide 68
Very low
Approximately 50 ohms
Approximately 300 ohms
Very high
G9D02
What is the feed point impedance of an end-fed half-wave antenna?

## Slide 69
Broadside to the plane of the halo
Opposite the feed point
Omnidirectional in the plane of the halo
On the same side as the feed point
G9D03
In which direction is the maximum radiation from a VHF/UHF “halo” antenna?

## Slide 70
To enable multiband operation
To notch spurious frequencies
To provide balanced feed point impedance
To prevent out-of-band operation
G9D04
What is the primary function of antenna traps?

## Slide 71
It allows quick selection of vertical or horizontal polarization
It allows simultaneous vertical and horizontal polarization
It narrows the main lobe in azimuth
It narrows the main lobe in elevation
G9D05
What is an advantage of vertically stacking horizontally polarized Yagi antennas?

## Slide 72
Wide bandwidth
Higher gain per element than a Yagi antenna
Harmonic suppression
Polarization diversity
G9D06
Which of the following is an advantage of a log-periodic antenna?

## Slide 73
Element length and spacing vary logarithmically along the boom
Impedance varies periodically as a function of frequency
Gain varies logarithmically as a function of frequency
SWR varies periodically as a function of boom length
G9D07
Which of the following describes a log-periodic antenna?

## Slide 74
By varying its body capacitance
By varying the base loading inductance
By extending and retracting the whip
By deploying a capacitance hat
G9D08
How does a “screwdriver” mobile antenna adjust its feed point impedance?

## Slide 75
Directional receiving for MF and low HF bands
Directional transmitting for low HF bands
Portable direction finding at higher HF frequencies
Portable direction finding at lower HF frequencies
G9D09
What is the primary use of a Beverage antenna?

## Slide 76
In the plane of the loop
Broadside to the loop
Broadside and in the plane of the loop
Electrically small loops are omnidirectional
G9D10
In which direction or directions does an electrically small loop (less than 1/10 wavelength in circumference) have nulls in its radiation pattern?

## Slide 77
They present low impedance on all design frequencies
They must be used with an antenna tuner
They must be fed with open wire line
They have poor harmonic rejection
G9D11
Which of the following is a disadvantage of multiband antennas?

## Slide 78
Inverted V
Inverted L
Sloper
Lazy H
G9D12
What is the common name of a dipole with a single central support?

## Slide 79
It heats body tissue
It causes radiation poisoning
It causes the blood count to reach a dangerously low level
It cools body tissue
G0A01
What is one way that RF energy can affect human body tissue?

## Slide 80
Its duty cycle
Its frequency
Its power density
All these choices are correct
G0A02
Which of the following is used to determine RF exposure from a transmitted signal?

## Slide 81
By calculation based on FCC OET Bulletin 65
By calculation based on computer modeling
By measurement of field strength using calibrated equipment
All these choices are correct
G0A03
How can you determine that your station complies with FCC RF exposure regulations?

## Slide 82
The average amount of power developed by the transmitter over a specific 24-hour period
The average time it takes RF radiation to have any long-term effect on the body
The total time of the exposure
The total RF exposure averaged over a certain period
G0A04
What does “time averaging” mean when evaluating RF radiation exposure?

## Slide 83
Take action to prevent human exposure to the excessive RF fields
File an Environmental Impact Statement (EIS-97) with the FCC
Secure written permission from your neighbors to operate above the controlled MPE limits
All these choices are correct
G0A05
What must you do if an evaluation of your station shows that the RF energy radiated by your station exceeds permissible limits for possible human absorption?

## Slide 84
Perform an RF Exposure Evaluation in accordance with FCC OET Bulletin 65
Contact the FCC for permission to transmit
Perform an RF exposure evaluation in accordance with World Meteorological Organization guidelines
Use an FCC-approved band-pass filter
G0A06
What must you do if your station fails to meet the FCC RF exposure exemption criteria?

## Slide 85
A lower duty cycle permits greater power levels to be transmitted
A higher duty cycle permits greater power levels to be transmitted
Low duty cycle transmitters are exempt from RF exposure evaluation requirements
High duty cycle transmitters are exempt from RF exposure requirements
G0A07
What is the effect of modulation duty cycle on RF exposure?

## Slide 86
Post a copy of FCC Part 97.13 in the station
Notify neighbors within a 100-foot radius of the antenna of the existence of the station and power levels
Perform a routine RF exposure evaluation and prevent access to any identified high exposure areas
All these choices are correct
G0A08
Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations?

## Slide 87
A receiver with digital signal processing (DSP) noise reduction
A calibrated field strength meter with a calibrated antenna
An SWR meter with a peak-reading function
An oscilloscope with a high-stability crystal marker generator
G0A09
What type of instrument can be used to accurately measure an RF field strength?

## Slide 88
Change to a non-polarized antenna with higher gain
Use an antenna with a higher front-to-back ratio
Take precautions to ensure that the antenna cannot be pointed in their direction when they are present
All these choices are correct
G0A10
What should be done if evaluation shows that a neighbor might experience more than the allowable limit of RF exposure from the main lobe of a directional antenna?

## Slide 89
Locate the antenna close to your operating position to minimize feed-line radiation
Position the antenna along the edge of a wall to reduce parasitic radiation
Make sure that MPE limits are not exceeded in occupied areas
Make sure the antenna is properly shielded
G0A11
What precaution should be taken if you install an indoor transmitting antenna?

## Slide 90
All commercial stations; amateur radio stations are exempt
Only stations with antennas lower than one wavelength above the ground
Only stations transmitting more than 500 watts PEP
All stations with a time-averaged transmission of more than one milliwatt
G0A12
What stations are subject to the FCC rules on RF exposure?

## Slide 91
Only the hot wires
Only the neutral wire
Only the ground wire
All wires
G0B01
Which wire or wires in a four-conductor 240 VAC circuit should be attached to fuses or circuit breakers?

## Slide 92
AWG number 20
AWG number 16
AWG number 12
AWG number 8
G0B02
According to the National Electrical Code, what is the minimum wire size that may be used safely for wiring with a 20-ampere circuit breaker?

## Slide 93
30 amperes
25 amperes
20 amperes
15 amperes
G0B03
Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring?

## Slide 94
As close to the station equipment as possible
Outside the building
Next to the closest power pole
Parallel to the water supply line
G0B04
Where should the station’s lightning protection ground system be located?

## Slide 95
Current flowing from one or more of the hot wires to the neutral wire
Current flowing from one or more of the hot wires directly to ground
Overvoltage on the hot wires
All these choices are correct
G0B05
Which of the following conditions will cause a ground fault circuit interrupter (GFCI) to disconnect AC power?

## Slide 96
Acceptable bandwidth limits
Acceptable modulation limits
Electrical safety of the station
RF exposure limits of the human body
G0B06
Which of the following is covered by the National Electrical Code?

## Slide 97
Always hold on to the tower with one hand
Confirm that the harness is rated for the weight of the climber and that it is within its allowable service life
Ensure that all heavy tools are securely fastened to the harness
All these choices are correct
G0B07
Which of these choices should be observed when climbing a tower using a safety harness?

## Slide 98
Notify the electric company that a person will be working on the tower
Make sure all circuits that supply power to the tower are locked out and tagged
Unground the base of the tower
All these choices are correct
G0B08
What should be done before climbing a tower that supports electrically powered devices?

## Slide 99
Lead can contaminate food if hands are not washed carefully after handling the solder
High voltages can cause lead-tin solder to disintegrate suddenly
Tin in the solder can “cold flow,” causing shorts in the circuit
RF energy can convert the lead into a poisonous gas
G0B10
Which of the following is a danger from lead-tin solder?

## Slide 100
They must be bonded to all buried water and gas lines
Bends in ground wires must be made as close as possible to a right angle
Lightning grounds must be connected to all ungrounded wiring
They must be bonded together with all other grounds
G0B11
Which of the following is required for lightning protection ground rods?

## Slide 101
To prevent unauthorized changes to the circuit that would void the manufacturer’s warranty
To shut down the unit if it becomes too hot
To ensure that dangerous voltages are removed if the cabinet is opened
To shut off the power supply if too much voltage is produced
G0B12
What is the purpose of a power supply interlock?

## Slide 102
X
Q
Q