## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: Chapter 9
Skywave Excitement
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 6: Skywave Excitement
The F2 region is mainly responsible for the longest distance radio wave propagation because it is the highest ionospheric region. (G3C03)

## Slide 7: Skywave Excitement Layers of the Atomsphere

## Slide 8: Skywave Excitement Atmospheric Layers
Ionosphere
31 – 400 miles
Stratosphere
6 – 31 miles
Troposphere
0 – 6 miles
Terms we’ve heard before from space shuttle launches.
Now apply them to Ham Radio

## Slide 9: Skywave Excitement Regions in the Ionosphere
The “D” Region is closest to Earth.
The “D” Region absorbs MF/HF radio signals.
The “F2” Region is most responsible for long distance communication.
The “D” & “E” Regions disappear.
The “F1” & “F2” Regions combine into one with reduced ionization.
During the day....
At night....

## Slide 10: Skywave Excitement
2,500 miles is the approximate maximum distance along the Earth's surface that is normally covered in one hop using the F2 region. (G3B09)
Where the Sun is overhead, ionospheric layers reach their maximum height. (G3C02)
Some radio waves can reflect off the ionosphere (about 100-200 miles up) and travel hundreds of miles.
The ionosphere is what makes long-distance radio communications possible on the shortwave bands.

## Slide 11: Skywave Excitement
The highest takeoff angle that will return a radio wave to the Earth under specific ionospheric conditions is called the critical angle. (G3C04)
One factor that affects how well the ionosphere will reflect a signal is the angle at which the signal impinges upon it.
If the angle is too high, it will pass right through the ionosphere and not be reflected back to earth.

## Slide 12: Skywave Excitement
MUF stand for the Maximum Usable Frequency for communications between two points. (G3B08)
      The highest frequency that will be returned to earth for a given angle of incidence.
LUF stands for the Lowest Usable Frequency for communications between two points. (G3B07)
When they are sent into the ionosphere, radio waves with frequencies below the Lowest Usable Frequency (LUF) are completely absorbed by the ionosphere. (G3B06)
No HF radio frequency will support ordinary skywave communications over the path when the Lowest Usable Frequency (LUF) exceeds the Maximum Usable Frequency (MUF). (G3B11)

## Slide 13: Skywave Excitement
When they are sent into the ionosphere, radio waves with frequencies below the Maximum Usable Frequency (MUF) and above the Lowest Usable Frequency (LUF) are bent back to the Earth. (G3B05)
Notice frequencies change depending on the time of day.

## Slide 14: Skywave Excitement
A reliable way to determine if the Maximum Usable Frequency (MUF) is high enough to support skip propagation between your station and a distant location on frequencies between 14 and 30 MHz is to listen for signals from an international beacon. (G3B04)
Beacon stations: 14.100 MHz, 18.110 MHz, 21.150 MHz, 24.930 MHz, 28.200-28.300 MHz.

## Slide 15: Skywave Excitement
WSPR stands for "Weak Signal Propagation Reporter". It is a digital mode used as a low-power beacon for assessing HF propagation. (G8C02)
It is a protocol, implemented in a computer program.
That is used for weak-signal radio communication.
Between amateur radio operators.
When selecting a frequency for lowest attenuation when transmitting on HF, select a frequency just below the MUF. (G3B03)
Factors that affect the MUF: (G3B02)
    Path distance and location.
    Time of day and season.
    Solar radiation and ionospheric disturbances.
        All of these choices are correct.

## Slide 16: Skywave Excitement
The approximate maximum distance along the Earth’s surface that is normally covered in one hop using the E region (layer) is 1,200 Miles. (G3B10)
Notice that the F Layer signal goes about twice the distance as the E Layer.
~2500 Miles
~1200 Miles

## Slide 17: Skywave Excitement
The D Layer is the ionospheric layer closest to the surface of the Earth. (G3C01)
Daytime/Nighttime HF Propagation
Day
HF Band (meters)
Night
160, 80,60
Local and regional to 100 - 200 miles
Local to long distance with DX best near sunset or sunrise at one or both ends of the contact
40, 30
Local and regional to 300 - 400 miles
Short-range (20 or 30 miles) and medium distances (150 miles) to worldwide
20, 17
Regional to long distance, opening at or near sunrise and closing at night
20 meters is often open to the west at night and may be open 24 hours a day
15, 12, 10
Primarily long distance (1000 miles and more), opening to the east after sunrise and to the west in the afternoon
10 meters is often used for local communications 24 hours a day
Altitudes in Miles of Ionospheric Layers

## Slide 18: Skywave Excitement
The D layer is the ionospheric layer that is the most absorbent of long skip signals during daylight hours on frequencies below 10 MHz. (G3C11)
Long distance communications on the 40-meter, 60-meter, 80-meter, and 160-meter bands are more difficult during the day due to the D layer absorbing these signals daylight hours. (G3C05)
High levels of atmospheric noise or “static” are typical on lower HF bands in the summer. (G2D11)
E Layer
F Layer
D Layer
D Layer
E Layer
F Layer

## Slide 19: Skywave Excitement
One interesting propagation phenomenon is scatter propagation. Scatter propagation allows a signal to be detected at a distance too far for ground wave propagation but too near for normal sky-wave propagation. (G3C09)
HF scatter signals in the skip zone are usually weak because only a small part of the signal energy is scattered into the skip zone. (G3C08)
Scatter propagation

## Slide 20: Skywave Excitement
HF scatter signals often sound distorted because energy is scattered into the skip zone through several different radio wave paths. (G3C07)
A characteristic of HF scatter signals is that they have a wavering or fluttering sound. (G3C06)
Scatter propagation
Normal Skip
Signals fade in and out.

## Slide 21: Skywave Excitement
To figure where to point a directional antenna you’d use an azimuthal projection map. An azimuthal projection map is a world map projection centered on a particular location. (G2D04)
While signals most often take the shortest path from point to point, sometimes the best path for radio propagation is in the opposite direction, also called the “long path.” A slightly delayed echo might be heard if a sky-wave signal arrives at your receiver by both short path and long path propagation. (G3B01)
Centered on Dallas, Texas

## Slide 22: Skywave Excitement
Most communications take place on the “short path,” that is the most direct path between two stations. At times, however, propagation may favor the long path. A directional antenna is pointed 180 degrees from its short-path heading when making a “long-path” contact with another station. (G2D06)
The significance of the sunspot number with regards to HF propagation is that the higher sunspot numbers generally indicate a greater probability of good propagation at higher frequencies. (G3A01)
The sunspot cycle is a long-term phenomenon. There are other phenomena that affect radio wave propagation in the short term. For example, the Sun’s rotation on its axis causes HF propagation conditions to vary periodically in a 28-day cycle. (G3A10)
Solar flares and sunspots affect radiowave propagation

## Slide 23: Skywave Excitement
A possible benefit to radio communications resulting from periods of high geomagnetic activity is that the aurora that can reflect VHF signals. (G3A09)
The least reliable for long-distance communications during periods of low solar activity are 15 meters, 12 meters, and 10 meters. (G3A04)

## Slide 24: Skywave Excitement
The solar-flux index is a measure of solar radiation at 10.7 cm. (G3A05)
        10.7 cm wavelength = 2.80 GHz or 2800 Mhz
There are two indices that give an indication of the stability of the Earth’s magnetic field. The K-index indicates the short term stability of the Earth’s magnetic field. (G3A12)

## Slide 25: Skywave Excitement
The A-index indicates the long term stability of the Earth’s geomagnetic field. (G3A13)

## Slide 26: Skywave Excitement
8 minutes is approximately how long it takes for the increased ultraviolet and X-ray radiation from solar flares to affect radio-wave propagation on the Earth. (G3A03)
Geomagnetic activity, such as a geomagnetic storm, can also affect radio propagation. A geomagnetic storm is a temporary disturbance in the Earth's magnetosphere. (G3A06)

## Slide 27: Skywave Excitement
The effect a Sudden Ionospheric Disturbance has on the daytime ionospheric propagation of HF radio waves is that it disrupts signals on lower frequencies more than those on higher frequencies. (G3A02)
A Sudden Ionic Disturbance (SID) is a phenomenon that can have a drastic effect on propagation.
During an SID, the sun emits a great deal of ultraviolet and X-ray radiation.

## Slide 28: Skywave Excitement
One of the effects a geomagnetic storm can have on radio-wave propagation is degraded high-latitude HF propagation. (G3A08)
It takes 20 to 40 hours for charged particles from Coronal Mass Ejections (CME) to affect radio-wave propagation on the Earth. (G3A11)
Coronal Mass Ejections take 20 – 40 hours to reach the earth where ultraviolet and X-Ray radiation from solar flares take 8 minutes.
A coronal mass ejection (CME) is a massive burst of solar wind and magnetic fields rising above the solar corona or being released into space.

## Slide 29: Skywave Excitement
One of the effects a geomagnetic storm can have on radio-wave propagation is degraded high-latitude HF propagation. (G3A14)
At any point in the solar cycle, the 20 meter band usually supports worldwide propagation during daylight hours. (G3A07)

## Slide 30: Element 3 General Class Question Pool
Skywave Excitement
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 31: G3C03 Why is skip propagation via the F2 region longer than that via the other ionospheric regions?
Because it is the densest ionospheric layer.
Because it does not absorb radio waves as much as other ionospheric regions.
Because it is the highest ionospheric region.
All of these choices are correct.

## Slide 32: G3B09 What is the approximate maximum distance along the Earth’s surface normally covered in one hop using the F2 region?
180 miles.
1,200 miles.
2,500 miles.
12,000 miles.

## Slide 33: G3C04 What does the term “critical angle” mean, as applied to radio wave propagation?
The long path azimuth of a distant station.
The short path azimuth of a distant station.
The lowest takeoff angle that will return a radio wave to Earth under specific ionospheric conditions.
The highest takeoff angle that will return a radio wave to Earth under specific ionospheric conditions.

## Slide 34: G3C02 What is meant by the term “critical frequency” at a given incidence angle?
The highest frequency which is refracted back to Earth
The lowest frequency which is refracted back to Earth
The frequency at which the signal-to-noise ratio approaches unity
The frequency at which the signal-to-noise ratio is 6 dB

## Slide 35: G3B08 What does MUF stand for?
The Minimum Usable Frequency for communications between two points.
The Maximum Usable Frequency for communications between two points.
The Minimum Usable Frequency during a 24-hour period.
The Maximum Usable Frequency during a 24-hour period.

## Slide 36: G3B07 What does LUF stand for?
The Lowest Usable Frequency for communications between two specific points
Lowest Usable Frequency for communications to any point outside a 100-mile radius
The Lowest Usable Frequency during a 24-hour period
Lowest Usable Frequency during the past 60 minutes

## Slide 37: G3B06 What usually happens to radio waves with frequencies below the LUF?
They are refracted back to Earth
They pass through the ionosphere
They are attenuated before reaching the destination
They are refracted and trapped in the ionosphere to circle Earth

## Slide 38: G3B11 What happens to HF propagation when the LUF exceeds the MUF?
Propagation via ordinary skywave communications is not possible over that path
HF communications over the path are enhanced
Double-hop propagation along the path is more common
Propagation over the path on all HF frequencies is enhanced

## Slide 39: G3B05 How does the ionosphere affect radio waves with frequencies below the MUF and above the LUF?
They are refracted back to Earth
They pass through the ionosphere
They are amplified by interaction with the ionosphere
They are refracted and trapped in the ionosphere to circle Earth

## Slide 40: G3B02 What factors affect the (MUF)?
Path distance and location.
Time of day and season.
Solar radiation and ionospheric disturbance.
All of these choices are correct.

## Slide 41: G3B04 Which of the following is a way to determine current propagation on a desired band from your station?
Use a network of automated receiving stations on the internet to see where your transmissions are being received
Check the A-index
Send a series of dots and listen for echoes
All these choices are correct

## Slide 42: G8C02 Which digital mode is used as a low-power beacon for assessing HF propagation?
WSPR
MFSK16
PSK31
SSB-SC

## Slide 43: G3B03 Which frequency will have the least attenuation for long-distance skip propagation?
Just below the MUF
Just above the LUF
Just below the critical frequency
Just above the critical frequency

## Slide 44: G3B10 What is the approximate maximum distance along the Earth's surface that is normally covered in one hop using the E region?
180 miles.
1,200 miles.
2,500 miles.
12,000 miles.

## Slide 45: G3C01 Which ionospheric region is closest to the surface of Earth?
The D region
The E region
The F1 region
The F2 region

## Slide 46: G3C11 Which ionospheric region is the most absorbent of signals below 10 MHz during daylight hours?
The F2 layer.
The F1 layer.
The E layer.
The D layer.

## Slide 47: G3C05 Why is long distance communication on the 40-meter, 60-meter, 80-meter and 160 meter bands more difficult during the day?
The F layer absorbs these frequencies during daylight hours.
The F layer is unstable during daylight hours.
The D layer absorbs these frequencies during daylight hours.
The E layer is unstable during daylight hours.

## Slide 48: G3B12 Which of the following is typical of the lower HF frequencies during the summer?
Poor propagation at any time of day.
World-wide propagation during the daylight hours.
Heavy distortion on signals due to photon absorption.
High levels of atmospheric noise or “static”.

## Slide 49: G3C09 What type of propagation allows signals to be heard in the transmitting station’s skip zone?
Faraday rotation.
Scatter.
Chordal hop.
Short-path.

## Slide 50: G3C08 Why are HF scatter signals in the skip zone usually weak?
Only a small part of the signal energy is scattered into the skip zone.
Signals are scattered from the magnetosphere which is not a good reflector.
Propagation is through ground waves which absorb most of the signal energy.
Propagations is through ducts in F region which absorb most of the energy.

## Slide 51: G3C07 What makes HF scatter signals often sound distorted?
The ionospheric layer involved is unstable.
Ground waves are absorbing much of the signal.
The E-region is not present.
Energy is scattered into the skip zone through several different radio wave paths.

## Slide 52: G3C06 What is a characteristic of HF scatter signals?
Phone signals have high intelligibility.
Signals have a fluttering sound.
There are very large, sudden swings in signal strength.
Scatter propagation occurs only at night.

## Slide 53: G2D04 Which of the following describes an azimuthal projection map?
A map that shows accurate land masses
A map that shows true bearings and distances from a specific location
A map that shows the angle at which an amateur satellite crosses the equator
A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit

## Slide 54: G3B01 What is a characteristic of skywave signals arriving at your location by both short-path and long-path propagation?
Periodic fading approximately every 10 seconds
Signal strength increased by 3 dB
The signal might be cancelled causing severe attenuation
A slightly delayed echo might be heard

## Slide 55: G2D06 How is a directional antenna pointed when making a “long-path” contact with another station?
Toward the rising sun.
Along the Gray Line.
180 degrees from its short-path heading.
Toward the North.

## Slide 56: G3A01 How does a higher sunspot number affect HF propagation?
Higher sunspot numbers generally indicate a greater probability of good propagation at higher frequencies
Lower sunspot numbers generally indicate greater probability of sporadic E propagation
A zero sunspot number indicates that radio propagation is not possible on any band
A zero sunspot number indicates undisturbed conditions

## Slide 57: G3A10 What causes HF propagation conditions to vary periodically in a roughly 28-day cycle?
Long term oscillations in the upper atmosphere
Cyclic variation in Earth’s radiation belts
Rotation of the Sun’s surface layers around its axis
The position of the Moon in its orbit

## Slide 58: G3A09 How can high geomagnetic activity benefit radio communications?
Creates auroras that can reflect VHF signals
Increases signal strength for HF signals passing through the polar regions
Improve HF long path propagation
Reduce long delayed echoes

## Slide 59: G3A04 Which of the following are least reliable for long-distance communications during periods of low solar activity?
80 meters and 160 meters.
60 meters and 40 meters.
30 meters and 20 meters.
15 meters, 12 meters, and 10 meters.

## Slide 60: G3A05 What is the solar-flux index?
A measure of the highest frequency that is useful for ionospheric propagation between two points on the Earth.
A count of sunspots which is adjusted for solar emissions.
Another name for the American sunspot number.
A measure of solar radiation at 10.7 centimeters wavelength.

## Slide 61: G3A12 What is the K-index?
The relative position of sunspots on the surface of the Sun
The short-term stability of Earth’s geomagnetic field
The short-term stability of the Sun’s magnetic field
The solar radio flux at Boulder, Colorado

## Slide 62: G3A13 What is the A-index?
The relative position of sunspots on the surface of the Sun
The amount of polarization of the Sun’s electric field
The long-term stability of Earth’s geomagnetic field
The solar radio flux at Boulder, Colorado

## Slide 63: G3A03 Approximately how long does it take the increased ultraviolet and X-ray radiation from a solar flare to affect radio propagation on Earth?
28 days.
1 to 2 hours.
8 minutes.
20 to 40 hours.

## Slide 64: G3A06 What is a geomagnetic storm?
A sudden drop in the solar-flux index.
A thunderstorm that affects radio propagation.
Ripples in the ionosphere.
A temporary disturbance in the Earth's magnetosphere.

## Slide 65: G3A02 What effect does a Sudden Ionospheric Disturbance have on the daytime ionospheric propagation of HF radio waves?
It enhances propagation on all HF frequencies.
It disrupts signals on lower frequencies more than those on higher frequencies.
It disrupts communications via satellite more than direct communications.
None, because only areas on the night side of the Earth are affected.

## Slide 66: G3A08 Which of the following effects can a geomagnetic storm have on radio propagation?
Improved high-latitude HF propagation.
Degraded high-latitude HF propagation.
Improved ground wave propagation.
Degraded ground wave propagation.

## Slide 67: G3A11 How long does it take a coronal mass ejection to affect radio propagation on Earth?
28 days.
14 days.
4 to 8 minutes.
20 to 40 hours.

## Slide 68: G3A14 How is long distance radio communication usually affected by the charged particles that reach Earth from solar coronal holes?
HF communications are improved.
HF communications are disturbed.
VHF/UHF ducting is improved.
VHF/UHF ducting is disturbed.

## Slide 69: G3A07 At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours?
At the summer solstice
Only at the maximum point
Only at the minimum point
At any point

## Slide 70: Thank You!