What must be considered to determine the minimum current capacity needed for a transceiver power supply?
A. Efficiency of the transmitter at full power output
B. Receiver and control circuit power
C. Power supply regulation and heat dissipation
D. All of these choices are correct
 T4A01 HRLM (5 - 16)

---
What must be considered to determine the minimum current capacity needed for a transceiver power supply?
A. Efficiency of the transmitter at full power output
B. Receiver and control circuit power
C. Power supply regulation and heat dissipation
D. All of these choices are correct
(D) T4A01 HRLM (5 - 16)

---
How might a computer be used as part of an amateur radio station?
A. For logging contacts and contact information
B. For sending and/or receiving CW
C. For generating and decoding digital signals
D. All of these choices are correct
 T4A02 HRLM (5 - 11)

---
How might a computer be used as part of an amateur radio station?
A. For logging contacts and contact information
B. For sending and/or receiving CW
C. For generating and decoding digital signals
D. All of these choices are correct
(D) T4A02 HRLM (5 - 11)

---
Why should wiring between the power source and radio be heavy-gauge wire and kept as short as possible?
A. To avoid voltage falling below that needed for proper operation
B. To provide a good counterpoise for the antenna
C. To avoid RF interference
D. All of these choices are correct
 T4A03 HRLM (5 - 17)

---
Why should wiring between the power source and radio be heavy-gauge wire and kept as short as possible?
A. To avoid voltage falling below that needed for proper operation
B. To provide a good counterpoise for the antenna
C. To avoid RF interference
D. All of these choices are correct
(A) T4A03 HRLM (5 - 17)
A 20-ft. run of 14-gauge wire from the radio to the battery or power source (Total of 40ft. of
wire for both positive and negative leads) would have a resistance of .05 ohms. With a current
of 20 amperes for a mobile HF Rig this would amount to a 2.02-volt voltage drop. With a 12-
volt power source the radio would only see 9.98 volts from the 12-volt source.

---
Which computer sound card port is connected to a transceiver’s headphone or speaker output for operating digital modes?
A. Headphone output
B. Mute
C. Microphone or line input
D. PCI or SDI
 T4A04 HRLM (5 - 15)

---
Which computer sound card port is connected to a transceiver’s headphone or speaker output for operating digital modes?
A. Headphone output
B. Mute
C. Microphone or line input
D. PCI or SDI
(C) T4A04 HRLM (5 - 15)
So you can TRANSMIT:
Computer sound ----→ the transceiver microphone input
So you can RECEIVE:
Radio audio signals ----→ computer mic input

---
What is the proper location for an external SWR meter?
What is the proper location for an external SWR meter?
A. In series with the feed line, between the transmitter and antenna
B. In series with the station's ground
C. In parallel with the push-to-talk line and the antenna
D. In series with the power supply cable, as close as possible to the radio
 T4A05 HRLM (4 - 18)

---
What is the proper location for an external SWR meter?
What is the proper location for an external SWR meter?
A. In series with the feed line, between the transmitter and antenna
B. In series with the station's ground
C. In parallel with the push-to-talk line and the antenna
D. In series with the power supply cable, as close as possible to the radio
(A) T4A05 HRLM (4 – 18)
    SHOW IT TO THEM…..

---
Which of the following connections might be used between a voice transceiver and a computer for digital operation?
A. Receive and transmit mode, status, and location
B. Antenna and RF power
C. Receive audio, transmit audio, and push-to-talk (PTT)
D. NMEA GPS location and DC power
 T4A06 HRLM (5 - 15)

---
Which of the following connections might be used between a voice transceiver and a computer for digital operation?
A. Receive and transmit mode, status, and location
B. Antenna and RF power
C. Receive audio, transmit audio, and push-to-talk (PTT)
D. NMEA GPS location and DC power
(C) T4A06 HRLM (5 – 15)
SHOW IT TO THEM---

---
How is a computer’s sound card used when conducting digital communications?
A. The sound card communicates between the computer CPU and the video display
B. The sound card records the audio frequency for video display
C. The sound card provides audio to the radio's microphone input and converts received audio to digital form
D. All of these choices are correct
 T4A07 HRLM (5 - 15)

---
How is a computer’s sound card used when conducting digital communications?
A. The sound card communicates between the computer CPU and the video display
B. The sound card records the audio frequency for video display
C. The sound card provides audio to the radio's microphone input and converts received audio to digital form
D. All of these choices are correct
(C) T4A07 HRLM (5 – 15) DEMONSTRATE FLDIGI IF you HAVENT ALREADY

---
Which of the following conductors provides the lowest impedance to RF signals?
A. Round stranded wire
B. Round copper-clad steel wire
C. Twisted-pair cable
D. Flat strap
 T4A08 HRLM (9 - 7)

---
Which of the following conductors provides the lowest impedance to RF signals?
A. Round stranded wire
B. Round copper-clad steel wire
C. Twisted-pair cable
D. Flat strap
(D) T4A08 HRLM (9 – 7) LOWEST INDUCTANCE. INDUCTANCE MEANS THE VOLTAGE AT ONE POINT ONTHE GROUND WIRE….ISN’T THE SAME AS ON ANOTHER POINT…..RADIO FREQUENCY IS MUCH DIFFERENT FROM DC.

---
Which of the following could you use to cure distorted audio caused by RF current on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke
 T4A09 HRLM (9 - 8)

---
Which of the following could you use to cure distorted audio caused by RF current on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke
(D) T4A09 HRLM (9 – 8) SHOW FERRITE BEAD.

---
What is the source of a high-pitched whine that varies with engine speed in a mobile transceiver’s receive audio?
A. The ignition system
B. The alternator
C. The electric fuel pump
D. Anti-lock braking system controllers
 T4A10 HRLM (5 - 17)

---
What is the source of a high-pitched whine that varies with engine speed in a mobile transceiver’s receive audio?
A. The ignition system
B. The alternator
C. The electric fuel pump
D. Anti-lock braking system controllers
(B) T4A10 HRLM (5 - 17)

---
Where should the negative return connection of a mobile transceiver's power cable be connected?
A. At the battery or engine block ground strap
B. At the antenna mount
C. To any metal part of the vehicle
D. Through the transceiver’s mounting bracket
 T4A11 HRLM (5 - 17)

---
Where should the negative return connection of a mobile transceiver's power cable be connected?
A. At the battery or engine block ground strap
B. At the antenna mount
C. To any metal part of the vehicle
D. Through the transceiver’s mounting bracket
(A) T4A11 HRLM (5 - 17)

---
What may happen if a transmitter is operated with the microphone gain set too high?
A. The output power might be too high
B. The output signal might become distorted
C. The frequency might vary
D. The SWR might increase
 T4B01 HRLM (5 - 8)

---
What may happen if a transmitter is operated with the microphone gain set too high?
A. The output power might be too high
B. The output signal might become distorted
C. The frequency might vary
D. The SWR might increase
(B) T4B01 HRLM (5 – 8) DRAW SPLATTER!!

---
Which of the following can be used to enter the operating frequency on a modern transceiver?
A. The keypad or VFO knob
B. The CTCSS or DTMF encoder
C. The Automatic Frequency Control
D. All of these choices are correct
 T4B02 HRLM (5 - 6)

---
Which of the following can be used to enter the operating frequency on a modern transceiver?
A. The keypad or VFO knob
B. The CTCSS or DTMF encoder
C. The Automatic Frequency Control
D. All of these choices are correct
(A) T4B02 HRLM (5 - 6)

---
What is the purpose of the squelch control on a transceiver?_clipboard0
What is the purpose of the squelch control on a transceiver?
A. To set the highest level of volume desired
B. To set the transmitter power level
C. To adjust the automatic gain control
D. To mute receiver output noise when no signal is being received
 T4B03 HRLM (5 - 9)

---
What is the purpose of the squelch control on a transceiver?
What is the purpose of the squelch control on a transceiver?
A. To set the highest level of volume desired
B. To set the transmitter power level
C. To adjust the automatic gain control
D. To mute receiver output noise when no signal is being received
(D) T4B03 HRLM (5 – 9) DEMONSTRATE

---
What is a way to enable quick access to a favorite frequency on your transceiver?
A. Enable the CTCSS tones
B. Store the frequency in a memory channel
C. Disable the CTCSS tones
D. Use the scan mode to select the desired frequency
 T4B04 HRLM (5 - 7)

---
What is a way to enable quick access to a favorite frequency on your transceiver?
A. Enable the CTCSS tones
B. Store the frequency in a memory channel
C. Disable the CTCSS tones
D. Use the scan mode to select the desired frequency
(B) T4B04 HRLM (5 - 7)

---
Which of the following would reduce ignition interference to a receiver?
A. Change frequency slightly
B. Decrease the squelch setting
C. Turn on the noise blanker
D. Use the RIT control
 T4B05 HRLM (5 - 10)

---
Which of the following would reduce ignition interference to a receiver?
A. Change frequency slightly
B. Decrease the squelch setting
C. Turn on the noise blanker
D. Use the RIT control
(C) T4B05 HRLM (5 - 10)

---
Which of the following controls could be used if the voice pitch of a single-sideband signal seems too high or low?
A. The AGC or limiter
B. The bandwidth selection
C. The tone squelch
D. The receiver RIT or clarifier
 T4B06 HRLM (5 - 10)

---
Which of the following controls could be used if the voice pitch of a single-sideband signal seems too high or low?
A. The AGC or limiter
B. The bandwidth selection
C. The tone squelch
D. The receiver RIT or clarifier
(D) T4B06 HRLM (5 – 10) demonstrate!!

---
What does the term “RIT” mean?_clipboard1
What does the term “RIT” mean?
A. Receiver Input Tone
B. Receiver Incremental Tuning
C. Rectifier Inverter Test
D. Remote Input Transmitter
 T4B07 HRLM (5 - 10)

---
What does the term “RIT” mean?
What does the term “RIT” mean?
A. Receiver Input Tone
B. Receiver Incremental Tuning
C. Rectifier Inverter Test
D. Remote Input Transmitter
(B) T4B07 HRLM (5 – 10) DEMONSTRATE

---
What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
A. Permits monitoring several modes at once
B. Permits noise or interference reduction by selecting a bandwidth matching the mode
C. Increases the number of frequencies that can be stored in memory
D. Increases the amount of offset between receive and transmit frequencies
 T4B08 HRLM (5 - 9)

---
What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
A. Permits monitoring several modes at once
B. Permits noise or interference reduction by selecting a bandwidth matching the mode
C. Increases the number of frequencies that can be stored in memory
D. Increases the amount of offset between receive and transmit frequencies
(B) T4B08 HRLM (5 – 9) DRAW IT

---
Which of the following is an appropriate receive filter bandwidth for minimizing noise and interference for SSB reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
 T4B09 HRLM (5 - 9)

---
Which of the following is an appropriate receive filter bandwidth for minimizing noise and interference for SSB reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
(C) T4B09 HRLM (5 – 9) VOICE WILL ALWAYS BE CONSIDERED SOMEWHERE BETWEEN 2KHZ AND 3 KHZ WIDE.

---
Which of the following is an appropriate receive filter bandwidth for minimizing noise and interference for CW reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
 T4B10 HRLM (5 - 9)

---
Which of the following is an appropriate receive filter bandwidth for minimizing noise and interference for CW reception?
A. 500 Hz
B. 1000 Hz
C. 2400 Hz
D. 5000 Hz
(A) T4B10 HRLM (5 – 9) SHOW IT ON FLDIGI

---
What is the function of automatic gain control, or AGC?_clipboard2
What is the function of automatic gain control, or AGC?
A. To keep received audio relatively constant
B. To protect an antenna from lightning
C. To eliminate RF on the station cabling
D. An asymmetric goniometer control used for antenna matching
 T4B11 HRLM (5 - 9)

---
What is the function of automatic gain control, or AGC?
What is the function of automatic gain control, or AGC?
A. To keep received audio relatively constant
B. To protect an antenna from lightning
C. To eliminate RF on the station cabling
D. An asymmetric goniometer control used for antenna matching
(A) T4B11 HRLM (5 – 9) EXPLAIN USING UBITX

---
Which of the following could be used to remove power line noise or ignition noise?
A. Squelch
B. Noise blanker
C. Notch filter
D. All of these choices are correct
 T4B12 HRLM (5 - 10)

---
Which of the following could be used to remove power line noise or ignition noise?
A. Squelch
B. Noise blanker
C. Notch filter
D. All of these choices are correct
(B) T4B12 HRLM (5 - 10)

---
Which of the following is a use for the scanning function of an FM transceiver?
A. To check incoming signal deviation
B. To prevent interference to nearby repeaters
C. To scan through a range of frequencies to check for activity
D. To check for messages left on a digital bulletin board
 T4B13 HRLM (6 - 10)

---
Which of the following is a use for the scanning function of an FM transceiver?
A. To check incoming signal deviation
B. To prevent interference to nearby repeaters
C. To scan through a range of frequencies to check for activity
D. To check for messages left on a digital bulletin board
(C) T4B13 HRLM (6 - 10)