General License Course
Chapter 4
Lesson Plan Module 10 –
Electrical Review

---
Current Voltage and Power
Current = I, the flow of electrons, measured in Amperes (A or Amps) with an ammeter
Voltage = E, the force that makes electrons move, measured in volts (V) with a voltmeter
Power (P) is measured in watts (W) with a wattmeter, P = E x I
[Speaker Notes: Notes area]

---
Resistance & Ohms Law
Resistance (R) is the opposition to current flow measured in Ohms (Ω) with an ohmmeter.
R=E/I, I=E/R, E=I x R, P=I x E, P=I2 x R, P=E2 / R
[Speaker Notes: Notes area]

---
Doing the Math
G5B03 – How many watts of electrical power are used if 400 V dc is supplied to an 800 ohm resister?
P=E2/R
P= (400 x 400) / 800 = 160,000 / 800
160,000 / 800 = 200 watts
[Speaker Notes: Notes area]

---
Doing the Math
G5B04 – How many watts of electrical power are used by a 12 V dc light bulb that draws 0.2 A?
P = E x I
P = 12V x 0.2A = 2.4 watts
[Speaker Notes: Notes area]

---
Doing the Math
G5B05 – How many watts are being dissipated when a current of 7.0 mA flows through a 1.25 kΩ resistor?
P = I2 x R
P = (.007 x .007) x 1250 = 0.06125 W
0.06125 = 61.25 mW
[Speaker Notes: At this point the Lesson Plan provides a list of topics from the Technician exam and which can be covered as a short review. If necessary, revisit the various topics. The slides in the Technician’s Instructor’s Manual can be used as visual aids and teaching guides.]

---
Doing the Math - Decibels
The formula for calculating decibels (dB)
dB = 10 log10 (power ratio) = 20 log10 (voltage ratio)
dB = 10 log10 (PM / PRef) = 20 log10 (VM /VRef)
What is the gain of an amplifier that turns a 5 watt signal into a 25 watt signal?
dB = 10 log10 (25 / 5) = 10 log10 (5) = 10 x (0.7) = 7 dB Calculator key strokes: 5, log, x, 10, = 6.9897 (round up to 7)
[Speaker Notes: Notes area]

---
What in the heck is “log-1”???
INVERSE LOG
LoG

---
Doing the Math - Decibels
Calculating a Power or Voltage Ratio from dB
Power ratio = log-1 (dB/10)
Example 1: A power ratio of 9 dB = ?
log-1 (9/10), log-1 (.9) = 8
Keystrokes: 9 / 10 = .9 [2nd function] log = 7.94328 (round up)
Voltage ratio = log-1 (dB/20)
Example 2: A voltage ratio of 32 dB = ?
log-1 (32/20) = log-1 (1.6) = 40
Keystrokes: 32/20=1.6 [2nd function] log = 39.8107
Round the answer up to 40
[Speaker Notes: Notes area]

---
Doing the Math Decibels
Converting dB to percentage and vice versa:
dB = 10 log (Percentage Power / 100%)
dB = 20 log (Percentage Voltage / 100%)
Percentage Power = 100% x log-1 (dB/10)
Percentage Voltage = 100% x log-1 (dB/20)
[Speaker Notes: Notes area]

---
Doing the Math Decibels
G5B10 - What percentage of power loss would result from a transmission line loss of 1 dB?
Percentage Power = 100% x log-1 (dB/10)
100% x log-1 (-1/10) = 100% x log-1 (-.1) = 79.4%
Keystrokes: 1 [+/-] /10= [2nd function] log x 100 = 79.4328 (round the answer to 79.4%)
Power loss is 100 – 79.4 = 20.6%
Question pool used different rounding to arrive at 20.5%
[Speaker Notes: Notes area]

---
3 dB Rule
G5B01 – Remember that to double or reduce in half is a 3dB change
A 2 times increase in power is ___ dB?
dB = 10 log10 (PM / PRef)
dB = 10 log10 (2 / 1) = 3dB
Keystrokes: 2 / 1 = 2 [log] x 10 = 3.010299
(round answer to 3dB)
[Speaker Notes: Notes area]

---
Practice Questions
Practice Questions

---
What dB change represents a two-times increase or decrease in power?
A. Approximately 2 dB
B. Approximately 3 dB
C. Approximately 6 dB
D. Approximately 12 dB
G5B01

---
What dB change represents a two-times increase or decrease in power?
A. Approximately 2 dB
B. Approximately 3 dB
C. Approximately 6 dB
D. Approximately 12 dB
 G5B01

---
How many watts of electrical power are used if 400 VDC is supplied to an 800 ohm load?
A. 0.5 watts
B. 200 watts
C. 400 watts
D. 3200 watts
 G5B03

---
How many watts of electrical power are used if 400 VDC is supplied to an 800 ohm load?
A. 0.5 watts
B. 200 watts
C. 400 watts
D. 3200 watts
 G5B03

---
How many watts of electrical power are used by a 12 VDC light bulb that draws 0.2 amperes?
A. 2.4 watts
B. 24 watts
C. 6 watts
D. 60 watts
 G5B04

---
How many watts of electrical power are used by a 12 VDC light bulb that draws 0.2 amperes?
A. 2.4 watts
B. 24 watts
C. 6 watts
D. 60 watts
 G5B04

---
How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms resistance?
A. Approximately 61 milliwatts
B. Approximately 61 watts
C. Approximately 11 milliwatts
D. Approximately 11 watts
 G5B05

---
How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms resistance?
A. Approximately 61 milliwatts
B. Approximately 61 watts
C. Approximately 11 milliwatts
D. Approximately 11 watts
 G5B05

---
What percentage of power loss would result from a transmission line loss of 1 dB?
A. 10.9 percent
B. 12.2 percent
C. 20.5 percent
D. 25.9 percent
 G5B10

---
What percentage of power loss would result from a transmission line loss of 1 dB?
A. 10.9 percent
B. 12.2 percent
C. 20.5 percent
D. 25.9 percent
 G5B10

---
General License Course Chapter 4
General License Course
Chapter 4
Lesson Plan Module 11 –
AC Power

---
AC Power
Definition and Measurement
Root Mean Square (VRMS)
The RMS value for an ac voltage is equivalent to the value of a dc voltage that results in the same power dissipation in a resistor
2015 General License Course
[Speaker Notes: Notes area]

---
Definition & Measurement
RMS value is 0.707 times the ac waveform’s peak voltage (VPK)
VRMS = 0.707 x VPK = 0.707 x (VP-P / 2)
VPK = 1.414 x VRMS
VP-P = 2 x 1.414 x VRMS = 2.828 x VRMS
[Speaker Notes: Notes area]

---
Measurements
Relationships between RMS, average, peak-to-peak values
[Speaker Notes: Notes area]

---
Doing the RMS Math
A sine wave with a peak voltage of 17 V has an RMS value of?
VRMS = 0.707 x 17 V = 12 V
A sine wave with a peak-to-peak voltage of 100 V has an RMS value of?
VRMS = 0.707 x (100 / 2) = 35.4 V
A sine wave with an RMS voltage of 120 V has a peak-to-peak voltage of?
VP-P = 2 x 1.414 x 120 = 2.828 x 120 = 339.4 V
[Speaker Notes: Notes area]

---
PEP Definition & Measurement
1500 W PEP (peak envelope power) is full amateur power limit
PEP is the average power of one complete RF cycle at the peak of the signal’s envelope
PEP is an easy way to measure or specify the maximum power of an amplitude modulated signal
PEV (peak envelope voltage) is the voltage at the peak of the signal envelope
[Speaker Notes: Be sure the students understand the difference between: Peak voltage Peak-to-peak voltage Peak envelope voltage]

---
PEP Doing the Math
Example 10:
Keystrokes:
50 x 0.707 = 35.35 [x2] = 1249.6225 / 50 = 24.99245 W
Round the answer to 25 W
[Speaker Notes: Notes area]

---
PEP Doing the Math
Example 11:
Keystrokes:
1200 x 50 = 60,000 [square root symbol] = 244.9489
Round answer to 245 V
[Speaker Notes: Notes area]

---
PEP Doing the Math
Example 13:
Keystrokes:
0.707 x 200 = 141.4 / 2 = 70.7 [x2] / 50 = 99.968
Round answer to 100 W
[Speaker Notes: Notes area]

---
PEP Doing the Math
What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 Ω resistor connected to the transmitter output?
Keystrokes:
0.707 x 500 = 353.5 / 2 = 176.75 [x2] / 50 = 624.81125
Round answer to 625 W
[Speaker Notes: Notes area]

---
PEP & Average Readings
PEP is equal to average power if an amplitude modulated signal is not modulated
An unmodulated AM signal, a key down CW signal, and a FM signal are all constant power modes for which PEP = Average Power.
Single sideband PEP is not equal to average power
If your CW transmitter generates 1060 W average output power, the PEP is also 1060 W
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output?
What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output?
A. 1.4 watts
B. 100 watts
C. 353.5 watts
D. 400 watts
  G5B06

---
What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output?
A. 1.4 watts
B. 100 watts
C. 353.5 watts
D. 400 watts
  G5B06

---
What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value?
What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value?
A. The peak-to-peak value
B. The peak value
C. The RMS value
D. The reciprocal of the RMS value
  G5B07

---
What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value?
A. The peak-to-peak value
B. The peak value
C. The RMS value
D. The reciprocal of the RMS value
  G5B07

---
What is the RMS voltage of a sine wave with a value of 17 volts peak?
What is the RMS voltage of a sine wave with a value of 17 volts peak?
A. 8.5 volts
B. 12 volts
C. 24 volts
D. 34 volts
  G5B09

---
What is the RMS voltage of a sine wave with a value of 17 volts peak?
A. 8.5 volts
B. 12 volts
C. 24 volts
D. 34 volts
  G5B09

---
What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts?
What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts?
A. 173 volts
B. 245 volts
C. 346 volts
D. 692 volts
  G5B12

---
What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts?
A. 173 volts
B. 245 volts
C. 346 volts
D. 692 volts
  G5B12

---
What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts?
What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts?
A. 530 watts
B. 1060 watts
C. 1500 watts
D. 2120 watts
  G5B13

---
What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts?
A. 530 watts
B. 1060 watts
C. 1500 watts
D. 2120 watts
  G5B13

---
What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output?
What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output?
A. 8.75 watts
B. 625 watts
C. 2500 watts
D. 5000 watts
  G5B14

---
What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output?
A. 8.75 watts
B. 625 watts
C. 2500 watts
D. 5000 watts
  G5B14

---
General License Course
Chapter 4
Lesson Plan Module 12 –
Basic Components

---
Resistors & Resistance
Resistors may have the same nominal value but vary in other characteristics
[Speaker Notes: Notes area]

---
Resistors & Resistance
Resistance nominal values
1 to more than 1 M (value or color bands printed on them)
Resistor Tolerance (accuracy)
Precision (1% or less), general purpose (5 or 10%)
Temperature Coefficients (tempco) are change characteristics (positive or negative)
Positive increases in value as temperature goes up
Negative decreases in value as temperature goes down
[Speaker Notes: Temperature Sensors can use thermistors which are resistors with a precisely known temperature coefficient as sensing elements for control systems.]

---
Resistors & Resistance
Parasitic Inductance:
Parasitic – unwanted characteristic resulting from the component’s physical construction (wire-wound resistor on a ceramic form)
Placing a wire-wound resistor in an RF circuit can disrupt operation or tuning
RF circuits normally use carbon composition, carbon film, or metal oxide resistors which have very low inductance
[Speaker Notes: Notes area]

---
Inductors & Inductance
Laminated iron core – dc and ac power and filtering
Powdered iron solenoid – power supplies, RF chokes, audio and low-frequency circuits
Powdered iron & ferrite toroids – audio and radio circuits
Air core – RF
transmitting
[Speaker Notes: Point out the difference in the schematic symbols]

---
Inductors & Inductance
Variable inductors – used in low-power receiving and transmitting applications
Low-power - adjusted by moving a magnetic core in and out of the inductor
High-Power - adjusted by moving a sliding contact along the inductor, like a roller inductor in an antenna matching network
[Speaker Notes: Notes area]

---
Inductors & Inductance
Inductance is the ability to store magnetic energy (measured in henries, H)
Increasing the core permeability will increase the ability to store magnetic energy and thus the inductance
The core material is selected based on its suitability for a range of frequencies
[Speaker Notes: Notes area]

---
Inductors & Inductance
When inductors are placed close together with their axes aligned, the magnetic energy from one inductor passes through the other inductor, sharing some of its energy (coupling or mutual inductance)
[Speaker Notes: Notes area]

---
Inductors & Inductance
Two solenoid inductors should be oriented at right angles to each other to minimize their mutual inductance
Coupling allows signals to be shared between circuits without a direct connection.
Coupling can be undesirable
Toroid inductors with a magnetic core keep nearly all of the magnetic energy in the core so that coupling is minimized.
[Speaker Notes: Notes area]

---
Capacitors & Capacitance
Capacitors have two conducting surfaces (electrodes) separated by a dielectric
Capacitance is the ability to store electric energy, measured in farads, F
Blocks dc current flow
[Speaker Notes: Notes area]

---
Capacitors & Capacitance
The simplest capacitor is a pair of metal plates separated by air
Capacitor types:
Ceramic – RF filtering, bypassing at high frequencies, low cost
Plastic film – audio circuits & lower radio frequencies
Silvered-mica – highly stable, low loss, use in RF circuits
Electrolytic and tantalum – power supply filter circuits
Air and vacuum dielectric – transmitting and RF circuits
[Speaker Notes: Notes area]

---
Capacitors & Capacitance
Aluminum and tantalum electrolytic capacitors
Dielectric is a thin film
Voltage must be applied with the correct polarity
Benefit – Create large capacitances in comparatively small volumes
[Speaker Notes: Notes area]

---
Components in Series & Parallel Circuits
Kirchhoff’s Voltage Law
Kirchhoff’s Current Law
[Speaker Notes: Show how voltages add to zero around a series circuit (KVL) and how currents must balance going into and out of a parallel circuit junction (KCL).]

---
Adding Components in Series and Parallel
[Speaker Notes: Show the different formulas and point out that there are only two: Adding values Reciprocal of Reciprocals Resistors and inductors in series are like a higher value resistor or inductor. Capacitors in parallel are like a capacitor with bigger electrodes and more capacitance.]

---
Doing the Math
[Speaker Notes: Notes area]

---
Doing the Math
Make your calculator do the hard work
Some calculators require a 2nd function key to get to a 2nd set of commands, like using the shift key on your computer’s keyboard
Example 14: Three 100 Ω resistors in parallel?
Keystrokes: 100 [2nd function 1/x] + 100 [2nd function 1/x] + 100 [2nd function 1/x] = .3, [2nd function 1/x] = 33.333333 Ω
[Speaker Notes: Notes area]

---
Doing the Math
Ex. 15: Three 100 F capacitors in series?
Keystrokes: 100 [2nd function 1/x] + 100 [2nd function 1/x] + 100 [2nd function 1/x] =.03, [2nd function 1/x] = 33.33333 F
Ex. 16: Three 10 mH inductors in parallel?
Keystrokes: 10 [2nd function 1/x] + 10 [2nd function 1/x] + 10 [2nd function 1/x] = .3, [2nd function 1/x] 3.33333 mH
Ex. 17: A 20 mH and 50 mH inductor in series?
Keystrokes: 20 + 50 = 70 mH (simple addition)
[Speaker Notes: This is a great opportunity to review the common metric prefixes and symbols that are common to electronic components: Milli Micro Nano Pico Also review how to convert between the various prefixes]

---
Doing the Math
Ex. 18: A 20 F and 50 F capacitor in series?
Keystrokes: 20 [2nd function 1/x] + 50 [2nd function 1/x] = .07, [2nd function 1/x] 14.2857 F (round to 14.29 F)
Ex. 19: A 10  20  and 50  resistor in parallel?
Keystrokes: 10 [2nd function 1/x] + 20 [2nd function 1/x] + 50 [2nd function 1/x] = 0.17, [2nd function 1/x] 5.88235  (round to 5.9 )
[Speaker Notes: Notes area]

---
Doing the Math
Ex. 20: Total capacitance of two 5 nF and one 750 pF in parallel?
(First convert 5nF to pF = 5 x 1000 = 5000 pF)
Keystrokes: 5000 + 5000 + 750 = 10750 pF/1000 = 10.75 nF
Ex. 21: What three equal value resistors can be combined in parallel to equal 50 ?
Problem restated R/3 = 50 , multiply both sides by 3 to put the R by itself. R = 3 x 50 = 150 
Proof: 150 [2nd function 1/x] + 150 [2nd function 1/x] + 150 [2nd function 1/x] = 0.02, [2nd function 1/x] 50 
[Speaker Notes: Notes area]

---
Transformers
Primary Winding – power is applied
Secondary winding – power is extracted
When voltage is applied to the primary winding (EP), mutual inductance causes voltage (ES) to appear across the secondary winding (works in both directions)
The turns ratio of the secondary (NS) to the primary (NP) windings determines how the current and voltage are changed
ES = EP × (NS / NP) and IS = IP × (NP / NS)
[Speaker Notes: Take care to show the inversion of the turns ratio when calculating secondary voltage or current.]

---
Transformers
Transformers
- A significant change between primary and secondary voltage usually requires a change in the size of wire between windings
- In a step-up transformer, the primary winding carries higher current and is wound with larger-diameter wire than the secondary

---
Doing the Transformer Math
Example 22 – Voltage across a 500 turn secondary when 120 V is applied to a 2250 turn primary?
ES = (applied voltage) x (NS/NP)
Keystrokes:
ES = 500/2250 = 0.22222222 x 120 = 26.66666666 V
Answer is rounded to 26.7 V
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit?
How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit?
A. It equals the average of each branch current
B. It decreases as more parallel branches are added to the circuit
C. It equals the sum of the currents through each branch
D. It is the sum of the reciprocal of each individual voltage drop
  G5B02

---
How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit?
A. It equals the average of each branch current
B. It decreases as more parallel branches are added to the circuit
C. It equals the sum of the currents through each branch
D. It is the sum of the reciprocal of each individual voltage drop
  G5B02

---
What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding?
What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding?
A. Capacitive coupling
B. Displacement current coupling
C. Mutual inductance
D. Mutual capacitance
  G5C01

---
What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding?
A. Capacitive coupling
B. Displacement current coupling
C. Mutual inductance
D. Mutual capacitance
  G5C01

---
What happens if you reverse the primary and secondary windings of a 4:1 voltage step down transformer?
What happens if you reverse the primary and secondary windings of a 4:1 voltage step down transformer?
A. The secondary voltage becomes 4 times the primary voltage
B. The transformer no longer functions as it is a unidirectional device
C. Additional resistance must be added in series with the primary to prevent overload
D. Additional resistance must be added in parallel with the secondary to prevent overload
  G5C02

---
What happens if you reverse the primary and secondary windings of a 4:1 voltage step down transformer?
A. The secondary voltage becomes 4 times the primary voltage
B. The transformer no longer functions as it is a unidirectional device
C. Additional resistance must be added in series with the primary to prevent overload
D. Additional resistance must be added in parallel with the secondary to prevent overload
  G5C02

---
Which of the following components should be added to an existing resistor to increase the resistance?
Which of the following components should be added to an existing resistor to increase the resistance?
A. A resistor in parallel
B. A resistor in series
C. A capacitor in series
D. A capacitor in parallel
  G5C03

---
Which of the following components should be added to an existing resistor to increase the resistance?
A. A resistor in parallel
B. A resistor in series
C. A capacitor in series
D. A capacitor in parallel
  G5C03

---
What is the total resistance of three 100 ohm resistors in parallel?
What is the total resistance of three 100 ohm resistors in parallel?
A. 0.30 ohms
B. 0.33 ohms
C. 33.3 ohms
D. 300 ohms
  G5C04

---
What is the total resistance of three 100 ohm resistors in parallel?
A. 0.30 ohms
B. 0.33 ohms
C. 33.3 ohms
D. 300 ohms
  G5C04

---
If three equal value resistors in series produce 450 ohms, what is the value of each resistor?
If three equal value resistors in series produce 450 ohms, what is the value of each resistor?
A. 1500 ohms
B. 90 ohms
C. 150 ohms
D. 175 ohms
  G5C05

---
If three equal value resistors in series produce 450 ohms, what is the value of each resistor?
A. 1500 ohms
B. 90 ohms
C. 150 ohms
D. 175 ohms
  G5C05

---
What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC?
What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC?
A. 2370 volts
B. 540 volts
C. 26.7 volts
D. 5.9 volts
  G5C06

---
What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC?
A. 2370 volts
B. 540 volts
C. 26.7 volts
D. 5.9 volts
  G5C06

---
What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance?
What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance?
A. 12.2 to 1
B. 24.4 to 1
C. 150 to 1
D. 300 to 1
  G5C07

---
What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance?
A. 12.2 to 1
B. 24.4 to 1
C. 150 to 1
D. 300 to 1
  G5C07

---
What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel?
What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel?
A. 576.9 nanofarads
B. 1733 picofarads
C. 3583 picofarads
D. 10.750 nanofarads
  G5C08

---
What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel?
A. 576.9 nanofarads
B. 1733 picofarads
C. 3583 picofarads
D. 10.750 nanofarads
  G5C08

---
What is the capacitance of three 100 microfarad capacitors connected in series?
What is the capacitance of three 100 microfarad capacitors connected in series?
A. 0.30 microfarads
B. 0.33 microfarads
C. 33.3 microfarads
D. 300 microfarads
  G5C09

---
What is the capacitance of three 100 microfarad capacitors connected in series?
A. 0.30 microfarads
B. 0.33 microfarads
C. 33.3 microfarads
D. 300 microfarads
  G5C09

---
What is the inductance of three 10 millihenry inductors connected in parallel?
What is the inductance of three 10 millihenry inductors connected in parallel?
A. 0.30 henrys
B. 3.3 henrys
C. 3.3 millihenrys
D. 30 millihenrys
  G5C10

---
What is the inductance of three 10 millihenry inductors connected in parallel?
A. 0.30 henrys
B. 3.3 henrys
C. 3.3 millihenrys
D. 30 millihenrys
  G5C10

---
What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor?
What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor?
A. 0.07 millihenrys
B. 14.3 millihenrys
C. 70 millihenrys
D. 1000 millihenrys
  G5C11

---
What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor?
A. 0.07 millihenrys
B. 14.3 millihenrys
C. 70 millihenrys
D. 1000 millihenrys
  G5C11

---
What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor?
What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor?
A. 0.07 microfarads
B. 14.3 microfarads
C. 70 microfarads
D. 1000 microfarads
  G5C12

---
What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor?
A. 0.07 microfarads
B. 14.3 microfarads
C. 70 microfarads
D. 1000 microfarads
  G5C12

---
Which of the following components should be added to a capacitor to increase the capacitance?
Which of the following components should be added to a capacitor to increase the capacitance?
A. An inductor in series
B. A resistor in series
C. A capacitor in parallel
D. A capacitor in series
  G5C13

---
Which of the following components should be added to a capacitor to increase the capacitance?
A. An inductor in series
B. A resistor in series
C. A capacitor in parallel
D. A capacitor in series
  G5C13

---
Which of the following components should be added to an inductor to increase the inductance?
Which of the following components should be added to an inductor to increase the inductance?
A. A capacitor in series
B. A resistor in parallel
C. An inductor in parallel
D. An inductor in series
  G5C14

---
Which of the following components should be added to an inductor to increase the inductance?
A. A capacitor in series
B. A resistor in parallel
C. An inductor in parallel
D. An inductor in series
  G5C14

---
What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor connected in parallel?
What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor connected in parallel?
A. 5.9 ohms
B. 0.17 ohms
C. 10000 ohms
D. 80 ohms
  G5C15

---
What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor connected in parallel?
A. 5.9 ohms
B. 0.17 ohms
C. 10000 ohms
D. 80 ohms
  G5C15

---
Why is the conductor of the primary winding of many voltage step up transformers larger in diameter than the conductor of the secondary winding?
Why is the conductor of the primary winding of many voltage step up transformers larger in diameter than the conductor of the secondary winding?
A. To improve the coupling between the primary and secondary
B. To accommodate the higher current of the primary
C. To prevent parasitic oscillations due to resistive losses in the primary
D. To insure that the volume of the primary winding is equal to the volume of the secondary winding
  G5C16

---
Why is the conductor of the primary winding of many voltage step up transformers larger in diameter than the conductor of the secondary winding?
A. To improve the coupling between the primary and secondary
B. To accommodate the higher current of the primary
C. To prevent parasitic oscillations due to resistive losses in the primary
D. To insure that the volume of the primary winding is equal to the volume of the secondary winding
  G5C16

---
What is the value in nanofarads (nF) of a 22,000 pF capacitor?
What is the value in nanofarads (nF) of a 22,000 pF capacitor?
A. 0.22 nF
B. 2.2 nF
C. 22 nF
D. 220 nF
  G5C17

---
What is the value in nanofarads (nF) of a 22,000 pF capacitor?
A. 0.22 nF
B. 2.2 nF
C. 22 nF
D. 220 nF
  G5C17

---
What is the value in microfarads of a 4700 nanofarad (nF) capacitor?
What is the value in microfarads of a 4700 nanofarad (nF) capacitor?
A. 47 uF
B. 0.47 uF
C. 47,000 uF
D. 4.7 uF
  G5C18

---
What is the value in microfarads of a 4700 nanofarad (nF) capacitor?
A. 47 uF
B. 0.47 uF
C. 47,000 uF
D. 4.7 uF
  G5C18

---
Why is the polarity of applied voltages important for polarized capacitors?
Why is the polarity of applied voltages important for polarized capacitors?
A. Incorrect polarity can cause the capacitor to short-circuit
B. Reverse voltages can destroy the dielectric layer of an electrolytic capacitor
C. The capacitor could overheat and explode
D. All of these choices are correct
  G6A13

---
Why is the polarity of applied voltages important for polarized capacitors?
A. Incorrect polarity can cause the capacitor to short-circuit
B. Reverse voltages can destroy the dielectric layer of an electrolytic capacitor
C. The capacitor could overheat and explode
D. All of these choices are correct
  G6A13

---
Which of the following is an advantage of ceramic capacitors as compared to other types of capacitors?
Which of the following is an advantage of ceramic capacitors as compared to other types of capacitors?
A. Tight tolerance
B. High stability
C. High capacitance for given volume
D. Comparatively low cost
  G6A14

---
Which of the following is an advantage of ceramic capacitors as compared to other types of capacitors?
A. Tight tolerance
B. High stability
C. High capacitance for given volume
D. Comparatively low cost
  G6A14

---
Which of the following is an advantage of an electrolytic capacitor?
Which of the following is an advantage of an electrolytic capacitor?
A. Tight tolerance
B. Much less leakage than any other type
C. High capacitance for a given volume
D. Inexpensive RF capacitor
  G6A15

---
Which of the following is an advantage of an electrolytic capacitor?
A. Tight tolerance
B. Much less leakage than any other type
C. High capacitance for a given volume
D. Inexpensive RF capacitor
  G6A15

---
What will happen to the resistance if the temperature of a resistor is increased?
What will happen to the resistance if the temperature of a resistor is increased?
A. It will change depending on the resistor’s reactance coefficient
B. It will stay the same
C. It will change depending on the resistor's temperature coefficient
D. It will become time dependent
  G6A16

---
What will happen to the resistance if the temperature of a resistor is increased?
A. It will change depending on the resistor’s reactance coefficient
B. It will stay the same
C. It will change depending on the resistor's temperature coefficient
D. It will become time dependent
  G6A16

---
Which of the following is a reason not to use wire-wound resistors in an RF circuit?
Which of the following is a reason not to use wire-wound resistors in an RF circuit?
A. The resistor's tolerance value would not be adequate for such a circuit
B. The resistor's inductance could make circuit performance unpredictable
C. The resistor could overheat
D. The resistor's internal capacitance would detune the circuit
  G6A17

---
Which of the following is a reason not to use wire-wound resistors in an RF circuit?
A. The resistor's tolerance value would not be adequate for such a circuit
B. The resistor's inductance could make circuit performance unpredictable
C. The resistor could overheat
D. The resistor's internal capacitance would detune the circuit
  G6A17

---
What is an advantage of using a ferrite core toroidal inductor?
What is an advantage of using a ferrite core toroidal inductor?
A. Large values of inductance may be obtained
B. The magnetic properties of the core may be optimized for a specific range of frequencies
C. Most of the magnetic field is contained in the core
D. All of these choices are correct
  G6A18

---
What is an advantage of using a ferrite core toroidal inductor?
A. Large values of inductance may be obtained
B. The magnetic properties of the core may be optimized for a specific range of frequencies
C. Most of the magnetic field is contained in the core
D. All of these choices are correct
  G6A18

---
How should the winding axes of two solenoid inductors be oriented to minimize their mutual inductance?
How should the winding axes of two solenoid inductors be oriented to minimize their mutual inductance?
A. In line
B. Parallel to each other
C. At right angles to each other
D. Interleaved
  G6A19

---
How should the winding axes of two solenoid inductors be oriented to minimize their mutual inductance?
A. In line
B. Parallel to each other
C. At right angles to each other
D. Interleaved
  G6A19

---
Which symbol in figure G7-1 represents a field effect transistor?
Which symbol in figure G7-1 represents a field effect transistor?
A. Symbol 2
B. Symbol 5
C. Symbol 1
D. Symbol 4
  G7A09

---
Which symbol in figure G7-1 represents a field effect transistor?
A. Symbol 2
B. Symbol 5
C. Symbol 1
D. Symbol 4
  G7A09

---
Which symbol in figure G7-1 represents a Zener diode?
Which symbol in figure G7-1 represents a Zener diode?
A. Symbol 4
B. Symbol 1
C. Symbol 11
D. Symbol 5
  G7A10

---
Which symbol in figure G7-1 represents a Zener diode?
A. Symbol 4
B. Symbol 1
C. Symbol 11
D. Symbol 5
  G7A10

---
Which symbol in figure G7-1 represents an NPN junction transistor?
Which symbol in figure G7-1 represents an NPN junction transistor?
A. Symbol 1
B. Symbol 2
C. Symbol 7
D. Symbol 11
  G7A11

---
Which symbol in figure G7-1 represents an NPN junction transistor?
A. Symbol 1
B. Symbol 2
C. Symbol 7
D. Symbol 11
  G7A11

---
Which symbol in Figure G7-1 represents a multiple-winding transformer?
Which symbol in Figure G7-1 represents a multiple-winding transformer?
A. Symbol 4
B. Symbol 7
C. Symbol 6
D. Symbol 1
  G7A12

---
Which symbol in Figure G7-1 represents a multiple-winding transformer?
A. Symbol 4
B. Symbol 7
C. Symbol 6
D. Symbol 1
  G7A12

---
Which symbol in Figure G7-1 represents a tapped inductor?
Which symbol in Figure G7-1 represents a tapped inductor?
A. Symbol 7
B. Symbol 11
C. Symbol 6
D. Symbol 1
  G7A13

---
Which symbol in Figure G7-1 represents a tapped inductor?
A. Symbol 7
B. Symbol 11
C. Symbol 6
D. Symbol 1
  G7A13

---
General License Course
Chapter 4
Lesson Plan Module 13 –
Reactance and Impedance

---
Reactance
Definition: The resistance to the flow of ac current caused by capacitance or inductance is called reactance and is denoted by X. It is measured in ohms, like resistance.
[Speaker Notes: Notes area]

---
Reactance
Capacitive reactance: The opposition to ac current flow from the stored energy in a capacitor is called capacitive reactance (XC)
As the frequency of the applied signal increases, XC decreases. and vice versa
[Speaker Notes: Notes area]

---
Reactance
Inductive reactance is the opposition to ac current flow from the stored energy in a inductor and is denoted by XL
As the frequency of the applied signal increases, XL increases and visa versa
[Speaker Notes: Note that capacitive and inductive reactance act in a complementary way with respect to frequency.]

---
Impedance
Impedance - opposition to current flow in an ac circuit
Denoted by “Z” and is measured in ohms ()
The ratio of voltage to current
[Speaker Notes: Note that impedance is the sum of resistance and reactance in a circuit]

---
Resonance
Resonance in a circuit or antenna occurs when capacitive and inductive reactance are equal
In a resonant series circuit the reactances of the L and C cancel, forming a short circuit, leaving only the resistance, R, as the circuit’s impedance
Resonance is used in filters or tuned circuits to pass or reject specific frequencies
[Speaker Notes: If anyone asks about the parallel resonant circuit, explain that instead of forming a short circuit, it forms an open circuit.]

---
Impedance Transformation
- A transformer changes the ratio of voltage and current between the primary and secondary circuits and so changes the impedance
- Zp = Zs (Np / Ns)2 and √(Zp / Zs) = Np / Ns
- Example 27: What turns ratio is required to change a 600 Ω impedance to a 4 Ω impedance?
    Keystrokes: 600 / 4 = 150 [sq root] =12.24744871,
    rounded to 12.25 :1
[Speaker Notes: Notes area]

---
Impedance Matching
Maximum power transfer occurs when the source and load impedances are equal
Amateur transmitting equipment is designed to have a 50  output
Most antennas are designed to have a feed point impedance of 50  but rarely present that impedance over the whole band
An impedance-matching circuit changes the variable impedance into the desired value
[Speaker Notes: Notes area]

---
Impedance Matching
Most impedance matching circuits are LC circuits made up of inductors and capacitors
[Speaker Notes: Notes area]

---
Impedance Matching
Special RF impedance-matching transformers are often used to equalize impedances of the source and load to maximize the transfer of power to the load
Special lengths of coax can be used to match impedances
[Speaker Notes: No need to get into the details of transmission line transformers but you can mention stubs, quarter-wave transformers, and so forth.]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is impedance?
What is impedance?
A. The electric charge stored by a capacitor
B. The inverse of resistance
C. The opposition to the flow of current in an AC circuit
D. The force of repulsion between two similar electric fields
  G5A01

---
What is impedance?
A. The electric charge stored by a capacitor
B. The inverse of resistance
C. The opposition to the flow of current in an AC circuit
D. The force of repulsion between two similar electric fields
  G5A01

---
What is reactance?
What is reactance?
A. Opposition to the flow of direct current caused by resistance
B. Opposition to the flow of alternating current caused by capacitance or inductance
C. A property of ideal resistors in AC circuits
D. A large spark produced at switch contacts when an inductor is de-energized
  G5A02

---
What is reactance?
A. Opposition to the flow of direct current caused by resistance
B. Opposition to the flow of alternating current caused by capacitance or inductance
C. A property of ideal resistors in AC circuits
D. A large spark produced at switch contacts when an inductor is de-energized
  G5A02

---
Which of the following causes opposition to the flow of alternating current in an inductor?
Which of the following causes opposition to the flow of alternating current in an inductor?
A. Conductance
B. Reluctance
C. Admittance
D. Reactance
  G5A03

---
Which of the following causes opposition to the flow of alternating current in an inductor?
A. Conductance
B. Reluctance
C. Admittance
D. Reactance
  G5A03

---
Which of the following causes opposition to the flow of alternating current in a capacitor?
Which of the following causes opposition to the flow of alternating current in a capacitor?
A. Conductance
B. Reluctance
C. Reactance
D. Admittance
  G5A04

---
Which of the following causes opposition to the flow of alternating current in a capacitor?
A. Conductance
B. Reluctance
C. Reactance
D. Admittance
  G5A04

---
How does an inductor react to AC?
How does an inductor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the amplitude of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance decreases
D. As the frequency of the applied AC increases, the reactance increases
  G5A05

---
How does an inductor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the amplitude of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance decreases
D. As the frequency of the applied AC increases, the reactance increases
  G5A05

---
How does a capacitor react to AC?
How does a capacitor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the frequency of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance increases
D. As the amplitude of the applied AC increases, the reactance decreases
  G5A06

---
How does a capacitor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
B. As the frequency of the applied AC increases, the reactance increases
C. As the amplitude of the applied AC increases, the reactance increases
D. As the amplitude of the applied AC increases, the reactance decreases
  G5A06

---
What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive?
What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive?
A. The source delivers minimum power to the load
B. The electrical load is shorted
C. No current can flow through the circuit
D. The source can deliver maximum power to the load
  G5A07

---
What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive?
A. The source delivers minimum power to the load
B. The electrical load is shorted
C. No current can flow through the circuit
D. The source can deliver maximum power to the load
  G5A07

---
Why is impedance matching important?
Why is impedance matching important?
A. So the source can deliver maximum power to the load
B. So the load will draw minimum power from the source
C. To ensure that there is less resistance than reactance in the circuit
D. To ensure that the resistance and reactance in the circuit are equal
  G5A08

---
Why is impedance matching important?
A. So the source can deliver maximum power to the load
B. So the load will draw minimum power from the source
C. To ensure that there is less resistance than reactance in the circuit
D. To ensure that the resistance and reactance in the circuit are equal
  G5A08

---
What unit is used to measure reactance?
What unit is used to measure reactance?
A. Farad
B. Ohm
C. Ampere
D. Siemens
  G5A09

---
What unit is used to measure reactance?
A. Farad
B. Ohm
C. Ampere
D. Siemens
  G5A09

---
What unit is used to measure impedance?
What unit is used to measure impedance?
A. Volt
B. Ohm
C. Ampere
D. Watt
  G5A10

---
What unit is used to measure impedance?
A. Volt
B. Ohm
C. Ampere
D. Watt
  G5A10

---
Which of the following describes one method of impedance matching between two AC circuits?
Which of the following describes one method of impedance matching between two AC circuits?
A. Insert an LC network between the two circuits
B. Reduce the power output of the first circuit
C. Increase the power output of the first circuit
D. Insert a circulator between the two circuits
  G5A11

---
Which of the following describes one method of impedance matching between two AC circuits?
A. Insert an LC network between the two circuits
B. Reduce the power output of the first circuit
C. Increase the power output of the first circuit
D. Insert a circulator between the two circuits
  G5A11

---
What is one reason to use an impedance matching transformer?
What is one reason to use an impedance matching transformer?
A. To minimize transmitter power output
B. To maximize the transfer of power
C. To reduce power supply ripple
D. To minimize radiation resistance
  G5A12

---
What is one reason to use an impedance matching transformer?
A. To minimize transmitter power output
B. To maximize the transfer of power
C. To reduce power supply ripple
D. To minimize radiation resistance
  G5A12

---
Which of the following devices can be used for impedance matching at radio frequencies?
Which of the following devices can be used for impedance matching at radio frequencies?
A. A transformer
B. A Pi-network
C. A length of transmission line
D. All of these choices are correct
  G5A13

---
Which of the following devices can be used for impedance matching at radio frequencies?
A. A transformer
B. A Pi-network
C. A length of transmission line
D. All of these choices are correct
  G5A13

---
What is the ratio of peak envelope power to average power for an unmodulated carrier?
What is the ratio of peak envelope power to average power for an unmodulated carrier?
A. 0.707
B. 1.00
C. 1.414
D. 2.00
  G5B11

---
What is the ratio of peak envelope power to average power for an unmodulated carrier?
A. 0.707
B. 1.00
C. 1.414
D. 2.00
  G5B11