General License Course Chapter 5
General License Course
Chapter 5
Lesson Plan Module 17 –
Signals and Equipment

---
Signal Review
Continuous wave (CW) – A radio signal at one frequency whose strength never changes
Modulation – adding information to a signal by changing its frequency, phase angle, or amplitude
Demodulation – recovering the information from a modulated signal
2015 General License Course
[Speaker Notes: Notes area]

---
Signal Review
If speech is the information used to modulate a signal, the result is a voice mode or phone (short for radiotelephone) signal
If data is the information used to modulate a signal, the result is a data mode or digital mode signal
[Speaker Notes: Note that digitally-encoded speech is still considered a voice mode by the FCC rules.]

---
Signal Review
Analog modes carry information, such as speech, that can be understood directly by a human
Digital or data modes carry information as data characters between two computers
[Speaker Notes: Notes area]

---
Amplitude Modulated Modes
Amplitude modulation (AM) is the instantaneous varying of the power or amplitude of a signal by adding speech or data information
The AM signal’s carrier is a continuous wave whose amplitude does not change and contains no information
The AM signal’s envelope follows the modulating signal. The modulating information can be recovered from the envelope by detection
[Speaker Notes: Notes area]

---
Amplitude Modulated Modes
An AM signal is composed of a carrier and two sidebands – one higher than the carrier frequency (upper sideband – USB) and one lower (lower sideband – LSB).
Each sideband contains a copy of the modulating information.
A single sideband (SSB) signal is an AM signal with the carrier and one sideband removed.
[Speaker Notes: The carrier is used when simple detection is used for recovering the modulating signal from the envelope of an AM signal. By using all of the transmitter’s power for the single remaining sideband, signal range is extended. Recovering the modulating information is more complicated, however.]

---
Angle Modulated Modes
Frequency modulation (FM) is a mode that varies the frequency of a signal to add speech or data information
Deviation is the amount that an FM signal’s frequency varies when modulated
Phase modulation (PM) is created by varying a signal’s phase angle
FM and PM have many sidebands but the signals have a constant power
[Speaker Notes: While these signals sound like they might be quite different, note that they are virtually indistinguishable on the air.]

---
Bandwidth Definition
Bandwidth:
The FCC limits signal bandwidth so that many stations and types of signals can share the limited amount of spectrum
Single sideband is the phone emission which uses the narrowest bandwidth
Defined as the range within which the signal is no more than 26 dB (1/400th) below the average signal power.
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is the name of the process that changes the phase angle of an RF wave to convey information?
What is the name of the process that changes the phase angle of an RF wave to convey information?
A. Phase convolution
B. Phase modulation
C. Angle convolution
D. Radian inversion
  G8A02

---
What is the name of the process that changes the phase angle of an RF wave to convey information?
A. Phase convolution
B. Phase modulation
C. Angle convolution
D. Radian inversion
  G8A02

---
What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
A. Frequency convolution
B. Frequency transformation
C. Frequency conversion
D. Frequency modulation
  G8A03

---
What is the name of the process that changes the instantaneous frequency of an RF wave to convey information?
A. Frequency convolution
B. Frequency transformation
C. Frequency conversion
D. Frequency modulation
  G8A03

---
What type of modulation varies the instantaneous power level of the RF signal?
What type of modulation varies the instantaneous power level of the RF signal?
A. Frequency shift keying
B. Phase modulation
C. Frequency modulation
D. Amplitude modulation
  G8A05

---
What type of modulation varies the instantaneous power level of the RF signal?
A. Frequency shift keying
B. Phase modulation
C. Frequency modulation
D. Amplitude modulation
  G8A05

---
Which of the following phone emissions uses the narrowest bandwidth?
Which of the following phone emissions uses the narrowest bandwidth?
A. Single sideband
B. Double sideband
C. Phase modulation
D. Frequency modulation
  G8A07

---
Which of the following phone emissions uses the narrowest bandwidth?
A. Single sideband
B. Double sideband
C. Phase modulation
D. Frequency modulation
  G8A07

---
General License Course Chapter 5
General License Course
Chapter 5
Lesson Plan Module 18 –
Radio’s Building Blocks

---
Oscillators
An oscillator consists of an amplifier that increases signal amplitude (gain) and a feedback circuit to route some of the amplifier’s output signal back to its input
Oscillator circuits must include a filter so that feedback is present at only the intended frequency
The oscillator output frequency can be fixed or variable
[Speaker Notes: Notes area]

---
Oscillators
The filter of an LC oscillator is a resonant circuit made from inductors and capacitors. It sets the oscillator’s frequency
Resonant LC circuits are sometimes called tank circuits because they store energy
The output frequency of a variable-frequency oscillator (VFO) can be adjusted by changing the L or C. VFOs are used to tune a radio to different frequencies
[Speaker Notes: Notes area]

---
Oscillator
Two other widely used VFO circuits:
Phase-locked loop (PLL)
Direct digital synthesizer (DDS)
The DDS has the advantage of being controllable by software and having stability comparable to a crystal oscillator
[Speaker Notes: Explain that PLL and DDS circuits are ways of making a VFO that can be adjusted over a wider frequency than a single oscillator but that still have acceptable stability for use in radio circuits.]

---
Mixers
A mixer circuit combines signals with two frequencies, f1 and f2, and produces signals with the sum and difference frequencies at its output (heterodyning)
Example: If f1 = 14.050 MHz and f2 = 3.35 MHz, the output of the mixer will contain signals at both 10.7 MHz (f1 – f2) and at 17.4 MHz (f1 + f2).
A mixer can change a signal to any other frequency
The input signals are called the RF and LO (Local Oscillator) and the outputs are mixing products

---
Multipliers
Multipliers – create harmonics of an input signal
Multipliers are often used when a stable VHF or UHF signal is required that cannot be generated directly at VHF/UHF
A low-frequency oscillator supplies the multiplier input, and the output is tuned to the desired harmonic of the input signal
[Speaker Notes: Notes area]

---
Modulators
Modulator circuits add information to a carrier signal by varying its amplitude, frequency, or phase
The modulating information can be speech, data, or images
[Speaker Notes: Notes area]

---
Amplitude Modulators
AM and double-sideband (DSB) can be generated by a balanced modulator
SSB is generated by removing the unwanted sideband and carrier with a filter (filter method) or by combining signals with certain phase relationships (phasing method)
Using only one sideband uses transmitted output power more effectively
[Speaker Notes: Notes area]

---
Frequency & Phase Modulation
Frequency modulation (FM) – the signal frequency varies (deviates) in proportion to the modulating signal’s amplitude
Phase modulation (PM) – deviation varies with both amplitude and frequency of the modulating signal
PM is produced by a reactance modulator connected to a tuned RF amplifier following the oscillator
[Speaker Notes: FM and PM signals are very similar and can both be received and demodulated by the same receiver.]

---
Practice Questions
[Speaker Notes: Notes area]

---
What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
A. 7.178 to 7.181 MHz
B. 7.178 to 7.184 MHz
C. 7.175 to 7.178 MHz
D. 7.1765 to 7.1795 MHz
  G4D08

---
What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
A. 7.178 to 7.181 MHz
B. 7.178 to 7.184 MHz
C. 7.175 to 7.178 MHz
D. 7.1765 to 7.1795 MHz
  G4D08

---
What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
A. 14.347 to 14.647 MHz
B. 14.347 to 14.350 MHz
C. 14.344 to 14.347 MHz
D. 14.3455 to 14.3485 MHz
  G4D09

---
What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
A. 14.347 to 14.647 MHz
B. 14.347 to 14.350 MHz
C. 14.344 to 14.347 MHz
D. 14.3455 to 14.3485 MHz
  G4D09

---
How close to the lower edge of the 40-meter General Class phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
How close to the lower edge of the 40-meter General Class phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
A. At least 3 kHz above the edge of the segment
B. At least 3 kHz below the edge of the segment
C. Your displayed carrier frequency may be set at the edge of the segment
D. At least 1 kHz above the edge of the segment
  G4D10

---
How close to the lower edge of the 40-meter General Class phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
A. At least 3 kHz above the edge of the segment
B. At least 3 kHz below the edge of the segment
C. Your displayed carrier frequency may be set at the edge of the segment
D. At least 1 kHz above the edge of the segment
  G4D10

---
How close to the upper edge of the 20-meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
How close to the upper edge of the 20-meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
A. At least 3 kHz above the edge of the band
B. At least 3 kHz below the edge of the band
C. Your displayed carrier frequency may be set at the edge of the band
D. At least 1 kHz below the edge of the segment
  G4D11

---
How close to the upper edge of the 20-meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB?
A. At least 3 kHz above the edge of the band
B. At least 3 kHz below the edge of the band
C. Your displayed carrier frequency may be set at the edge of the band
D. At least 1 kHz below the edge of the segment
  G4D11

---
What are the basic components of virtually all sine wave oscillators?
What are the basic components of virtually all sine wave oscillators?
A. An amplifier and a divider
B. A frequency multiplier and a mixer
C. A circulator and a filter operating in a feed-forward loop
D. A filter and an amplifier operating in a feedback loop
  G7B07

---
What are the basic components of virtually all sine wave oscillators?
A. An amplifier and a divider
B. A frequency multiplier and a mixer
C. A circulator and a filter operating in a feed-forward loop
D. A filter and an amplifier operating in a feedback loop
  G7B07

---
What determines the frequency of an LC oscillator?
What determines the frequency of an LC oscillator?
A. The number of stages in the counter
B. The number of stages in the divider
C. The inductance and capacitance in the tank circuit
D. The time delay of the lag circuit
  G7B09

---
What determines the frequency of an LC oscillator?
A. The number of stages in the counter
B. The number of stages in the divider
C. The inductance and capacitance in the tank circuit
D. The time delay of the lag circuit
  G7B09

---
Which of the following is an advantage of a transceiver controlled by a direct digital synthesizer (DDS)?
Which of the following is an advantage of a transceiver controlled by a direct digital synthesizer (DDS)?
A. Wide tuning range and no need for band switching
B. Relatively high power output
C. Relatively low power consumption
D. Variable frequency with the stability of a crystal oscillator
  G7C05

---
Which of the following is an advantage of a transceiver controlled by a direct digital synthesizer (DDS)?
A. Wide tuning range and no need for band switching
B. Relatively high power output
C. Relatively low power consumption
D. Variable frequency with the stability of a crystal oscillator
  G7C05

---
What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
A. Multiplex modulation
B. Phase modulation
C. Amplitude modulation
D. Pulse modulation
  G8A04

---
What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage?
A. Multiplex modulation
B. Phase modulation
C. Amplitude modulation
D. Pulse modulation
  G8A04

---
What is one advantage of carrier suppression in a single sideband phone transmission versus full carrier amplitude modulation?
What is one advantage of carrier suppression in a single sideband phone transmission versus full carrier amplitude modulation?
A. Audio fidelity is improved
B. Greater modulation percentage is obtainable with lower distortion
C. Available transmitter power can be used more effectively
D. Simpler receiving equipment can be used
  G8A06

---
What is one advantage of carrier suppression in a single sideband phone transmission versus full carrier amplitude modulation?
A. Audio fidelity is improved
B. Greater modulation percentage is obtainable with lower distortion
C. Available transmitter power can be used more effectively
D. Simpler receiving equipment can be used
  G8A06

---
What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal?
What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal?
A. Mixer
B. BFO
C. VFO
D. Discriminator
  G8B01

---
What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal?
A. Mixer
B. BFO
C. VFO
D. Discriminator
  G8B01

---
What is another term for the mixing of two RF signals?
What is another term for the mixing of two RF signals?
A. Heterodyning
B. Synthesizing
C. Cancellation
D. Phase inverting
  G8B03

---
What is another term for the mixing of two RF signals?
A. Heterodyning
B. Synthesizing
C. Cancellation
D. Phase inverting
  G8B03

---
What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
A. Mixer
B. Reactance modulator
C. Pre-emphasis network
D. Multiplier
  G8B04

---
What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency?
A. Mixer
B. Reactance modulator
C. Pre-emphasis network
D. Multiplier
  G8B04

---
General License Course
Chapter 5
Lesson Plan Module 19 –
Transmitter Structure

---
CW Transmitters
Simplest transmitter is a two-stage CW transmitter
It consists of an oscillator and an amplifier, with the amplifier turned on and off by a key or keyer
[Speaker Notes: Notes area]

---
SSB Phone Transmitters
A balanced modulator stage combines signals from the carrier oscillator and speech amplifier to produce DSB
The first filter removes the unwanted sideband, producing SSB.
[Speaker Notes: The balanced modulator produces DSB with the carrier suppressed. The first filter then removes the unwanted sideband, producing SSB. A mixer shifts the frequency of the SSB signal to the desired output frequency and a filter removes the unwanted mixing product.]

---
FM Transmitters
In a 2 meter FM transmitter, the modulated oscillator frequency is approximately 12 MHz
Multipliers then select the 12th harmonic for transmission (12 x 12 = 144)
For example, for an output on 146.52 MHz, the oscillator must produce a 146.52 ÷ 12 = 12.21 MHz signal
[Speaker Notes: A VHF/UHF FM (or PM) transmitter starts by producing a modulated signal at a low frequency with a stable oscillator. Multiplier stages then produce harmonics of the modulated signal in steps of x2 or x3. The 12th harmonic can be produced by two x3 multipliers (triplers) and a single x2 (double) or by a tripler (x3) and two doublers (x2, x2).]

---
FM Transmitters
[Speaker Notes: Notes area]

---
FM Transmitters
Deviation of the modulated oscillator output is also multiplied, increasing with each harmonic
Example: If the 146.52 FM signal produced from the 12 MHz oscillator is to have the standard deviation of 5 kHz, the maximum deviation of the oscillator is:
5 kHz ÷ 12 = 416.7 Hz
[Speaker Notes: Notes area]

---
FM Transmitters
Carson’s Rule is a formula that gives an approximation of an FM signal’s bandwidth:
BW = 2 × (peak deviation + highest modulating frequency)
Example: If an FM phone signal’s peak deviation is limited to 5 kHz and the highest modulating frequency is 3 kHz, then:
BW = 2 × (5 + 3) = 16 kHz
[Speaker Notes: Notes area]

---
Signal Quality
Overmodulation – AM Modes:
Distorts the transmitted audio
Increases the signal’s bandwidth by creating unwanted spurious signals called splatter or buckshot
Often caused by mis-adjustment
Mic gain set too high (reduce microphone gain or speak more quietly)
Speech processor set too high (turn it down or off
[Speaker Notes: This section discusses the causes of poor signal quality and what the operator should do about them]

---
Overmodulation
Modulation Envelope
[Speaker Notes: This is an AM signal. Show the relationship between the modulating signal and the envelope of the modulated AM signal. Note that SSB signals look similar but are not quite the same.]

---
Overmodulation
If the drive level to transmitter output stages or external amplifiers is increased beyond the point of maximum output power level, the result is flat-topping or clipping
Use normal speech or audio levels during both testing and on-the-air contacts
Under difficult conditions it’s natural to raise your voice (only reduces intelligibility)
[Speaker Notes: This is just one type of overmodulation. If the envelope flattens out on the top, that is “flat-topping” or “clipping”. Other possible ways for over-modulation are excessive compression.]

---
Overmodulation
Automatic level control (ALC) system helps prevent overmodulation and excessive drive
ALC reduces output power on voice peaks
Mic gain should be adjusted to cause the ALC to activate only on voice peaks
Two-tone test for transmitter linearity is very helpful in keeping your signal clean
Test consists of modulating your transmitter with a pair of audio tones that are not harmonically related (700 and 1900 Hz)
[Speaker Notes: Excessive ALC action also causes signal distortion and spurious output signals. ALC should not be used with digital signals.]

---
Speech Processing
Speech processing increases the average power of the speech signal without excessively distorting the signal
The result is improved intelligibility of the received signal in poor conditions
Speech processors can also amplify low-level background noise, reducing intelligibility (balance power increase against reduction in intelligibility)
[Speaker Notes: Speech processing and compression should never be used with digital signals.]

---
Overmodulation
Overmodulated FM signals:
Overdeviation is caused by speaking too loudsly or mic gain too high
The received signal is distorted
Creates interference to adjacent channels
[Speaker Notes: Notes area]

---
Key Clicks
Key clicks are sharp transient clicking sounds heard on adjacent frequencies as a transmitter turns on and off too rapidly during CW transmissions
[Speaker Notes: Notes area]

---
Amplifiers
High-power HF amplifiers usually use vacuum tube circuits that require operator adjustment
Solid-state becoming more common
AM modes such as SSB require linear amplifiers that accurately reproduce the input signal waveform
[Speaker Notes: Note that tubes are very tolerant of misadjustment and are rugged but solid state amplifiers are becoming more common and affordable. Solid state “no-tune” amplifiers are available at different power levels.]

---
Amplifier Classes
Class A – The most linear
Lowest signal distortion
Least efficient
Class B – (push-pull) a pair of amplifying devices each active during complementary halves of the signal’s cycle
Good efficiency
Linearity can be good
[Speaker Notes: Notes area]

---
Amplifier Classes
Class AB – the amplifying device is active for more than one-half but less than an entire signal cycle
Linearity is not as good as Class A, but efficiency is improved
Class C – amplifying devices are active for less than one-half of the signal’s cycle
The highest efficiency but poor linearity
Only suitable for CW and FM because they have very poor linearity
[Speaker Notes: Explain why linearity is not required for CW and FM. Note that harmonics of the transmitted signal must still be removed. Note that switchmode amplifiers (Class D, E, etc) are not yet common in amateur service.]

---
Amateur Amplifiers
Most linear amplifiers can be operated in either Class AB for SSB operation or in Class C for CW
The efficiency of an amplifier is defined as the RF output power divided by the dc input power
[Speaker Notes: A front-panel switch changes the bias between SSB and CW settings]

---
Amplifiers
Transceivers often include a delay in the keying circuit
T/R relay is completely switched before the transceiver is allowed to supply any RF output
Delay prevents hot-switching
Hot-switching can destroy the relay or other external devices
[Speaker Notes: When using external equipment such as a preamp or antenna switch, it is important for all switches to be completely set before RF is generated. More complex systems such as for VHF/UHF DXing or contesting use a sequencer to control the switches, relays, and RF output.]

---
Amplifier Tuning
Set the band switch to proper frequency
Apply a small amount of drive power while adjusting the TUNE control for a minimum setting (“dip”) plate current
Adjust the LOAD control to maximize (or “peak”) output power
[Speaker Notes: Used on vacuum tube amplifiers]

---
Amplifier Tuning
Continue to adjust drive, tune, load for desired output power
Watch meters to prevent exceeding the maximum grid and plate current
Input power may also be adjusted during the process
Continue adjustments until desired output power is reached
[Speaker Notes: Most hams keep a list of settings for their amplifiers on each band. This allows them to minimize tune-up time on the air. Explain why this is good practice.]

---
Neutralization
HF amplifiers are capable of becoming an oscillator (called self-oscillation)
Self-oscillation creates spurious output signals and may damage the tube or amplifier components
The technique of preventing self-oscillation is called neutralization
[Speaker Notes: Neutralization is only required when tubes or components are changed.]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is normally meant by operating a transceiver in "split" mode?
What is normally meant by operating a transceiver in "split" mode?
A. The radio is operating at half power
B. The transceiver is operating from an external power source
C. The transceiver is set to different transmit and receive frequencies
D. The transmitter is emitting an SSB signal, as opposed to DSB operation
  G4A03

---
What is normally meant by operating a transceiver in "split" mode?
A. The radio is operating at half power
B. The transceiver is operating from an external power source
C. The transceiver is set to different transmit and receive frequencies
D. The transmitter is emitting an SSB signal, as opposed to DSB operation
  G4A03

---
What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control?
What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control?
A. A pronounced peak
B. A pronounced dip
C. No change will be observed
D. A slow, rhythmic oscillation
  G4A04

---
What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control?
A. A pronounced peak
B. A pronounced dip
C. No change will be observed
D. A slow, rhythmic oscillation
  G4A04

---
What condition can lead to permanent damage to a solid-state RF power amplifier?
What condition can lead to permanent damage to a solid-state RF power amplifier?
A. Insufficient drive power
B. Low input SWR
C. Shorting the input signal to ground
D. Excessive drive power
  G4A07

---
What condition can lead to permanent damage to a solid-state RF power amplifier?
A. Insufficient drive power
B. Low input SWR
C. Shorting the input signal to ground
D. Excessive drive power
  G4A07

---
What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier?
What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier?
A. Minimum SWR on the antenna
B. Minimum plate current without exceeding maximum allowable grid current
C. Highest plate voltage while minimizing grid current
D. Maximum power output without exceeding maximum allowable plate current
  G4A08

---
What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier?
A. Minimum SWR on the antenna
B. Minimum plate current without exceeding maximum allowable grid current
C. Highest plate voltage while minimizing grid current
D. Maximum power output without exceeding maximum allowable plate current
  G4A08

---
Why is a time delay sometimes included in a transmitter keying circuit?
Why is a time delay sometimes included in a transmitter keying circuit?
A. To prevent stations from interfering with one another
B. To allow the transmitter power regulators to charge properly
C. To allow time for transmit-receive changeover operations to complete properly before RF output is allowed
D. To allow time for a warning signal to be sent to other stations
  G4A09

---
Why is a time delay sometimes included in a transmitter keying circuit?
A. To prevent stations from interfering with one another
B. To allow the transmitter power regulators to charge properly
C. To allow time for transmit-receive changeover operations to complete properly before RF output is allowed
D. To allow time for a warning signal to be sent to other stations
  G4A09

---
Which of the following is a common use for the dual VFO feature on a transceiver?
Which of the following is a common use for the dual VFO feature on a transceiver?
A. To allow transmitting on two frequencies at once
B. To permit full duplex operation, that is transmitting and receiving at the same time
C. To permit monitoring of two different frequencies
D. To facilitate computer interface
  G4A12

---
Which of the following is a common use for the dual VFO feature on a transceiver?
A. To allow transmitting on two frequencies at once
B. To permit full duplex operation, that is transmitting and receiving at the same time
C. To permit monitoring of two different frequencies
D. To facilitate computer interface
  G4A12

---
What signals are used to conduct a two-tone test?
What signals are used to conduct a two-tone test?
A. Two audio signals of the same frequency shifted 90 degrees
B. Two non-harmonically related audio signals
C. Two swept frequency tones
D. Two audio frequency range square wave signals of equal amplitude
  G4B07

---
What signals are used to conduct a two-tone test?
A. Two audio signals of the same frequency shifted 90 degrees
B. Two non-harmonically related audio signals
C. Two swept frequency tones
D. Two audio frequency range square wave signals of equal amplitude
  G4B07

---
What type of transmitter performance does a two-tone test analyze?
What type of transmitter performance does a two-tone test analyze?
A. Linearity
B. Percentage of suppression of carrier and undesired sideband for SSB
C. Percentage of frequency modulation
D. Percentage of carrier phase shift
  G4B15

---
What type of transmitter performance does a two-tone test analyze?
A. Linearity
B. Percentage of suppression of carrier and undesired sideband for SSB
C. Percentage of frequency modulation
D. Percentage of carrier phase shift
  G4B15

---
What is the purpose of a speech processor as used in a modern transceiver?
What is the purpose of a speech processor as used in a modern transceiver?
A. Increase the intelligibility of transmitted phone signals during poor conditions
B. Increase transmitter bass response for more natural sounding SSB signals
C. Prevent distortion of voice signals
D. Decrease high-frequency voice output to prevent out of band operation
  G4D01

---
What is the purpose of a speech processor as used in a modern transceiver?
A. Increase the intelligibility of transmitted phone signals during poor conditions
B. Increase transmitter bass response for more natural sounding SSB signals
C. Prevent distortion of voice signals
D. Decrease high-frequency voice output to prevent out of band operation
  G4D01

---
Which of the following describes how a speech processor affects a transmitted single sideband phone signal?
Which of the following describes how a speech processor affects a transmitted single sideband phone signal?
A. It increases peak power
B. It increases average power
C. It reduces harmonic distortion
D. It reduces intermodulation distortion
  G4D02

---
Which of the following describes how a speech processor affects a transmitted single sideband phone signal?
A. It increases peak power
B. It increases average power
C. It reduces harmonic distortion
D. It reduces intermodulation distortion
  G4D02

---
Which of the following can be the result of an incorrectly adjusted speech processor?
Which of the following can be the result of an incorrectly adjusted speech processor?
A. Distorted speech
B. Splatter
C. Excessive background pickup
D. All of these choices are correct
  G4D03

---
Which of the following can be the result of an incorrectly adjusted speech processor?
A. Distorted speech
B. Splatter
C. Excessive background pickup
D. All of these choices are correct
  G4D03

---
How is the efficiency of an RF power amplifier determined?
How is the efficiency of an RF power amplifier determined?
A. Divide the DC input power by the DC output power
B. Divide the RF output power by the DC input power
C. Multiply the RF input power by the reciprocal of the RF output power
D. Add the RF input power to the DC output power
  G7B08

---
How is the efficiency of an RF power amplifier determined?
A. Divide the DC input power by the DC output power
B. Divide the RF output power by the DC input power
C. Multiply the RF input power by the reciprocal of the RF output power
D. Add the RF input power to the DC output power
  G7B08

---
Which of the following is a characteristic of a Class A amplifier?
Which of the following is a characteristic of a Class A amplifier?
A. Low standby power
B. High Efficiency
C. No need for bias
D. Low distortion
  G7B10

---
Which of the following is a characteristic of a Class A amplifier?
A. Low standby power
B. High Efficiency
C. No need for bias
D. Low distortion
  G7B10

---
For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal?
For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal?
A. SSB
B. CW
C. AM
D. All of these choices are correct
  G7B11

---
For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal?
A. SSB
B. CW
C. AM
D. All of these choices are correct
  G7B11

---
Which of these classes of amplifiers has the highest efficiency?
Which of these classes of amplifiers has the highest efficiency?
A. Class A
B. Class B
C. Class AB
D. Class C
  G7B12

---
Which of these classes of amplifiers has the highest efficiency?
A. Class A
B. Class B
C. Class AB
D. Class C
  G7B12

---
What is the reason for neutralizing the final amplifier stage of a transmitter?
What is the reason for neutralizing the final amplifier stage of a transmitter?
A. To limit the modulation index
B. To eliminate self-oscillations
C. To cut off the final amplifier during standby periods
D. To keep the carrier on frequency
  G7B13

---
What is the reason for neutralizing the final amplifier stage of a transmitter?
A. To limit the modulation index
B. To eliminate self-oscillations
C. To cut off the final amplifier during standby periods
D. To keep the carrier on frequency
  G7B13

---
Which of the following describes a linear amplifier?
Which of the following describes a linear amplifier?
A. Any RF power amplifier used in conjunction with an amateur transceiver
B. An amplifier in which the output preserves the input waveform
C. A Class C high efficiency amplifier
D. An amplifier used as a frequency multiplier
  G7B14

---
Which of the following describes a linear amplifier?
A. Any RF power amplifier used in conjunction with an amateur transceiver
B. An amplifier in which the output preserves the input waveform
C. A Class C high efficiency amplifier
D. An amplifier used as a frequency multiplier
  G7B14

---
Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters?
Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters?
A. Carrier oscillator
B. Filter
C. IF amplifier
D. RF amplifier
  G7C01

---
Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters?
A. Carrier oscillator
B. Filter
C. IF amplifier
D. RF amplifier
  G7C01

---
Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters?
Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters?
A. Discriminator
B. Detector
C. IF amplifier
D. Balanced modulator
  G7C02

---
Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters?
A. Discriminator
B. Detector
C. IF amplifier
D. Balanced modulator
  G7C02

---
Which of the following is an effect of overmodulation?
Which of the following is an effect of overmodulation?
A. Insufficient audio
B. Insufficient bandwidth
C. Frequency drift
D. Excessive bandwidth
  G8A08

---
Which of the following is an effect of overmodulation?
A. Insufficient audio
B. Insufficient bandwidth
C. Frequency drift
D. Excessive bandwidth
  G8A08

---
What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver?
What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver?
A. The RF clipping level
B. Transmit audio or microphone gain
C. Antenna inductance or capacitance
D. Attenuator level
  G8A09

---
What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver?
A. The RF clipping level
B. Transmit audio or microphone gain
C. Antenna inductance or capacitance
D. Attenuator level
  G8A09

---
What is meant by the term flat-topping when referring to a single sideband phone transmission?
What is meant by the term flat-topping when referring to a single sideband phone transmission?
A. Signal distortion caused by insufficient collector current
B. The transmitter's automatic level control (ALC) is properly adjusted
C. Signal distortion caused by excessive drive
D. The transmitter's carrier is properly suppressed
  G8A10

---
What is meant by the term flat-topping when referring to a single sideband phone transmission?
A. Signal distortion caused by insufficient collector current
B. The transmitter's automatic level control (ALC) is properly adjusted
C. Signal distortion caused by excessive drive
D. The transmitter's carrier is properly suppressed
  G8A10

---
What is the modulation envelope of an AM signal?
What is the modulation envelope of an AM signal?
A. The waveform created by connecting the peak values of the modulated signal
B. The carrier frequency that contains the signal
C. Spurious signals that envelop nearby frequencies
D. The bandwidth of the modulated signal
  G8A11

---
What is the modulation envelope of an AM signal?
A. The waveform created by connecting the peak values of the modulated signal
B. The carrier frequency that contains the signal
C. Spurious signals that envelop nearby frequencies
D. The bandwidth of the modulated signal
  G8A11

---
What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
A. 3 kHz
B. 5 kHz
C. 8 kHz
D. 16 kHz
  G8B06

---
What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency?
A. 3 kHz
B. 5 kHz
C. 8 kHz
D. 16 kHz
  G8B06

---
What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
A. 101.75 Hz
B. 416.7 Hz
C. 5 kHz
D. 60 kHz
  G8B07

---
What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter?
A. 101.75 Hz
B. 416.7 Hz
C. 5 kHz
D. 60 kHz
  G8B07

---
General License Course
Chapter 5
Lesson Plan Module 20 –
Receiver Structure

---
Superheterodyne Receivers
Received signals are incredibly weak – on the order of nano or picowatts
[Speaker Notes: Notes area]

---
Superhet Receiver
Received signals are first boosted by the RF amplifier, then applied to the RF input of a mixer
The local oscillator (LO) is adjusted so that the desired signal creates a mixing product at the intermediate frequency (IF)
A detector or demodulator stage follows the IF to recover the modulating information
[Speaker Notes: Superhet receivers are being displaced by SDR and DSP techniques that perform the frequency conversion and demodulation in software.]

---
Simplest Superhet
The simplest possible superhet consists of a mixer connected to the antenna, an HF oscillator to act as an LO, and a detector that operates directly on the resulting IF signal
Once amplified to a more usable level, SSB and CW signals are demodulated by a product detector
A type of mixer that combines the IF signal with the output of a beat frequency oscillator (BFO) to produce an audio frequency mixing product
[Speaker Notes: Cover the definitions of sensitivity (the ability to detect a signal) and selectivity (the ability to discriminate between different signals). Detectors can be simple envelope detectors for AM. SSB and CW require the product detector to provide an audio signals. FM requires a discriminator or quadrature detector.]

---
Superhet Receiver
The receiver’s front end is made up of the RF amplifier (if any) and the first mixer
A preamplifier is used for weak signals
A preselector is an RF filter to remove strong out of band signals
In an FM receiver the linear IF amplifier is replaced by a limiter.
A discriminator or a quadrature detector replaces the product detector
[Speaker Notes: The limiter amplifies the FM signal until it is a square wave with varying frequency. All amplitude information has been removed. This is why FM receivers don’t respond to natural static and noise – that information is removed from the signal by the lmiter.]

---
Doing the Math
Example: If the IF is 455 kHz and the LO frequency is 13.800 MHz, signals at both 14.255 and 13.345 MHz will create a mixing product at 455 kHz
Assuming the receiver is supposed to receive the 14.255 MHz signal, the undesired signal at 13.345 MHz is called an image
Filters in the RF Front End remove signals at image frequencies to eliminate this source of interfering signals.
[Speaker Notes: Notes area]

---
Superhet Receiver
Superhet receivers may have one, two, or three IF stages, resulting in a single-, double-, or triple-conversion receiver
Filters are applied at each IF to remove unwanted signals and noise
Filters improve signal quality with the lowest unwanted noise and interference, maximizing the signal-to-noise ratio (SNR)
[Speaker Notes: Note that SNR can be improved by either increasing signal strength or removing noise and interference. Using the right receiver bandwidth allows all of the desired signal to be received while removing noise and undesired signals.]

---
Digital Signal Processing
The general term for converting signals from analog to digital form, operating on them with a microprocessor, and converting them back to analog is digital signal processing (DSP)
[Speaker Notes: Notes area]

---
SDR
Some transceivers have so much of their functions implemented by DSP that the entire structure can be changed by running different software
These radios are referred to as SDR, for software-defined radios
SDR is rapidly becoming the dominant technology in high-performance transceivers
[Speaker Notes: Notes area]

---
Common DSP Functions
Signal filtering – offers selectable preprogrammed filters and adjustable filter bandwidth and shape, such as notch filters
Noise reduction – DSP can distinguish and remove some kinds of noise, leaving only the desired speech or CW for the operator to copy
Audio frequency equalization – Adjustable receive or transmit audio frequency response to suit preferences
[Speaker Notes: Remind students that DSP noise reduction programs may cause significant problems for digital mode reception because they affect the audio of the received signal.]

---
Common DSP Functions
Notch filtering – Interfering signals in the receiver’s passband, particularly carriers from broadcast stations, can be sensed and removed by DSP
An automatic notch filter can track interfering signals as they change frequency and eliminate more than one at a time
[Speaker Notes: Notes area]

---
RF Gain Control
Set the RF gain control to maximum for the highest receiver sensitivity
Lower values of RF gain reduces background noise and helps prevent receiver overload
Maximum sensitivity may not be the best
The automatic gain control (AGC) circuits vary the gain of the RF and IF amplifiers so that the output volume of a signal stays relatively constant for both weak and strong signals
[Speaker Notes: Notes area]

---
S Meter
The AGC circuit adjusts receiver gain by changing a voltage that controls the RF and IF amplifier gain
The voltage is read by the S meter of the receiver, which is used to measure received signal strength
“S” stands for “signal”
[Speaker Notes: Notes area]

---
S Meter
S meters are calibrated in S units, equal to 6 dB change per S unit
S9 is at the midpoint of the S meter display – good signal
Additional markings 20, 40, and 60 correspond to dB above S9
A reading of S9 + 20 dB, therefore corresponds to a signal 20 dB (100 times) stronger than an S9 signal
[Speaker Notes: Most S meters are not strictly calibrated to the 6 dB/S unit standard and may only approach that level of accuracy in the middle of their range. S units are not expected to be accurate – mostly used a relative signal strength comparisons. 6 dB = 4 times increase in power 20 dB = 100 times increase in power]

---
Receiver Linearity
If the received signal is distorted, spurious signals will appear just as if a transmitting station were emitting them
The most common form of receiver nonlinearity is caused by front-end overload
The attenuator and RF gain controls can reduce received noise and distortion caused by strong signals
[Speaker Notes: Encourage students to adjust their receiver RF gain and attenuator controls to keep the receiver operating linearly and for best SNR. The preamplifier and noise blanker circuits make the receiver susceptible to overload, creating a great deal of interfering signals inside the receiver ciruits]

---
Practice Questions
[Speaker Notes: Notes area]

---
Which of the following is a use for the IF shift control on a receiver?
Which of the following is a use for the IF shift control on a receiver?
A. To avoid interference from stations very close to the receive frequency
B. To change frequency rapidly
C. To permit listening on a different frequency from that on which you are transmitting
D. To tune in stations that are slightly off frequency without changing your transmit frequency
  G4A11

---
Which of the following is a use for the IF shift control on a receiver?
A. To avoid interference from stations very close to the receive frequency
B. To change frequency rapidly
C. To permit listening on a different frequency from that on which you are transmitting
D. To tune in stations that are slightly off frequency without changing your transmit frequency
  G4A11

---
What is one reason to use the attenuator function that is present on many HF transceivers?
What is one reason to use the attenuator function that is present on many HF transceivers?
A. To reduce signal overload due to strong incoming signals
B. To reduce the transmitter power when driving a linear amplifier
C. To reduce power consumption when operating from batteries
D. To slow down received CW signals for better copy
  G4A13

---
What is one reason to use the attenuator function that is present on many HF transceivers?
A. To reduce signal overload due to strong incoming signals
B. To reduce the transmitter power when driving a linear amplifier
C. To reduce power consumption when operating from batteries
D. To slow down received CW signals for better copy
  G4A13

---
Which of the following is a function of a digital signal processor?
Which of the following is a function of a digital signal processor?
A. To provide adequate grounding
B. To remove noise from received signals
C. To increase antenna gain
D. To increase antenna bandwidth
  G4C11

---
Which of the following is a function of a digital signal processor?
A. To provide adequate grounding
B. To remove noise from received signals
C. To increase antenna gain
D. To increase antenna bandwidth
  G4C11

---
Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter?
Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter?
A. A wide range of filter bandwidths and shapes can be created
B. Fewer digital components are required
C. Mixing products are greatly reduced
D. The DSP filter is much more effective at VHF frequencies
  G4C12

---
Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter?
A. A wide range of filter bandwidths and shapes can be created
B. Fewer digital components are required
C. Mixing products are greatly reduced
D. The DSP filter is much more effective at VHF frequencies
  G4C12

---
Which of the following can perform automatic notching of interfering carriers?
Which of the following can perform automatic notching of interfering carriers?
A. Bandpass tuning
B. A Digital Signal Processor (DSP) filter
C. Balanced mixing
D. A noise limiter
  G4C13

---
Which of the following can perform automatic notching of interfering carriers?
A. Bandpass tuning
B. A Digital Signal Processor (DSP) filter
C. Balanced mixing
D. A noise limiter
  G4C13

---
What does an S meter measure?
What does an S meter measure?
A. Conductance
B. Impedance
C. Received signal strength
D. Transmitter power output
  G4D04

---
What does an S meter measure?
A. Conductance
B. Impedance
C. Received signal strength
D. Transmitter power output
  G4D04

---
How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
A. It is 10 times less powerful
B. It is 20 times less powerful
C. It is 20 times more powerful
D. It is 100 times more powerful
  G4D05

---
How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
A. It is 10 times less powerful
B. It is 20 times less powerful
C. It is 20 times more powerful
D. It is 100 times more powerful
  G4D05

---
Where is an S meter found?
Where is an S meter found?
A. In a receiver
B. In an SWR bridge
C. In a transmitter
D. In a conductance bridge
  G4D06

---
Where is an S meter found?
A. In a receiver
B. In an SWR bridge
C. In a transmitter
D. In a conductance bridge
  G4D06

---
How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
A. Approximately 1.5 times
B. Approximately 2 times
C. Approximately 4 times
D. Approximately 8 times
  G4D07

---
How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
A. Approximately 1.5 times
B. Approximately 2 times
C. Approximately 4 times
D. Approximately 8 times
  G4D07

---
What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver?
What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver?
A. Balanced modulator
B. IF amplifier
C. Mixer
D. Detector
  G7C03

---
What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver?
A. Balanced modulator
B. IF amplifier
C. Mixer
D. Detector
  G7C03

---
What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers?
What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers?
A. RF oscillator
B. IF filter
C. Balanced modulator
D. Product detector
  G7C04

---
What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers?
A. RF oscillator
B. IF filter
C. Balanced modulator
D. Product detector
  G7C04

---
What is the simplest combination of stages that implement a superheterodyne receiver?
What is the simplest combination of stages that implement a superheterodyne receiver?
A. RF amplifier, detector, audio amplifier
B. RF amplifier, mixer, IF discriminator
C. HF oscillator, mixer, detector
D. HF oscillator, prescaler, audio amplifier
  G7C07

---
What is the simplest combination of stages that implement a superheterodyne receiver?
A. RF amplifier, detector, audio amplifier
B. RF amplifier, mixer, IF discriminator
C. HF oscillator, mixer, detector
D. HF oscillator, prescaler, audio amplifier
  G7C07

---
What type of circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio?
What type of circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio?
A. Product detector
B. Phase inverter
C. Mixer
D. Discriminator
  G7C08

---
What type of circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio?
A. Product detector
B. Phase inverter
C. Mixer
D. Discriminator
  G7C08

---
Which of the following is needed for a Digital Signal Processor IF filter?
Which of the following is needed for a Digital Signal Processor IF filter?
A. An analog to digital converter
B. A digital to analog converter
C. A digital processor chip
D. All of the these choices are correct
  G7C09

---
Which of the following is needed for a Digital Signal Processor IF filter?
A. An analog to digital converter
B. A digital to analog converter
C. A digital processor chip
D. All of the these choices are correct
  G7C09

---
How is Digital Signal Processor filtering accomplished?
How is Digital Signal Processor filtering accomplished?
A. By using direct signal phasing
B. By converting the signal from analog to digital and using digital processing
C. By differential spurious phasing
D. By converting the signal from digital to analog and taking the difference of mixing products
  G7C10

---
How is Digital Signal Processor filtering accomplished?
A. By using direct signal phasing
B. By converting the signal from analog to digital and using digital processing
C. By differential spurious phasing
D. By converting the signal from digital to analog and taking the difference of mixing products
  G7C10

---
What is meant by the term “software defined radio” (SDR)?
What is meant by the term “software defined radio” (SDR)?
A. A radio in which most major signal processing functions are performed by software
B. A radio that provides computer interface for automatic logging of band and frequency
C. A radio that uses crystal filters designed using software
D. A computer model that can simulate performance of a radio to aid in the design process
  G7C11

---
What is meant by the term “software defined radio” (SDR)?
A. A radio in which most major signal processing functions are performed by software
B. A radio that provides computer interface for automatic logging of band and frequency
C. A radio that uses crystal filters designed using software
D. A computer model that can simulate performance of a radio to aid in the design process
  G7C11

---
If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, what type of interference will a 13.345 MHz signal produce in the receiver?
If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, what type of interference will a 13.345 MHz signal produce in the receiver?
A. Quadrature noise
B. Image response
C. Mixer interference
D. Intermediate interference
  G8B02

---
If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, what type of interference will a 13.345 MHz signal produce in the receiver?
A. Quadrature noise
B. Image response
C. Mixer interference
D. Intermediate interference
  G8B02

---
Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
A. It is required by FCC rules
B. It minimizes power consumption in the receiver
C. It improves impedance matching of the antenna
D. It results in the best signal to noise ratio
  G8B09

---
Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
A. It is required by FCC rules
B. It minimizes power consumption in the receiver
C. It improves impedance matching of the antenna
D. It results in the best signal to noise ratio
  G8B09

---
General License Course
Chapter 5
Lesson Plan Module 21 –
HF Station Installation

---
Mobile Installations
Mobile 100 W HF rigs require 20 A or more current at 11.5 or 12 V minimum
Power connection is direct to the battery using heavy gauge wire with a fuse in both the positive and negative leads
Do not use a cigarette lighter socket
Wiring not rated for 20 A
Socket may be damaged
[Speaker Notes: Newer cars may have a battery management system (BMS) or electronic load management (ELM) modules which require special attention to how the radio power leads should be attached. Consult the dealer or service manual for how to do this properly.]

---
Mobile Installations
Do not assume that the vehicle’s metal chassis is a suitable dc ground connection
Vehicles made from separate subsections insulated by paint or plastic
Body parts may be plastic
Connect the radio power ground either directly to the battery or to the battery ground strap where it attaches to the engine block or vehicle chassis
[Speaker Notes: Notes area]

---
Antenna Connections
The most significant limitation of mobile HF operating is the antenna system
Usually smaller in terms of a wavelength than for a home station
Can be full-size on 10 and 12 meters
40, 60, 80/75, 160 meters are particularly challenging because of electrically short antennas
[Speaker Notes: Remind students that attention must be paid to proper antenna grounding and antenna installation to get good results for HF mobile.]

---
Mobile HF Antennas
The entire vehicle is part of the antenna system
Use the most efficient antenna you can
Make sure RF ground connections to the vehicle are solid
Mount the antenna where it is as clear as possible of metal surfaces
[Speaker Notes: Remind students that attention must be paid to proper antenna grounding and antenna installation to get good results for HF mobile.]

---
Mobile Interference
Ignition noise from arcs in the spark plugs
Vehicle’s onboard control computers
Electric fuel pumps and windows
Battery charging systems
Manufacturer service bulletins can help deal with interference and noise problems
[Speaker Notes: Also see books and websites on mobile operating for guidance on proper installation and any interference or antenna problems.]

---
Grounding & Bonding
AC safety ground wiring can act more like an antenna than a ground
RF bonding is to keep all equipment at the same RF voltage
Minimizes “hot spots” (high RF voltage)
Reduces RF current flowing between pieces of equipment which can cause audio distortion or improper operation
[Speaker Notes: Notes area]

---
Grounding & Bonding
During digital operation:
Unwanted RF currents can cause audio distortion or erratic operation of computer interfaces
Activate the transmitter improperly (such as when using VOX)
Garble digital protocols causing data or connections to be lost
[Speaker Notes: Notes area]

---
Grounding & Bonding
External ground or earth connections – make the connection as short as possible with heavy wire or strap
As ground connection length approaches an odd number of ¼-wavelengths:
Presents a high impedance
Allows RF voltages on equipment enclosures and connecting cables
[Speaker Notes: Keep ground and earth connections short Use heavy conductors such as #12 or #14 AWG wire or copper strap Avoid use of coax braid – not designed to be used outside the cable jacket Flat-weave tinned braid is okay indoors if protected from water]

---
Ground & Bonding
Ground loops are created when a continuous current path exists through enclosures and cables. Loops are nearly impossible to avoid.
The loops act as single-turn inductors picking up voltages from magnetic fields. The result can be a “hum” or “buzz” in audio signals or an ac signal that interferes with control or data signals
Minimize the effect of loops by minimizing loop area and bonding equipment together.
[Speaker Notes: Minimize loop area, keep cables short, RF bonding helps minimize the effect of unavoidable loops.]

---
Ground & Bonding
Good practice is to provide good bonding and make earth connections short
All earth connections must be bonded per code
[Speaker Notes: Notes area]

---
RF Interference
Fundamental overload – radio or TV receivers unable to reject a strong signal. This causes distortion or inability to receive the desired signal.
Cure – prevent the offending signal from entering the equipment by using filters in the path of the signal.
[Speaker Notes: Notes area]

---
RF Interference
Common-mode and direct pickup (or direct detection) – The signal is picked up as common-mode current on the outside of cable shields or on all conductors of an unshielded connection
Power cords, speaker leads, telephone cable
Conducted into the equipment where it causes erratic operation or audio noise
Cure – block current with RF chokes
[Speaker Notes: Explain what common-mode current is: RF current that flows equally on all conductors of a cable (typical for unshielded cables like phone or power cords) or on the outside of a shielded cable (audio and video cables). This definition is somewhat different than is used for ac power. RF chokes can be ferrite beads or cores on the cable or the cable can be wound into a coil. The goal is to place enough impedance in the path of the current that it can’t get into the affected equipment.]

---
RF Interference
Harmonics – spurious emissions from an amateur station may be received by radio or TV equipment
Cure – use a low-pass filter at the transmitter to remove the spurious emissions
The filter’s impedance must match the characteristic impedance of the feed line
RFI to cable TV may be due to bad connectors allowing external signals to get in (or out – also known as cable leakage)
[Speaker Notes: Point out that the spurious emissions have to be filtered out at the transmitter. Once radiated, they can not be blocked. Low-pass or high-pass filters can not be used in cable systems because the system uses frequencies from HF through UHF.]

---
RF Interference
Rectification – Poor contacts between conductors picking up RF signals can create a mixer and mixing products from the signals
Cure - repair the contact or connection
Arcing – A spark or sustained arc creates radio crackling or buzz over a wide frequency range, typically from power-line hardware
May require the power company to make the necessary repairs
[Speaker Notes: Arcing noise can also be generated by motors or defective ac-powered devices and equipment. Identify the source of the noise by using portable receivers.]

---
RF Interference Suppression
Filters remove strong signals from antenna feed lines
RF chokes made from ferrite cores and beads block common-mode RF current
AC line filters may help block RF on the hot or neutral connections for ac power.
Combine line filter and RF choke to block RF on all three ac conductors.

---
RF Interference Suppression
Bypass capacitors may be recommended in older texts. This is not recommended for modern, solid-state audio amplifier outputs – it may cause them to become unstable and damage the amplifier.
Use RF chokes first
Twisted-pair speaker cable also helps.
Only try bypass capacitor as a last resort on power and non-audio signal connections
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is the purpose of the "notch filter" found on many HF transceivers?
What is the purpose of the "notch filter" found on many HF transceivers?
A. To restrict the transmitter voice bandwidth
B. To reduce interference from carriers in the receiver passband
C. To eliminate receiver interference from impulse noise sources
D. To enhance the reception of a specific frequency on a crowded band
  G4A01

---
What is the purpose of the "notch filter" found on many HF transceivers?
A. To restrict the transmitter voice bandwidth
B. To reduce interference from carriers in the receiver passband
C. To eliminate receiver interference from impulse noise sources
D. To enhance the reception of a specific frequency on a crowded band
  G4A01

---
What is one advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver?
What is one advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver?
A. Interference from impulse noise will be eliminated
B. More stations can be accommodated within a given signal passband
C. It may be possible to reduce or eliminate interference from other signals
D. Accidental out of band operation can be prevented
  G4A02

---
What is one advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver?
A. Interference from impulse noise will be eliminated
B. More stations can be accommodated within a given signal passband
C. It may be possible to reduce or eliminate interference from other signals
D. Accidental out of band operation can be prevented
  G4A02

---
What is a reason to use Automatic Level Control (ALC) with an RF power amplifier?
What is a reason to use Automatic Level Control (ALC) with an RF power amplifier?
A. To balance the transmitter audio frequency response
B. To reduce harmonic radiation
C. To reduce distortion due to excessive drive
D. To increase overall efficiency
  G4A05

---
What is a reason to use Automatic Level Control (ALC) with an RF power amplifier?
A. To balance the transmitter audio frequency response
B. To reduce harmonic radiation
C. To reduce distortion due to excessive drive
D. To increase overall efficiency
  G4A05

---
Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver?
Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver?
A. The VOX circuit does not un-key the transmitter
B. The transmitter signal is distorted
C. Frequent connection timeouts
D. All of these choices are correct
  G4A15

---
Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver?
A. The VOX circuit does not un-key the transmitter
B. The transmitter signal is distorted
C. Frequent connection timeouts
D. All of these choices are correct
  G4A15

---
Which of the following might be useful in reducing RF interference to audio frequency devices?
Which of the following might be useful in reducing RF interference to audio frequency devices?
A. Bypass inductor
B. Bypass capacitor
C. Forward-biased diode
D. Reverse-biased diode
  G4C01

---
Which of the following might be useful in reducing RF interference to audio frequency devices?
A. Bypass inductor
B. Bypass capacitor
C. Forward-biased diode
D. Reverse-biased diode
  G4C01

---
Which of the following could be a cause of interference covering a wide range of frequencies?
Which of the following could be a cause of interference covering a wide range of frequencies?
A. Not using a balun or line isolator to feed balanced antennas
B. Lack of rectification of the transmitter's signal in power conductors
C. Arcing at a poor electrical connection
D. Using a balun to feed an unbalanced antenna
  G4C02

---
Which of the following could be a cause of interference covering a wide range of frequencies?
A. Not using a balun or line isolator to feed balanced antennas
B. Lack of rectification of the transmitter's signal in power conductors
C. Arcing at a poor electrical connection
D. Using a balun to feed an unbalanced antenna
  G4C02

---
What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter?
What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter?
A. A steady hum whenever the transmitter is on the air
B. On-and-off humming or clicking
C. Distorted speech
D. Clearly audible speech
  G4C03

---
What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter?
A. A steady hum whenever the transmitter is on the air
B. On-and-off humming or clicking
C. Distorted speech
D. Clearly audible speech
  G4C03

---
What is the effect on an audio device or telephone system if there is interference from a nearby CW transmitter?
What is the effect on an audio device or telephone system if there is interference from a nearby CW transmitter?
A. On-and-off humming or clicking
B. A CW signal at a nearly pure audio frequency
C. A chirpy CW signal
D. Severely distorted audio
  G4C04

---
What is the effect on an audio device or telephone system if there is interference from a nearby CW transmitter?
A. On-and-off humming or clicking
B. A CW signal at a nearly pure audio frequency
C. A chirpy CW signal
D. Severely distorted audio
  G4C04

---
What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod?
What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod?
A. Flat braid rather than round wire has been used for the ground wire
B. Insulated wire has been used for the ground wire
C. The ground rod is resonant
D. The ground wire has high impedance on that frequency
  G4C05

---
What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod?
A. Flat braid rather than round wire has been used for the ground wire
B. Insulated wire has been used for the ground wire
C. The ground rod is resonant
D. The ground wire has high impedance on that frequency
  G4C05

---
What effect can be caused by a resonant ground connection?
What effect can be caused by a resonant ground connection?
A. Overheating of ground straps
B. Corrosion of the ground rod
C. High RF voltages on the enclosures of station equipment
D. A ground loop
  G4C06

---
What effect can be caused by a resonant ground connection?
A. Overheating of ground straps
B. Corrosion of the ground rod
C. High RF voltages on the enclosures of station equipment
D. A ground loop
  G4C06

---
What is one good way to avoid unwanted effects of stray RF energy in an amateur station?
What is one good way to avoid unwanted effects of stray RF energy in an amateur station?
A. Connect all equipment grounds together
B. Install an RF filter in series with the ground wire
C. Use a ground loop for best conductivity
D. Install a few ferrite beads on the ground wire where it connects to your station
  G4C07

---
What is one good way to avoid unwanted effects of stray RF energy in an amateur station?
A. Connect all equipment grounds together
B. Install an RF filter in series with the ground wire
C. Use a ground loop for best conductivity
D. Install a few ferrite beads on the ground wire where it connects to your station
  G4C07

---
Which of the following would reduce RF interference caused by common-mode current on an audio cable?
Which of the following would reduce RF interference caused by common-mode current on an audio cable?
A. Placing a ferrite choke around the cable
B. Adding series capacitors to the conductors
C. Adding shunt inductors to the conductors
D. Adding an additional insulating jacket to the cable
  G4C08

---
Which of the following would reduce RF interference caused by common-mode current on an audio cable?
A. Placing a ferrite choke around the cable
B. Adding series capacitors to the conductors
C. Adding shunt inductors to the conductors
D. Adding an additional insulating jacket to the cable
  G4C08

---
How can a ground loop be avoided?
How can a ground loop be avoided?
A. Connect all ground conductors in series
B. Connect the AC neutral conductor to the ground wire
C. Avoid using lock washers and star washers when making ground connections
D. Connect all ground conductors to a single point
  G4C09

---
How can a ground loop be avoided?
A. Connect all ground conductors in series
B. Connect the AC neutral conductor to the ground wire
C. Avoid using lock washers and star washers when making ground connections
D. Connect all ground conductors to a single point
  G4C09

---
What could be a symptom of a ground loop somewhere in your station?
What could be a symptom of a ground loop somewhere in your station?
A. You receive reports of “hum” on your station”s transmitted signal
B. The SWR reading for one or more antennas is suddenly very high
C. An item of station equipment starts to draw excessive amounts of current
D. You receive reports of harmonic interference from your station
  G4C10

---
What could be a symptom of a ground loop somewhere in your station?
A. You receive reports of “hum” on your station”s transmitted signal
B. The SWR reading for one or more antennas is suddenly very high
C. An item of station equipment starts to draw excessive amounts of current
D. You receive reports of harmonic interference from your station
  G4C10

---
Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation?
Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation?
A. To the battery using heavy gauge wire
B. To the alternator or generator using heavy gauge wire
C. To the battery using resistor wire
D. To the alternator or generator using resistor wire
  G4E03

---
Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation?
A. To the battery using heavy gauge wire
B. To the alternator or generator using heavy gauge wire
C. To the battery using resistor wire
D. To the alternator or generator using resistor wire
  G4E03

---
Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle’s auxiliary power socket?
Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle’s auxiliary power socket?
A. The socket is not wired with an RF-shielded power cable
B. The socket’s wiring may be inadequate for the current drawn by the transceiver
C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
D. Drawing more than 50 watts from this socket could cause the engine to overheat
  G4E04

---
Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle’s auxiliary power socket?
A. The socket is not wired with an RF-shielded power cable
B. The socket’s wiring may be inadequate for the current drawn by the transceiver
C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
D. Drawing more than 50 watts from this socket could cause the engine to overheat
  G4E04

---
Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band?
Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band?
A. “Picket Fencing” signal variation
B. The wire gauge of the DC power line to the transceiver
C. The antenna system
D. FCC rules limiting mobile output power on the 75-meter band
  G4E05

---
Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band?
A. “Picket Fencing” signal variation
B. The wire gauge of the DC power line to the transceiver
C. The antenna system
D. FCC rules limiting mobile output power on the 75-meter band
  G4E05

---
Which of the following may cause interference to be heard in the receiver of an HF radio installed in a recent model vehicle?
Which of the following may cause interference to be heard in the receiver of an HF radio installed in a recent model vehicle?
A. The battery charging system
B. The fuel delivery system
C. The vehicle control computer
D. All of these choices are correct
  G4E07

---
Which of the following may cause interference to be heard in the receiver of an HF radio installed in a recent model vehicle?
A. The battery charging system
B. The fuel delivery system
C. The vehicle control computer
D. All of these choices are correct
  G4E07

---
What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted?
What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted?
A. Substantially higher
B. About the same
C. Substantially lower
D. Twice the transmission line impedance
  G7C06

---
What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted?
A. Substantially higher
B. About the same
C. Substantially lower
D. Twice the transmission line impedance
  G7C06