General License Course Chapter 4
General License Course
Chapter 4
Lesson Plan Module 14 –
Active Components

---
Semiconductor Components
Diodes & Rectifiers
Junction diode uses PN junction to block flow of current in one direction
Current flows when a positive voltage is applied from the P-type to the N-type material (forward bias)
Diode forward voltage:
silicon 0.7 V,
germanium 0.3 V
2015 General License Course
[Speaker Notes: Explain the diode’s forward voltage is created by the amount of energy it takes to force current across the junction.]

---
Semiconductor Components
Diode Ratings:
Peak inverse voltage (PIV) – maximum reverse voltage before breakdown occurs.
Average forward current (IF) – Exceeding the diode’s rating will destroy the diode’s internal structure due to heat.
Junction capacitance (CJ) – when reverse biased, layers of P- and N-type material act like plates of a small capacitor. The larger the CJ the longer it takes to switch to conducting.
[Speaker Notes: Breakdown occurs because the junction is no longer able to keep the electrons from flowing across it – the voltage is too high. This usually destroys the junction and the diode. Heat is created by forward current times forward voltage, just like for a resistor.]

---
Diode Types
PIN diode – low forward voltage drop, used for RF switching
Schottky diode – low junction capacitance allows high-frequency operation
Varactor – reverse biased acts like a variable capacitor
Zener diode – used as a voltage regulator
[Speaker Notes: Notes area]

---
Bipolar Transistors
Bipolar junction
transistors have
3 electrodes:
Collector (C)
Base (B)
Emitter (E)
Controlled by current flow between base and emitter
[Speaker Notes: Notes area]

---
Bipolar Transistors
Very little base-emitter current is required for the collector-emitter current to flow
Control of a larger current by a smaller current is current gain or beta ()
[Speaker Notes: Notes area]

---
Field Effect Transistor (FET)
The FET has 3
electrodes
Drain (D)
Source (S)
Gate (G)
Controlled by voltage between gate and source.
Metal-oxide-semiconductors (MOSFETs) insulate the gate with a thin layer of oxide
[Speaker Notes: Notes area]

---
Transistors
Transistors’ high amplification makes them useful as switches for voltage and current
Saturation – when further increases in input result in no output change
Cutoff – when the input signal reduces output current to zero
Saturation & cutoff states represent a digital ON/OFF switch
A transistor’s metal case can be connected to the chassis or heat sink by an insulator
[Speaker Notes: Notes area]

---
Vacuum Tubes
All amplifying tubes have
at least 3 electrodes
Compared to transistors,
the tube is most like the
field effect transistor (FET)
Vacuum tubes typically
operate at hazardous
voltages as high as
2000 to 3000 volts
(use CAUTION!)
[Speaker Notes: Notes area]

---
Vacuum Tubes
Tube terminology:
Filament or heater – heats the cathode to make it emit electrons
Cathode – source of electrons
Control grid – regulates electron travel between the cathode and plate
Screen grid – reduces grid-to-plate capacitance
Suppressor grid – prevents electrons from traveling from the plate to the control or screen grid
Plate – collects electrons
[Speaker Notes: Notes area]

---
Analog Integrated Circuits (ICs)
Analog ICs or “chips”:
Used for amplification, filtering, measurement, and power control
A linear voltage regulator is used to maintain a power supply output at a constant voltage over a wide range of currents
Operational amps (op amp) are used for dc and audio circuits
[Speaker Notes: Notes area]

---
Digital Integrated Circuits (ICs)
Digital ICs operate with discrete values of voltage and current representing the binary numbers system values 0 and 1
Digital electronic circuits operate with only two stable states of operation, ON or OFF
Digital circuits can perform computations or control functions
CMOS (complementary metal-oxide semiconductors) technology is popular because of its high speed and low power consumption
[Speaker Notes: Notes area]

---
Digital Logic Basics
[Speaker Notes: Concentrate on showing the functions needed to pass the exam questions. Point out that these basic functions can be combined to create arbitrarily complex logic functions and form the heart of nearly all digital circuits, including microprocessors.]

---
Digital Logic Basics
The basic building blocks of digital circuits are called gates
Inversion (changing a 1 to a 0 and vice versa)
OR and AND functions
Inverted NOR and NAND
Truth tables explain the Boolean functions implemented by the gates
[Speaker Notes: Notes area]

---
Digital Logic Basics
Flip-flop – has 2 stable states
Sequential logic – built on flip-flops feeding other flip-flops (used in counters)
Example: a 3-bit counter (one with 3 flip-flops) can count 23 = 8 different states
Example: a 4-bit counter (one with 4 flip-flops) can count 24 = 16 different states
Shift register – a clocked array of circuits that passes data in steps along the array
[Speaker Notes: Called flip-flops because the output jumps from one state to the other based on input signals.]

---
RF Integrated Circuits
RF ICs are designed for functions commonly used for radio frequencies
Low-level high-gain amplifiers
Mixers
Modulators and demodulators
Filters
MMIC (monolithic microwave integrated circuit) works through microwave frequencies
[Speaker Notes: Notes area]

---
Microprocessors & Components
A microprocessor is a computer on a single Integrated Circuit
Capable of performing billions of instructions per second using combinations of digital logic gates
Has parallel and serial input-output ports, counters and timers
Nearly all built from CMOS logic
[Speaker Notes: Notes area]

---
Microprocessor Components
Memory:
Volatile memory loses the data stored when power is removed
Nonvolatile memory retains data permanently even when power is off
Random-access memory (RAM) can be read or written to in any order
Read-only memory (ROM) stores data permanently and can’t be changed
[Speaker Notes: Notes area]

---
Microprocessor Components
Interfaces:
Serial interface transfers one bit of data in each transfer
Parallel interface transfers multiple bits of data in each operation
RS-232 serial interface is rapidly being replaced by USB (universal serial bus) serial interface
Modern computers don’t have RS-232 ports, so use the USB port and RS-232 converter to interface them to your transceiver
[Speaker Notes: Notes area]

---
Microprocessor Components
Visual Interfaces:
Indicator – device that presents ON/OFF information (LED)
Display – device capable of presenting text or graphics in visual form
An LED is a special diode that produces light when it is forward biased
LEDs are available in several different colors, including white
LEDs have replaced incandescent light bulbs because they last longer and react faster
[Speaker Notes: Notes area]

---
Microprocessor Components
Liquid crystal display (LCD) – created by sandwiching liquid crystal material between transparent glass panels
When voltage is applied to the electrodes on the front panel, the liquid crystals twist and block the light
LCDs require ambient or back lighting since the liquid crystal layer does not generate light
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is the approximate junction threshold voltage of a germanium diode?
What is the approximate junction threshold voltage of a germanium diode?
A. 0.1 volt
B. 0.3 volts
C. 0.7 volts
D. 1.0 volts
  G6A03

---
What is the approximate junction threshold voltage of a germanium diode?
A. 0.1 volt
B. 0.3 volts
C. 0.7 volts
D. 1.0 volts
  G6A03

---
What is the approximate junction threshold voltage of a conventional silicon diode?
What is the approximate junction threshold voltage of a conventional silicon diode?
A. 0.1 volt
B. 0.3 volts
C. 0.7 volts
D. 1.0 volts
  G6A05

---
What is the approximate junction threshold voltage of a conventional silicon diode?
A. 0.1 volt
B. 0.3 volts
C. 0.7 volts
D. 1.0 volts
  G6A05

---
Which of the following is an advantage of using a Schottky diode in an RF switching circuit rather than a standard silicon diode?
Which of the following is an advantage of using a Schottky diode in an RF switching circuit rather than a standard silicon diode?
A. Lower capacitance
B. Lower inductance
C. Longer switching times
D. Higher breakdown voltage
  G6A06

---
Which of the following is an advantage of using a Schottky diode in an RF switching circuit rather than a standard silicon diode?
A. Lower capacitance
B. Lower inductance
C. Longer switching times
D. Higher breakdown voltage
  G6A06

---
What are the stable operating points for a bipolar transistor used as a switch in a logic circuit?
What are the stable operating points for a bipolar transistor used as a switch in a logic circuit?
A. Its saturation and cutoff regions
B. Its active region (between the cutoff and saturation regions)
C. Its peak and valley current points
D. Its enhancement and depletion modes
  G6A07

---
What are the stable operating points for a bipolar transistor used as a switch in a logic circuit?
A. Its saturation and cutoff regions
B. Its active region (between the cutoff and saturation regions)
C. Its peak and valley current points
D. Its enhancement and depletion modes
  G6A07

---
Why must the cases of some large power transistors be insulated from ground?
Why must the cases of some large power transistors be insulated from ground?
A. To increase the beta of the transistor
B. To improve the power dissipation capability
C. To reduce stray capacitance
D. To avoid shorting the collector or drain voltage to ground
  G6A08

---
Why must the cases of some large power transistors be insulated from ground?
A. To increase the beta of the transistor
B. To improve the power dissipation capability
C. To reduce stray capacitance
D. To avoid shorting the collector or drain voltage to ground
  G6A08

---
Which of the following describes the construction of a MOSFET?
Which of the following describes the construction of a MOSFET?
A. The gate is formed by a back-biased junction
B. The gate is separated from the channel with a thin insulating layer
C. The source is separated from the drain by a thin insulating layer
D. The source is formed by depositing metal on silicon
  G6A09

---
Which of the following describes the construction of a MOSFET?
A. The gate is formed by a back-biased junction
B. The gate is separated from the channel with a thin insulating layer
C. The source is separated from the drain by a thin insulating layer
D. The source is formed by depositing metal on silicon
  G6A09

---
Which element of a triode vacuum tube is used to regulate the flow of electrons between cathode and plate?
Which element of a triode vacuum tube is used to regulate the flow of electrons between cathode and plate?
A. Control grid
B. Heater
C. Screen Grid
D. Trigger electrode
  G6A10

---
Which element of a triode vacuum tube is used to regulate the flow of electrons between cathode and plate?
A. Control grid
B. Heater
C. Screen Grid
D. Trigger electrode
  G6A10

---
Which of the following solid state devices is most like a vacuum tube in its general operating characteristics?
Which of the following solid state devices is most like a vacuum tube in its general operating characteristics?
A. A bipolar transistor
B. A field effect transistor
C. A tunnel diode
D. A varistor
  G6A11

---
Which of the following solid state devices is most like a vacuum tube in its general operating characteristics?
A. A bipolar transistor
B. A field effect transistor
C. A tunnel diode
D. A varistor
  G6A11

---
What is the primary purpose of a screen grid in a vacuum tube?
What is the primary purpose of a screen grid in a vacuum tube?
A. To reduce grid-to-plate capacitance
B. To increase efficiency
C. To increase the control grid resistance
D. To decrease plate resistance
  G6A12

---
What is the primary purpose of a screen grid in a vacuum tube?
A. To reduce grid-to-plate capacitance
B. To increase efficiency
C. To increase the control grid resistance
D. To decrease plate resistance
  G6A12

---
Which of the following is an analog integrated circuit?
Which of the following is an analog integrated circuit?
A. NAND Gate
B. Microprocessor
C. Frequency Counter
D. Linear voltage regulator
  G6B01

---
Which of the following is an analog integrated circuit?
A. NAND Gate
B. Microprocessor
C. Frequency Counter
D. Linear voltage regulator
  G6B01

---
What is meant by the term MMIC?
What is meant by the term MMIC?
A. Multi Megabyte Integrated Circuit
B. Monolithic Microwave Integrated Circuit
C. Military Manufactured Integrated Circuit
D. Mode Modulated Integrated Circuit
  G6B02

---
What is meant by the term MMIC?
A. Multi Megabyte Integrated Circuit
B. Monolithic Microwave Integrated Circuit
C. Military Manufactured Integrated Circuit
D. Mode Modulated Integrated Circuit
  G6B02

---
Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits?
Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits?
A. Low power consumption
B. High power handling capability
C. Better suited for RF amplification
D. Better suited for power supply regulation
  G6B03

---
Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits?
A. Low power consumption
B. High power handling capability
C. Better suited for RF amplification
D. Better suited for power supply regulation
  G6B03

---
What is meant by the term ROM?
What is meant by the term ROM?
A. Resistor Operated Memory
B. Read Only Memory
C. Random Operational Memory
D. Resistant to Overload Memory
  G6B04

---
What is meant by the term ROM?
A. Resistor Operated Memory
B. Read Only Memory
C. Random Operational Memory
D. Resistant to Overload Memory
  G6B04

---
What is meant when memory is characterized as non-volatile?
What is meant when memory is characterized as non-volatile?
A. It is resistant to radiation damage
B. It is resistant to high temperatures
C. The stored information is maintained even if power is removed
D. The stored information cannot be changed once written
  G6B05

---
What is meant when memory is characterized as non-volatile?
A. It is resistant to radiation damage
B. It is resistant to high temperatures
C. The stored information is maintained even if power is removed
D. The stored information cannot be changed once written
  G6B05

---
What kind of device is an integrated circuit operational amplifier?
What kind of device is an integrated circuit operational amplifier?
A. Digital
B. MMIC
C. Programmable Logic
D. Analog
  G6B06

---
What kind of device is an integrated circuit operational amplifier?
A. Digital
B. MMIC
C. Programmable Logic
D. Analog
  G6B06

---
Which of the following is an advantage of an LED indicator compared to an incandescent indicator?
Which of the following is an advantage of an LED indicator compared to an incandescent indicator?
A. Lower power consumption
B. Faster response time
C. Longer life
D. All of these choices are correct
  G6B07

---
Which of the following is an advantage of an LED indicator compared to an incandescent indicator?
A. Lower power consumption
B. Faster response time
C. Longer life
D. All of these choices are correct
  G6B07

---
How is an LED biased when emitting light?
How is an LED biased when emitting light?
A. Beyond cutoff
B. At the Zener voltage
C. Reverse Biased
D. Forward Biased
  G6B08

---
How is an LED biased when emitting light?
A. Beyond cutoff
B. At the Zener voltage
C. Reverse Biased
D. Forward Biased
  G6B08

---
Which of the following is a characteristic of a liquid crystal display?
Which of the following is a characteristic of a liquid crystal display?
A. It requires ambient or back lighting
B. It offers a wide dynamic range
C. It has a wide viewing angle
D. All of these choices are correct
  G6B09

---
Which of the following is a characteristic of a liquid crystal display?
A. It requires ambient or back lighting
B. It offers a wide dynamic range
C. It has a wide viewing angle
D. All of these choices are correct
  G6B09

---
What two devices in an Amateur Radio station might be connected using a USB interface?
What two devices in an Amateur Radio station might be connected using a USB interface?
A. Computer and transceiver
B. Microphone and transceiver
C. Amplifier and antenna
D. Power supply and amplifier
  G6B10

---
What two devices in an Amateur Radio station might be connected using a USB interface?
A. Computer and transceiver
B. Microphone and transceiver
C. Amplifier and antenna
D. Power supply and amplifier
  G6B10

---
What is a microprocessor?
What is a microprocessor?
A. A low power analog signal processor used as a microwave detector
B. A computer on a single integrated circuit
C. A microwave detector, amplifier, and local oscillator on a single integrated circuit
D. A low voltage amplifier used in a microwave transmitter modulator stage
  G6B11

---
What is a microprocessor?
A. A low power analog signal processor used as a microwave detector
B. A computer on a single integrated circuit
C. A microwave detector, amplifier, and local oscillator on a single integrated circuit
D. A low voltage amplifier used in a microwave transmitter modulator stage
  G6B11

---
Complex digital circuitry can often be replaced by what type of integrated circuit?
Complex digital circuitry can often be replaced by what type of integrated circuit?
A. Microcontroller
B. Charge-coupled device
C. Phase detector
D. Window comparator
  G7B01

---
Complex digital circuitry can often be replaced by what type of integrated circuit?
A. Microcontroller
B. Charge-coupled device
C. Phase detector
D. Window comparator
  G7B01

---
Which of the following is an advantage of using the binary system when processing digital signals?
Which of the following is an advantage of using the binary system when processing digital signals?
A. Binary “ones” and “zeros” are easy to represent by an “on” or “off” state
B. The binary number system is most accurate
C. Binary numbers are more compatible with analog circuitry
D. All of these choices are correct
  G7B02

---
Which of the following is an advantage of using the binary system when processing digital signals?
A. Binary “ones” and “zeros” are easy to represent by an “on” or “off” state
B. The binary number system is most accurate
C. Binary numbers are more compatible with analog circuitry
D. All of these choices are correct
  G7B02

---
Which of the following describes the function of a two input AND gate?
Which of the following describes the function of a two input AND gate?
A. Output is high when either or both inputs are low
B. Output is high only when both inputs are high
C. Output is low when either or both inputs are high
D. Output is low only when both inputs are high
  G7B03

---
Which of the following describes the function of a two input AND gate?
A. Output is high when either or both inputs are low
B. Output is high only when both inputs are high
C. Output is low when either or both inputs are high
D. Output is low only when both inputs are high
  G7B03

---
Which of the following describes the function of a two input NOR gate?
Which of the following describes the function of a two input NOR gate?
A. Output is high when either or both inputs are low
B. Output is high only when both inputs are high
C. Output is low when either or both inputs are high
D. Output is low only when both inputs are high
  G7B04

---
Which of the following describes the function of a two input NOR gate?
A. Output is high when either or both inputs are low
B. Output is high only when both inputs are high
C. Output is low when either or both inputs are high
D. Output is low only when both inputs are high
  G7B04

---
How many states does a 3-bit binary counter have?
How many states does a 3-bit binary counter have?
A. 3
B. 6
C. 8
D. 16
  G7B05

---
How many states does a 3-bit binary counter have?
A. 3
B. 6
C. 8
D. 16
  G7B05

---
What is a shift register?
What is a shift register?
A. A clocked array of circuits that passes data in steps along the array
B. An array of operational amplifiers used for tri-state arithmetic operations
C. A digital mixer
D. An analog mixer
  G7B06

---
What is a shift register?
A. A clocked array of circuits that passes data in steps along the array
B. An array of operational amplifiers used for tri-state arithmetic operations
C. A digital mixer
D. An analog mixer
  G7B06

---
General License Course
Chapter 4
Lesson Plan Module 15 –
Practical Circuits

---
Rectifiers
Half-wave rectifier
allows current to flow
in one-half of the input
ac waveform (180°)
from the transformer,
as shown in “A”
Full-wave center-
trapped rectifier
two half-wave
rectifiers operating on
alternating half cycles, as shown in “B”, using the transformer center tap for the current’s return path
[Speaker Notes: Observe that different rectifier circuits are chosen based on cost, component rating, and output load.]

---
Rectifiers
Full Wave Rectifier Circuits
Advantage – output is
produced during entire
360° of the ac cycle
Output is a series of
pulses at twice the
frequency of the
input voltage
Full-wave bridge
rectifier – uses a pair
of diodes on alternating
ac cycle halves
[Speaker Notes: The full-wave’s output waveform is easier to filter to smooth dc voltage.]

---
Rectifiers
Full-wave bridge
rectifier
Diodes
only have to
withstand the
full supply output
voltage
Each diode carries
the full load current.
[Speaker Notes: Lesson plan should say that in the full-wave center-tapped rectifier, each diode carries one-half the load current. In the full-wave bridge rectifier, each diode carries the full load current.]

---
Rectifiers
Peak inverse voltage in a half-wave rectifier is twice the supply output voltage
Half-wave rectifier – the entire load current goes through one diode
[Speaker Notes: Notes area]

---
Filter Circuits
Rectifier’s pulsed output is unusable as dc
Filter networks – made up of capacitors and inductors, smooth out the ripple
Common method to smooth the ripple in a linear supply is a large electrolytic capacitor
Regulation – the percent variation in output voltage between no load and full load
Inductor-input or choke-input – uses an inductor to smooth current pulses with a capacitor so smooth voltage.
[Speaker Notes: Explain what a linear supply is and that switching supplies will be covered in a few slides.]

---
Power Supplies
Power supply safety:
Fuses in the primary are used to protect against short circuits or excessive current
Bleeder resistors discharge stored energy when the supply is turned off
Working on power supplies – wait for the bleeder resistor to discharge energy, even if it is unplugged
[Speaker Notes: Notes area]

---
Power Supplies
Switching or Switchmode supplies:
Transistors switch current pulses at a high frequency (20 kHz or more) through a transformer and/or inductor then a capacitor filters the voltage
The high frequency allows lightweight inductors and transformers to be used
Linear supplies are very heavy due to their large, iron-core power transformer
[Speaker Notes: Notes area]

---
Batteries
Large marine or RV storage batteries are often used as emergency backup power supplies
Liquid-electrolyte or gel-electrolyte batteries are rated at 12 V but should be maintained at 13.8 V
Lead-acid batteries are useful until their output drops to 10.5 V
Discharging batteries past their minimum voltage will reduce the life of the battery
[Speaker Notes: Notes area]

---
Batteries
[Speaker Notes: Notes area]

---
Batteries
NiCds (or Nicads) – designed to have low internal resistance to supply high discharge currents for tools and transmitters
Battery self-discharge gradually reduces stored energy over time
Slow by storage in a cool and dry place
Freezing will damage batteries with liquid or gel electrolytes
[Speaker Notes: Some batteries are designed for very low-temperature use. Check the battery temperature rating if this might be a problem.]

---
Charging Batteries
Different types of batteries require different charging methods
Use the proper type of charger to maximize the life and usefulness of the battery
Never attempt to recharge a carbon-zinc, alkaline, or silver-nickel type battery (chemical reaction can not be reversed)
[Speaker Notes: Using the wrong type of charger can damage the battery. For more information about batteries in general, recommend the Battery University website.]

---
Alternative Power
Solar Power – photovoltaic conversion of sunlight directly to electricity
Solar cells are a special type of diode
The forward voltage created as the electrons cross the junction is approximately 0.5 V dc (open circuit voltage)
Individual solar cells can be connected in series to create higher voltages (24 cells to create 12 V)
Wind generators use dc generators connected to propellers that spin them
[Speaker Notes: Solar panels are composed of multiple solar cells connected in series-parallel combination so that the output voltage is 12 V.]

---
Energy Storage
Wind and solar power require a substantial energy storage system
No wind or sun means no power
Excess power needs to be stored during peak periods of generation (batteries are the most common method)
Diodes prevent the batteries from discharging back through the solar panels
[Speaker Notes: Notes area]

---
Connectors
Keyed connectors only mate one way, reducing the possibility of damage
Plugs are installed on cables
Jacks are installed on equipment
Adaptors make connections between different style connectors
Splitters divide a signal between two connectors
[Speaker Notes: Notes area]

---
Power Connectors
Anderson Powerpole® connectors have become the standard for radio equipment used by ARES
[Speaker Notes: Molex connectors are also common, particularly on transceivers. Crimp pins are installed on the end of wires and then inserted into the body of the connector. A crimping tool suitable for the pin is required to make a reliable crimp – do not use pliers or some other gripping tool. Terminal strips are also used for wires terminated with fork or ring crimp terminals. Show examples of the different types of terminals and crimping tools.]

---
Audio Connectors
Consumer electronics and Amateur Radio share many of the same connectors
[Speaker Notes: Show examples of the different connector types.]

---
Audio Connectors
Contact tip is the end of the plug
The sleeve is the base of the plug
The ring is a third contact between the tip and sleeve
Phono plugs are often called RCA connectors (commonly used for audio signals)
DIN or mini-DIN connectors are keyed and have up to 9 pins and are used to control multiple circuits on radio equipment
[Speaker Notes: Show examples of the connectors. Point out the difference between mono and stereo phone plugs. Show the 1/8” and ¼” styles.]

---
RF Connectors
[Speaker Notes: Show UHF, N, and SMA connectors. Ask the students what kind of connector their handheld or mobile radios have. Show common adaptors.]

---
RF Connectors
Special RF feed line connectors:
UHF connectors (SO-239 & PL-259) can be used up to 150 MHz
“N” connectors are moisture resistant and used up to 10 GHz
SMA connectors are small threaded connectors designed for miniature coaxial cable and are rated up to 18 GHz
Used on many hand-held radios
[Speaker Notes: Notes area]

---
Data Connectors
Digital data is exchanged between the computers and amateur radios:
D-type connectors are used for RS-232 (COM ports) and parallel ports
D-type 9-pin connector is referred to as DB-9 or DE-9 (commonly used for serial ports)
25-pin D-type connector for parallel ports
USB ports are standard for current computers
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is the name of the process by which sunlight is changed directly into electricity?
What is the name of the process by which sunlight is changed directly into electricity?
A. Photovoltaic conversion
B. Photon emission
C. Photosynthesis
D. Photon decomposition
  G4E08

---
What is the name of the process by which sunlight is changed directly into electricity?
A. Photovoltaic conversion
B. Photon emission
C. Photosynthesis
D. Photon decomposition
  G4E08

---
What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
A. 0.02 VDC
B. 0.5 VDC
C. 0.2 VDC
D. 1.38 VDC
  G4E09

---
What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
A. 0.02 VDC
B. 0.5 VDC
C. 0.2 VDC
D. 1.38 VDC
  G4E09

---
What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel?
What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel?
A. The diode serves to regulate the charging voltage to prevent overcharge
B. The diode prevents self-discharge of the battery though the panel during times of low or no illumination
C. The diode limits the current flowing from the panel to a safe value
D. The diode greatly increases the efficiency during times of high illumination
  G4E10

---
What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel?
A. The diode serves to regulate the charging voltage to prevent overcharge
B. The diode prevents self-discharge of the battery though the panel during times of low or no illumination
C. The diode limits the current flowing from the panel to a safe value
D. The diode greatly increases the efficiency during times of high illumination
  G4E10

---
Which of the following is a disadvantage of using wind as the primary source of power for an emergency station?
Which of the following is a disadvantage of using wind as the primary source of power for an emergency station?
A. The conversion efficiency from mechanical energy to electrical energy is less than 2 percent
B. The voltage and current ratings of such systems are not compatible with amateur equipment
C. A large energy storage system is needed to supply power when the wind is not blowing
D. All of these choices are correct
  G4E11

---
Which of the following is a disadvantage of using wind as the primary source of power for an emergency station?
A. The conversion efficiency from mechanical energy to electrical energy is less than 2 percent
B. The voltage and current ratings of such systems are not compatible with amateur equipment
C. A large energy storage system is needed to supply power when the wind is not blowing
D. All of these choices are correct
  G4E11

---
What is the minimum allowable discharge voltage for maximum life of a standard 12 volt lead acid battery?
What is the minimum allowable discharge voltage for maximum life of a standard 12 volt lead acid battery?
A. 6 volts
B. 8.5 volts
C. 10.5 volts
D. 12 volts
  G6A01

---
What is the minimum allowable discharge voltage for maximum life of a standard 12 volt lead acid battery?
A. 6 volts
B. 8.5 volts
C. 10.5 volts
D. 12 volts
  G6A01

---
What is an advantage of the low internal resistance of nickel-cadmium batteries?
What is an advantage of the low internal resistance of nickel-cadmium batteries?
A. Long life
B. High discharge current
C. High voltage
D. Rapid recharge
  G6A02

---
What is an advantage of the low internal resistance of nickel-cadmium batteries?
A. Long life
B. High discharge current
C. High voltage
D. Rapid recharge
  G6A02

---
When is it acceptable to recharge a carbon-zinc primary cell?
When is it acceptable to recharge a carbon-zinc primary cell?
A. As long as the voltage has not been allowed to drop below 1.0 volt
B. When the cell is kept warm during the recharging period
C. When a constant current charger is used
D. Never
  G6A04

---
When is it acceptable to recharge a carbon-zinc primary cell?
A. As long as the voltage has not been allowed to drop below 1.0 volt
B. When the cell is kept warm during the recharging period
C. When a constant current charger is used
D. Never
  G6A04

---
Which of the following connectors would be a good choice for a serial data port?
Which of the following connectors would be a good choice for a serial data port?
A. PL-259
B. Type N
C. Type SMA
D. DE-9
  G6B12

---
Which of the following connectors would be a good choice for a serial data port?
A. PL-259
B. Type N
C. Type SMA
D. DE-9
  G6B12

---
Which of these connector types is commonly used for RF connections at frequencies up to 150 MHz?
Which of these connector types is commonly used for RF connections at frequencies up to 150 MHz?
A. Octal
B. RJ-11
C. PL-259
D. DB-25
  G6B13

---
Which of these connector types is commonly used for RF connections at frequencies up to 150 MHz?
A. Octal
B. RJ-11
C. PL-259
D. DB-25
  G6B13

---
Which of these connector types is commonly used for audio signals in Amateur Radio stations?
Which of these connector types is commonly used for audio signals in Amateur Radio stations?
A. PL-259
B. BNC
C. RCA Phono
D. Type N
  G6B14

---
Which of these connector types is commonly used for audio signals in Amateur Radio stations?
A. PL-259
B. BNC
C. RCA Phono
D. Type N
  G6B14

---
What is the main reason to use keyed connectors instead of non-keyed types?
What is the main reason to use keyed connectors instead of non-keyed types?
A. Prevention of use by unauthorized persons
B. Reduced chance of incorrect mating
C. Higher current carrying capacity
D. All of these choices are correct
  G6B15

---
What is the main reason to use keyed connectors instead of non-keyed types?
A. Prevention of use by unauthorized persons
B. Reduced chance of incorrect mating
C. Higher current carrying capacity
D. All of these choices are correct
  G6B15

---
Which of the following describes a type N connector?
Which of the following describes a type N connector?
A. A moisture-resistant RF connector useful to 10 GHz
B. A small bayonet connector used for data circuits
C. A threaded connector used for hydraulic systems
D. An audio connector used in surround-sound installations
  G6B16

---
Which of the following describes a type N connector?
A. A moisture-resistant RF connector useful to 10 GHz
B. A small bayonet connector used for data circuits
C. A threaded connector used for hydraulic systems
D. An audio connector used in surround-sound installations
  G6B16

---
What is the general description of a DIN type connector?
What is the general description of a DIN type connector?
A. A special connector for microwave interfacing
B. A DC power connector rated for currents between 30 and 50 amperes
C. A family of multiple circuit connectors suitable for audio and control signals
D. A special watertight connector for use in marine applications
  G6B17

---
What is the general description of a DIN type connector?
A. A special connector for microwave interfacing
B. A DC power connector rated for currents between 30 and 50 amperes
C. A family of multiple circuit connectors suitable for audio and control signals
D. A special watertight connector for use in marine applications
  G6B17

---
What is a type SMA connector?
What is a type SMA connector?
A. A large bayonet connector usable at power levels in excess of 1 KW
B. A small threaded connector suitable for signals up to several GHz
C. A connector designed for serial multiple access signals
D. A type of push-on connector intended for high voltage applications
  G6B18

---
What is a type SMA connector?
A. A large bayonet connector usable at power levels in excess of 1 KW
B. A small threaded connector suitable for signals up to several GHz
C. A connector designed for serial multiple access signals
D. A type of push-on connector intended for high voltage applications
  G6B18

---
What useful feature does a power supply bleeder resistor provide?
What useful feature does a power supply bleeder resistor provide?
A. It acts as a fuse for excess voltage
B. It ensures that the filter capacitors are discharged when power is removed
C. It removes shock hazards from the induction coils
D. It eliminates ground loop current
  G7A01

---
What useful feature does a power supply bleeder resistor provide?
A. It acts as a fuse for excess voltage
B. It ensures that the filter capacitors are discharged when power is removed
C. It removes shock hazards from the induction coils
D. It eliminates ground loop current
  G7A01

---
Which of the following components are used in a power supply filter network?
Which of the following components are used in a power supply filter network?
A. Diodes
B. Transformers and transducers
C. Quartz crystals
D. Capacitors and inductors
  G7A02

---
Which of the following components are used in a power supply filter network?
A. Diodes
B. Transformers and transducers
C. Quartz crystals
D. Capacitors and inductors
  G7A02

---
What is the peak-inverse-voltage across the rectifiers in a full-wave bridge power supply?
What is the peak-inverse-voltage across the rectifiers in a full-wave bridge power supply?
A. One-quarter the normal output voltage of the power supply
B. Half the normal output voltage of the power supply
C. Double the normal peak output voltage of the power supply
D. Equal to the normal peak output voltage of the power supply
  G7A03

---
What is the peak-inverse-voltage across the rectifiers in a full-wave bridge power supply?
A. One-quarter the normal output voltage of the power supply
B. Half the normal output voltage of the power supply
C. Double the normal peak output voltage of the power supply
D. Equal to the normal peak output voltage of the power supply
  G7A03

---
What is the peak-inverse-voltage across the rectifier in a half-wave power supply?
What is the peak-inverse-voltage across the rectifier in a half-wave power supply?
A. One-half the normal peak output voltage of the power supply
B. One-half the normal output voltage of the power supply
C. Equal to the normal output voltage of the power supply
D. Two times the normal peak output voltage of the power supply
  G7A04

---
What is the peak-inverse-voltage across the rectifier in a half-wave power supply?
A. One-half the normal peak output voltage of the power supply
B. One-half the normal output voltage of the power supply
C. Equal to the normal output voltage of the power supply
D. Two times the normal peak output voltage of the power supply
  G7A04

---
What portion of the AC cycle is converted to DC by a half-wave rectifier?
What portion of the AC cycle is converted to DC by a half-wave rectifier?
A. 90 degrees
B. 180 degrees
C. 270 degrees
D. 360 degrees
  G7A05

---
What portion of the AC cycle is converted to DC by a half-wave rectifier?
A. 90 degrees
B. 180 degrees
C. 270 degrees
D. 360 degrees
  G7A05

---
What portion of the AC cycle is converted to DC by a full-wave rectifier?
What portion of the AC cycle is converted to DC by a full-wave rectifier?
A. 90 degrees
B. 180 degrees
C. 270 degrees
D. 360 degrees
  G7A06

---
What portion of the AC cycle is converted to DC by a full-wave rectifier?
A. 90 degrees
B. 180 degrees
C. 270 degrees
D. 360 degrees
  G7A06

---
What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
A. A series of DC pulses at twice the frequency of the AC input
B. A series of DC pulses at the same frequency as the AC input
C. A sine wave at half the frequency of the AC input
D. A steady DC voltage
  G7A07

---
What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
A. A series of DC pulses at twice the frequency of the AC input
B. A series of DC pulses at the same frequency as the AC input
C. A sine wave at half the frequency of the AC input
D. A steady DC voltage
  G7A07

---
Which of the following is an advantage of a switchmode power supply as compared to a linear power supply?
Which of the following is an advantage of a switchmode power supply as compared to a linear power supply?
A. Faster switching time makes higher output voltage possible
B. Fewer circuit components are required
C. High frequency operation allows the use of smaller components
D. All of these choices are correct
  G7A08

---
Which of the following is an advantage of a switchmode power supply as compared to a linear power supply?
A. Faster switching time makes higher output voltage possible
B. Fewer circuit components are required
C. High frequency operation allows the use of smaller components
D. All of these choices are correct
  G7A08

---
General License Course
Chapter 4
Lesson Plan Module 16 –
Basic Test Equipment

---
Analog & Digital Meters
Volt-ohm meter (VOM) is the simplest piece of test equipment
Measures – volts, current, resistance
Tests – continuity, diodes, transistors
Two types of VOM – Analog and Digital
Analog meters have a moving needle and calibrated scales on the meter face
Analog meters are useful for finding a peak or minimum reading, such as when adjusting a tuned circuit
[Speaker Notes: Have an analog and digital multimeter available to illustrate the differences.]

---
Analog & Digital Meters
Digital meters (DDMs) offer significantly greater precision than analog meters
Digital meters have useful features:
auto-ranging to automatically select the proper display range
peak hold to capture maximum values
When measuring voltage, the meter should have a high input impedance to place the minimum load on the circuit being measured
[Speaker Notes: Explain that loading the circuit will cause measurement errors.]

---
Oscilloscope
The oscilloscope (or “scope”) provides a visual display of voltage against time
Updated rapidly enough to give a real-time picture of the signal
Fast-changing complex waveforms can be measured
External signals are connected to horizontal and vertical channel inputs to control the display
Variable gain and update rates are available to display many types of signals.
[Speaker Notes: Explain that older scopes use a CRT like an older TV. New scopes use LCD technology like TVs and computer monitors. Some scopes use a PC for their displays. Explain what a “time base” is and if a scope is available, show the measuring graticule and gain/speed controls.]

---
Monitoring Oscilloscope
The transmitter’s attenuated output connects to the vertical channel of the oscilloscope to monitor the signal
Monitoring helps adjust keying waveforms, mic gain, and speech processing
The scope shows the effects of any adjustments that might cause distortion
A scope provides information that numeric meters can’t measure.
[Speaker Notes: Notes area]

---
Impedance & Resonance Measurement
An antenna analyzer contains a CW signal generator, frequency counter, SWR bridge, and impedance meter
Connects to the antenna feed line to measure SWR using very small signals for measurements
Impedance measurements show resonance
Measures feed line velocity factor, electrical length, and characteristic impedance
Can be affected by strong nearby signals
[Speaker Notes: Have an analyzer available for demonstration. Show SWR, impedance, and resonance measurements.]

---
Field Strength & Power Meters
Field strength meters measure the electrical field of transmitted signals
Field strength meters can be used during antenna and transmitter adjustments
Field strength meters can be used to measure antenna radiation patterns
Standing wave ratio (SWR) can be measured from forward and reflected power measurements made with a directional wattmeter
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What item of test equipment contains horizontal and vertical channel amplifiers?
What item of test equipment contains horizontal and vertical channel amplifiers?
A. An ohmmeter
B. A signal generator
C. An ammeter
D. An oscilloscope
  G4B01

---
What item of test equipment contains horizontal and vertical channel amplifiers?
A. An ohmmeter
B. A signal generator
C. An ammeter
D. An oscilloscope
  G4B01

---
Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
A. An oscilloscope uses less power
B. Complex impedances can be easily measured
C. Input impedance is much lower
D. Complex waveforms can be measured
  G4B02

---
Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
A. An oscilloscope uses less power
B. Complex impedances can be easily measured
C. Input impedance is much lower
D. Complex waveforms can be measured
  G4B02

---
Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter?
Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter?
A. An oscilloscope
B. A field strength meter
C. A sidetone monitor
D. A wavemeter
  G4B03

---
Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter?
A. An oscilloscope
B. A field strength meter
C. A sidetone monitor
D. A wavemeter
  G4B03

---
What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
A. The local oscillator of the transmitter
B. An external RF oscillator
C. The transmitter balanced mixer output
D. The attenuated RF output of the transmitter
  G4B04

---
What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
A. The local oscillator of the transmitter
B. An external RF oscillator
C. The transmitter balanced mixer output
D. The attenuated RF output of the transmitter
  G4B04

---
Why is high input impedance desirable for a voltmeter?
Why is high input impedance desirable for a voltmeter?
A. It improves the frequency response
B. It decreases battery consumption in the meter
C. It improves the resolution of the readings
D. It decreases the loading on circuits being measured
  G4B05

---
Why is high input impedance desirable for a voltmeter?
A. It improves the frequency response
B. It decreases battery consumption in the meter
C. It improves the resolution of the readings
D. It decreases the loading on circuits being measured
  G4B05

---
What is an advantage of a digital voltmeter as compared to an analog voltmeter?
What is an advantage of a digital voltmeter as compared to an analog voltmeter?
A. Better for measuring computer circuits
B. Better for RF measurements
C. Better precision for most uses
D. Faster response
  G4B06

---
What is an advantage of a digital voltmeter as compared to an analog voltmeter?
A. Better for measuring computer circuits
B. Better for RF measurements
C. Better precision for most uses
D. Faster response
  G4B06

---
Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments?
Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments?
A. A field strength meter
B. An antenna noise bridge
C. A multimeter
D. A Q meter
  G4B08

---
Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments?
A. A field strength meter
B. An antenna noise bridge
C. A multimeter
D. A Q meter
  G4B08

---
Which of the following can be determined with a field strength meter?
Which of the following can be determined with a field strength meter?
A. The radiation resistance of an antenna
B. The radiation pattern of an antenna
C. The presence and amount of phase distortion of a transmitter
D. The presence and amount of amplitude distortion of a transmitter
  G4B09

---
Which of the following can be determined with a field strength meter?
A. The radiation resistance of an antenna
B. The radiation pattern of an antenna
C. The presence and amount of phase distortion of a transmitter
D. The presence and amount of amplitude distortion of a transmitter
  G4B09

---
Which of the following can be determined with a directional wattmeter?
Which of the following can be determined with a directional wattmeter?
A. Standing wave ratio
B. Antenna front-to-back ratio
C. RF interference
D. Radio wave propagation
  G4B10

---
Which of the following can be determined with a directional wattmeter?
A. Standing wave ratio
B. Antenna front-to-back ratio
C. RF interference
D. Radio wave propagation
  G4B10

---
Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
A. Receiver
B. Transmitter
C. Antenna and feed line
D. All of these choices are correct
  G4B11

---
Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
A. Receiver
B. Transmitter
C. Antenna and feed line
D. All of these choices are correct
  G4B11

---
What problem can occur when making measurements on an antenna system with an antenna analyzer?
What problem can occur when making measurements on an antenna system with an antenna analyzer?
A. Permanent damage to the analyzer may occur if it is operated into a high SWR
B. Strong signals from nearby transmitters can affect the accuracy of measurements
C. The analyzer can be damaged if measurements outside the ham bands are attempted
D. Connecting the analyzer to an antenna can cause it to absorb harmonics
  G4B12

---
What problem can occur when making measurements on an antenna system with an antenna analyzer?
A. Permanent damage to the analyzer may occur if it is operated into a high SWR
B. Strong signals from nearby transmitters can affect the accuracy of measurements
C. The analyzer can be damaged if measurements outside the ham bands are attempted
D. Connecting the analyzer to an antenna can cause it to absorb harmonics
  G4B12

---
What is a use for an antenna analyzer other than measuring the SWR of an antenna system?
What is a use for an antenna analyzer other than measuring the SWR of an antenna system?
A. Measuring the front to back ratio of an antenna
B. Measuring the turns ratio of a power transformer
C. Determining the impedance of an unknown or unmarked coaxial cable
D. Determining the gain of a directional antenna
  G4B13

---
What is a use for an antenna analyzer other than measuring the SWR of an antenna system?
A. Measuring the front to back ratio of an antenna
B. Measuring the turns ratio of a power transformer
C. Determining the impedance of an unknown or unmarked coaxial cable
D. Determining the gain of a directional antenna
  G4B13

---
What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout?
What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout?
A. When testing logic circuits
B. When high precision is desired
C. When measuring the frequency of an oscillator
D. When adjusting tuned circuits
  G4B14

---
What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout?
A. When testing logic circuits
B. When high precision is desired
C. When measuring the frequency of an oscillator
D. When adjusting tuned circuits
  G4B14