General License Course Chapter 6
General License Course
Chapter 6
Lesson Plan Module 22 –
Introduction to Digital Modes

---
Finding Digital Activity
Where to Find Digital Signals on the HF Bands
Band	Notes
(Meters)	(MHz)
160	1.800 - 1.810
80	3.570 - 3.600
60	Data emission not permitted
40	7.080 - 7.125 RTTY DX calling frequency 7.040 MHz
30	10.130 - 10.150
20	14.070 - 14.0995 and 14.1005 - 14.112 PSK31	calling frequency 14.070 MHz
17	18.100 - 18.110
15	21.070 - 21.110
12	24.920 - 24.930
10	28.070 - 28.150
2015 General License Course
[Speaker Notes: Remind students this is a band plan, not a regulation. Note that rule changes have been proposed and are under evaluation by the FCC. Watch the ARRL website for updates and more information.]

---
Digital Modes
Digital voice modes are regulated as voice emissions by the FCC
Icom’s D-STAR, Yaesu’s SystemFusion, AOR’s digital voice, WinDRM, FreeDV
Slow-scan TV (SSTV) is also regulated as an image mode on both HF and VHF/UHF
Fast-scan TV (ATV) is not used on HF due to bandwidth requirements
[Speaker Notes: Notes area]

---
Digital Mode Overview
Maximum data rates and bandwidths are specified by the FCC rules
Digital codes other than those specified by the FCC must be public
Amateurs are not allowed to use secret or private codes
This requirement includes the protocols used to control communications
[Speaker Notes: Rule changes regarding symbol rate and bandwidth have been proposed. Watch the ARRL website for updates and more information.]

---
Modes
Radioteletype (RTTY) – originally used mechanical teleprinters but migrated to computer sound cards
RTTY is popular on all the HF amateur bands (100% duty cycle)
PSK31 – good weak signal mode using low transmitter power and very narrow bandwidth (computer sound card)
[Speaker Notes: Notes area]

---
Modes
PACTOR and WINMOR: (Winlink 2000)
PACTOR stands for PACket Teletype Over Radio
WINMOR stands for Windows Messaging Over Radio
Both modes use advanced modulation techniques, including error correction and automatic communication control
[Speaker Notes: Both PACTOR and WINMOR are used by the Winlink system which accesses email servers via gateway and mailbox stations that link to the Internet.]

---
Modes
Packet Radio – common on the VHF and UHF bands (1200 & 9600 baud)
Uses the AX.25 protocol standard
Not popular on HF due to transmission errors from noise and fading, can only use a 300 baud data rate on HF
JT65 and JT9 are very effective at communicating at extremely low signal levels
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What segment of the 20-meter band is most often used for digital transmissions?
What segment of the 20-meter band is most often used for digital transmissions?
A. 14.000 - 14.050 MHz
B. 14.070 - 14.100 MHz
C. 14.150 - 14.225 MHz
D. 14.275 - 14.350 MHz
  G2E04

---
What segment of the 20-meter band is most often used for digital transmissions?
A. 14.000 - 14.050 MHz
B. 14.070 - 14.100 MHz
C. 14.150 - 14.225 MHz
D. 14.275 - 14.350 MHz
  G2E04

---
What segment of the 80-meter band is most commonly used for digital transmissions?
What segment of the 80-meter band is most commonly used for digital transmissions?
A. 3570 - 3600 kHz
B. 3500 - 3525 kHz
C. 3700 - 3750 kHz
D. 3775 - 3825 kHz
  G2E07

---
What segment of the 80-meter band is most commonly used for digital transmissions?
A. 3570 - 3600 kHz
B. 3500 - 3525 kHz
C. 3700 - 3750 kHz
D. 3775 - 3825 kHz
  G2E07

---
In what segment of the 20-meter band are most PSK31 operations commonly found?
In what segment of the 20-meter band are most PSK31 operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment, near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Below the RTTY segment, near 14.070 MHz
  G2E08

---
In what segment of the 20-meter band are most PSK31 operations commonly found?
A. At the bottom of the slow-scan TV segment, near 14.230 MHz
B. At the top of the SSB phone segment, near 14.325 MHz
C. In the middle of the CW segment, near 14.100 MHz
D. Below the RTTY segment, near 14.070 MHz
  G2E08

---
Which communication system sometimes uses the Internet to transfer messages?
Which communication system sometimes uses the Internet to transfer messages?
A. Winlink
B. RTTY
C. ARES
D. Skywarn
  G2E13

---
Which communication system sometimes uses the Internet to transfer messages?
A. Winlink
B. RTTY
C. ARES
D. Skywarn
  G2E13

---
Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands?
Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands?
A. FSK441 and Hellschreiber
B. JT9 and JT65
C. Clover
D. RTTY
  G8C01

---
Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands?
A. FSK441 and Hellschreiber
B. JT9 and JT65
C. Clover
D. RTTY
  G8C01

---
General License Course
Chapter 6
Lesson Plan Module 23 –
Digital Basics

---
Definitions
Bit – fundamental unit of data; 0 or 1
Bit rate – number of digital bits per second sent from one computing system to the other
Symbol – a characteristic of the transmitted signal that represents data
Baud or bauds – number of symbols sent per second (symbol rate)
[Speaker Notes: Symbols can be many things: a tone frequency, a shift in phase, presence or absence of carrier. For example, in semaphore, the symbols are flag positions. The transmitter sends symbols one at a time. Each symbol can represent more than one bit.]

---
Definitions
Duty cycle – the ratio of time that the transmitter is on to the total of on time plus off time
Protocol – rules that control the method used to exchange data
Mode – the combination of a protocol with a modulation method such as RTTY or PSK31
[Speaker Notes: Notes area]

---
Protocol and Modulation
Protocol – the set of rules that control the encoding, packaging, exchanging, and decoding of digital data
Specifies how each packet is constructed and exchanged, what characters are used
How errors are detected and managed
Method of modulation chosen by convention
SSB or FM for packet radio, FSK or AFSK for RTTY
[Speaker Notes: Notes area]

---
Frequency Shift Keying (FSK)
RTTY signal – two different tones shifting from one frequency to another
The rapidly changing tones are called mark and space
Space represents 0
Mark represents 1
[Speaker Notes: Notes area]

---
FSK – AFSK
FSK – the frequency of the transmitter’s VFO is controlled directly by a digital data signal from the computer
Audio frequency shift keying (AFSK) – audio tones are used to modulate an SSB or FM transmitter through the microphone input
Audio must be kept free of noise
ALC and compression must not be used to prevent distortion
[Speaker Notes: Many radios have a direct FSK input that can use a high or low voltage to shift the transmitter frequency. This avoids having to use the speech circuits for data.]

---
Practice Questions
[Speaker Notes: Notes area]

---
How is an FSK signal generated?
How is an FSK signal generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator’s frequency directly with a digital control signal
C. By using a transceiver’s computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator
  G8A01

---
How is an FSK signal generated?
A. By keying an FM transmitter with a sub-audible tone
B. By changing an oscillator’s frequency directly with a digital control signal
C. By using a transceiver’s computer data interface protocol to change frequencies
D. By reconfiguring the CW keying input to act as a tone generator
  G8A01

---
How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
A. Dot and Dash
B. On and Off
C. High and Low
D. Mark and Space
  G8C11

---
How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
A. Dot and Dash
B. On and Off
C. High and Low
D. Mark and Space
  G8C11

---
General License Course
Chapter 6
Lesson Plan Module 24 –
Character-based Modes

---
Radioteletype (RTTY)
RTTY uses the Baudot code, which represents (encodes) each text character as a sequence of 5 bits
An initial bit (the start bit) and an inter-character pause (the stop bit) are used to synchronize the transmitting and receiving stations
[Speaker Notes: Notes area]

---
RTTY
Baudot code uses 5 bits for encoding data (32 different characters)
Not enough for the entire English alphabet, numerals, and punctuation
Two special codes, LTRS and FIGS, are used to switch between two sets of characters, increasing the number of available characters to 62
[Speaker Notes: Notes area]

---
RTTY
On HF, the most common speeds are 60, 75, and 100 WPM (corresponding to 45, 56, and 75 baud)
Most RTTY conversations on HF are conducted at 45 baud and the most common shift between the mark and space frequencies is 170 Hz
You must match your speed and shift to communicate with the other RTTY station
[Speaker Notes: Notes area]

---
Multiple Frequency Shift Keying
MFSK16 uses 16 separate tones, all 15.625 Hz apart
Withstands fading and distortion better than FSK
DominoEX and Olivia are variations of MFSK
MT63, “MT” stands for “multi-tone” data signal composed of 64 tones
Uses advanced DSP techniques which enable it to perform well under noisy and fading conditions
[Speaker Notes: MFSK and similar modes are one of the most active areas of amateur experimentation. Much free software is available to enable hams to use the digital modes. Fldigi is the best-known package.]

---
PSK31
The “31” stands for the symbol rate of the protocol, actually 31.25 baud
PSK uses a variable length code called Varicode that assigns shorter codes to common characters and longer codes for others
Capital letters and punctuation characters take more bits and thus slow the contact
[Speaker Notes: RTTY users often use capital letters out of habit but should convert to lower-case letters on PSK31 to speed up the symbol rate. As has been the case on the Internet, capital letters are also interpreted as shouting.]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is the most common frequency shift for RTTY emissions in the amateur HF bands?
What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz
  G2E06

---
What is the most common frequency shift for RTTY emissions in the amateur HF bands?
A. 85 Hz
B. 170 Hz
C. 425 Hz
D. 850 Hz
  G2E06

---
How many data bits are sent in a single PSK31 character?
How many data bits are sent in a single PSK31 character?
A. The number varies
B. 5
C. 7
D. 8
  G8C02

---
How many data bits are sent in a single PSK31 character?
A. The number varies
B. 5
C. 7
D. 8
  G8C02

---
Which of the following describes Baudot code?
Which of the following describes Baudot code?
A. A 7-bit code with start, stop and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN
  G8C04

---
Which of the following describes Baudot code?
A. A 7-bit code with start, stop and parity bits
B. A code using error detection and correction
C. A 5-bit code with additional start and stop bits
D. A code using SELCAL and LISTEN
  G8C04

---
Which of the following statements is true about PSK31?
Which of the following statements is true about PSK31?
A. Upper case letters make the signal stronger
B. Upper case letters use longer Varicode signals and thus slow down transmission
C. Varicode Error Correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates
  G8C08

---
Which of the following statements is true about PSK31?
A. Upper case letters make the signal stronger
B. Upper case letters use longer Varicode signals and thus slow down transmission
C. Varicode Error Correction is used to ensure accurate message reception
D. Higher power is needed as compared to RTTY for similar error rates
  G8C08

---
What does the number 31 represent in “PSK31”?
What does the number 31 represent in “PSK31”?
A. The approximate transmitted symbol rate
B. The version of the PSK protocol
C. The year in which PSK31 was invented
D. The number of characters that can be represented by PSK31
  G8C09

---
What does the number 31 represent in "PSK31"?
What does the number 31 represent in "PSK31"?
A. The approximate transmitted symbol rate
B. The version of the PSK protocol
C. The year in which PSK31 was invented
D. The number of characters that can be represented by PSK31
  G8C09

---
Which type of code is used for sending characters in a PSK31 signal?
Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary
  G8C12

---
Which type of code is used for sending characters in a PSK31 signal?
A. Varicode
B. Viterbi
C. Volumetric
D. Binary
  G8C12

---
General License Course
Chapter 6
Lesson Plan Module 25 –
Packet-Based Modes

---
Packet Basics
Packet refers to the transmission of data in structured groups
Header – at the start of the packet – contains:
Synchronization patterns for the receiver
Control, routing and handling information
Error detection and correction information
[Speaker Notes: Notes area]

---
Packet Basics
Data – the data to be exchanged, often compressed for efficiency
Data can encapsulate another protocol’s packets
Trailer – additional control or status information and data used for error detection
The most common error detection is a cyclic redundancy check (CRC)
The result of a calculation based on the values of packet characters
[Speaker Notes: The CRC calculation is performed by the receiver on the data received and it must match the CRC sent by the transmitter, which did the same calculation. If both match, the data has a very high probability of being correct. If errors are detected, the protocol determines what action to take. Reliable transport means that the protocol does not allow data to be accepted unless no errors were detected in the received packet.]

---
Error Correction
Forward error correction (FEC) –includes additional redundant encoded information with the data being transmitted
Automatic Repeat reQuest (ARQ) – the protocol requires that a packet with errors in the data be retransmitted
Uses ACK (rcvd OK) and NAK (error detected) messages to the sending station
[Speaker Notes: Notes area]

---
Error Correction
ARQ protocols are designed to transfer data between two stations
An ACK or NAK response to the sending station can only be received from one receiving station
You can’t “break in” to an ongoing contact between two stations using an ARQ mode
[Speaker Notes: Notes area]

---
Error Correction
Monitoring or “MON” mode – stations can listen to the ARQ conversation and receive the data but without retransmission of “bad” packets
Monitoring mode allows you to determine if a frequency is occupied
PACTOR and WINMOR are ARQ protocols
Preferred method of HF data transmission for the popular Winlink email system
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations?
How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations?
A. Unplug the data connector temporarily and see if the channel-busy indication is turned off
B. Put the modem or controller in a mode which allows monitoring communications without a connection
C. Transmit UI packets several times and wait to see if there is a response from another PACTOR station
D. Send the message: “Is this frequency in use?”
  G2E02

---
How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations?
A. Unplug the data connector temporarily and see if the channel-busy indication is turned off
B. Put the modem or controller in a mode which allows monitoring communications without a connection
C. Transmit UI packets several times and wait to see if there is a response from another PACTOR station
D. Send the message: “Is this frequency in use?”
  G2E02

---
How do you join a contact between two stations using the PACTOR protocol?
How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode
B. Transmit a steady carrier until the PACTOR protocol times out and disconnects
C. Joining an existing contact is not possible, PACTOR connections are limited to two stations
D. Send a NAK response continuously so that the sending station has to pause
  G2E09

---
How do you join a contact between two stations using the PACTOR protocol?
A. Send broadcast packets containing your call sign while in MONITOR mode
B. Transmit a steady carrier until the PACTOR protocol times out and disconnects
C. Joining an existing contact is not possible, PACTOR connections are limited to two stations
D. Send a NAK response continuously so that the sending station has to pause
  G2E09

---
What part of a data packet contains the routing and handling information?
What part of a data packet contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Footer
  G8C03

---
What part of a data packet contains the routing and handling information?
A. Directory
B. Preamble
C. Header
D. Footer
  G8C03

---
In the PACTOR protocol, what is meant by an NAK response to a transmitted packet?
In the PACTOR protocol, what is meant by an NAK response to a transmitted packet?
A. The receiver is requesting the packet be retransmitted
B. The receiver is reporting the packet was received without error
C. The receiver is busy decoding the packet
D. The entire file has been received correctly
  G8C05

---
In the PACTOR protocol, what is meant by an NAK response to a transmitted packet?
A. The receiver is requesting the packet be retransmitted
B. The receiver is reporting the packet was received without error
C. The receiver is busy decoding the packet
D. The entire file has been received correctly
  G8C05

---
How does the receiving station respond to an ARQ data mode packet containing errors?
How does the receiving station respond to an ARQ data mode packet containing errors?
A. It terminates the contact
B. It requests the packet be retransmitted
C. It sends the packet back to the transmitting station
D. It requests a change in transmitting protocol
  G8C07

---
How does the receiving station respond to an ARQ data mode packet containing errors?
A. It terminates the contact
B. It requests the packet be retransmitted
C. It sends the packet back to the transmitting station
D. It requests a change in transmitting protocol
  G8C07

---
How does forward error correction (FEC) allow the receiver to correct errors in received data packets?
How does forward error correction (FEC) allow the receiver to correct errors in received data packets?
A. By controlling transmitter output power for optimum signal strength
B. By using the varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character
  G8C10

---
How does forward error correction (FEC) allow the receiver to correct errors in received data packets?
A. By controlling transmitter output power for optimum signal strength
B. By using the varicode character set
C. By transmitting redundant information with the data
D. By using a parity bit with each character
  G8C10

---
General License Course
Chapter 6
Lesson Plan Module 26 –
Receiving and Transmitting Digital Modes

---
Receiving and Transmitting Digital Modes
RTTY on HF is transmitted as an LSB signal. JT65 and JT9 use USB.
USB/LSB selected by convention for each mode.
Digital signals on the wrong sideband will not decode correctly because the relationship of the tones and the digital data will be inverted
Know where your sidebands are with respect to the displayed frequency – stay in the band!
[Speaker Notes: It is very common for new HF operators to assume that the displayed frequency on the transceiver is the frequency of their transmitted signal but that is not the case when using a voice, data, or image mode. Use the relationship between an RTTY signal’s displayed “carrier” frequency (even though there is no carrier) and the mark and space tone frequencies. Show how to determine where the signal’s emission frequencies actually are and how to stay within a band or band segment.]

---
Bandwidth of Digital Modes
The FCC rules define the bandwidth of a digital mode signal in the same way as any other signal
As the symbol rate of a signal increases, so does the bandwidth required to transmit that signal.
By packing more bits into a symbol the net bit rate can be increased while keeping symbol rate the same and without increasing bandwidth
[Speaker Notes: Notes area]

---
Bandwidth of Digital Modes
Table 6.2 – Bandwidth Comparison of Digital Modes
Mode	Bandwidth (Hz)
PSK31	50
RTTY	200
MFSK16	300
JT65	350
DominoEX	524
Olivia	1000
WINMOR	1600
MT63	2000
PACTOR-III, -IV	2300
Bandwidths are approximate for the highest commonly used symbol rate and are not specifications
[Speaker Notes: Notes area]

---
Transmitter Duty Cycle
Most amateur transmitters are not designed to operate at full power output for an extended time
RTTY, PSK31 – nearly 100% for extended periods
ARQ modes – less than 100% but still high
Reduce your transmitter power to about 50% of maximum output power for most digital modes
[Speaker Notes: Notes area]

---
Digital Mode Signal Quality
Excess audio levels causes distortion and splatter just as for voice modes
On a waterfall display, vertical lines to each side of the main signal represents a spurious emission
Distortion makes a signal harder to copy
Spurious emissions cause interference
Keep your data audio levels set correctly
[Speaker Notes: Notes area]

---
ALC and Digital Modes
Automatic Level Control (ALC) is used to prevent excessive drive to amplifier inputs
As it changes power levels, ALC can cause distortion of the original signal.
Distortion caused by ALC makes the signal harder to decode and creates spurious emissions
Mild distortion caused by ALC is acceptable on voice modes

---
ALC and Digital Modes
When using a digital mode, your ALC system should be either disabled or the microphone input level and gain turned down to the point where the ALC system does not activate
Monitor ALC during digital transmission (usually a meter function selection)
The ALC should not activate during digital transmissions.

---
Practice Questions
[Speaker Notes: Notes area]

---
Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter?
Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB
  G2E01

---
Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter?
A. USB
B. DSB
C. CW
D. LSB
  G2E01

---
What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band?
What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band?
A. LSB
B. USB
C. DSB
D. SSB
  G2E05

---
What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band?
A. LSB
B. USB
C. DSB
D. SSB
  G2E05

---
What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal?
What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal?
A. Long Path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation
  G2E11

---
What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal?
A. Long Path propagation
B. Backscatter propagation
C. Insufficient modulation
D. Overmodulation
  G2E11

---
What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed
B. You may have selected the wrong baud rate
C. You may be listening on the wrong sideband
D. All of these choices are correct
  G2E14

---
What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly?
A. The mark and space frequencies may be reversed
B. You may have selected the wrong baud rate
C. You may be listening on the wrong sideband
D. All of these choices are correct
  G2E14

---
What is likely to happen if a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode?
What is likely to happen if a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode?
A. ALC will invert the modulation of the AFSK mode
B. Improper action of ALC distorts the signal and can cause spurious emissions
C. When using digital modes, too much ALC activity can cause the transmitter to overheat
D. All of these choices are correct
  G4A14

---
What is likely to happen if a transceiver’s ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode?
A. ALC will invert the modulation of the AFSK mode
B. Improper action of ALC distorts the signal and can cause spurious emissions
C. When using digital modes, too much ALC activity can cause the transmitter to overheat
D. All of these choices are correct
  G4A14

---
What is the approximate bandwidth of a PACTOR3 signal at maximum data rate?
What is the approximate bandwidth of a PACTOR3 signal at maximum data rate?
A. 31.5 Hz
B. 500 Hz
C. 1800 Hz
D. 2300 Hz
  G8B05

---
What is the approximate bandwidth of a PACTOR3 signal at maximum data rate?
A. 31.5 Hz
B. 500 Hz
C. 1800 Hz
D. 2300 Hz
  G8B05

---
Why is it important to know the duty cycle of the mode you are using when transmitting?
Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles which could exceed the transmitter's average power rating
C. To allow time for the other station to break in during a transmission
D. All of these choices are correct
  G8B08

---
Why is it important to know the duty cycle of the mode you are using when transmitting?
A. To aid in tuning your transmitter
B. Some modes have high duty cycles which could exceed the transmitter's average power rating
C. To allow time for the other station to break in during a transmission
D. All of these choices are correct
  G8B08

---
What is the relationship between transmitted symbol rate and bandwidth?
What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is always half the symbol rate
  G8B10

---
What is the relationship between transmitted symbol rate and bandwidth?
A. Symbol rate and bandwidth are not related
B. Higher symbol rates require wider bandwidth
C. Lower symbol rates require wider bandwidth
D. Bandwidth is always half the symbol rate
  G8B10

---
General License Course
Chapter 6
Lesson Plan Module 27 –
Digital Operating Procedures

---
Listening First
To avoid causing interference, the control operator:
Must listen to the received audio or watch a waterfall-style display before transmitting
It’s not enough to just check a BUSY light on a modem
Follow good amateur practice and listen, listen, listen!
[Speaker Notes: Demonstrate the method of calling CQ on digital modes and that it is similar to calling CQ on CW or voice. Note that PACTOR and WINMOR have “connect” and “disconnect” messages that initiate and terminate a contact.]

---
Gateway & Mailbox Stations
Unmanned gateway and mailbox stations monitor a fixed frequency until another station attempts to connect to them
They respond without requiring a human control operator
The FCC classifies them as automatically controlled digital stations
[Speaker Notes: Winlink uses RMS (Radio Message Server) software to control the gateway/mailbox stations.]

---
Automatically Controlled Stations
Automatically controlled stations are only permitted to use RTTY and data modes in the 1.25 meter band and band segments on the HF bands
A station operating under FCC rules must be operating under local or remote control (i.e., with a control operator in charge of all transmissions) to contact these stations legally
[Speaker Notes: Notes area]

---
Automatically Controlled Stations
Automatic Control Band Segments for RTTY and Data
Band (Meters)	Frequency range (MHz)
80	3.585-3.600
40	7.100-7.105
30	10.140-10.150
20	14.0950-14.0995 and 14.1005-14.112
17	18.105-18.110
15	21.090-21.100
12	24.925-24.930
10	28.120-28.189
6	50.1-50.4
2	144.1-148
[Speaker Notes: Notes area]

---
Automatically Controlled Stations
Establishing a connection will vary with the equipment and mode being used
The contact starts with sending a CONNECT message to the station with which you want to connect
A training sequence then determines the best rate and modulation to use based on conditions
Once training is completed, a message can then be transferred
[Speaker Notes: A station using PACTOR or WINMOR can only connect to one other station at a time.]

---
Digital Contact Display
The waterfall displays the presence of signals as a series of lines, each representing a scan across the frequency range
The strength of the signals is represented as the brightness, intensity, or color of the line at each frequency on the display
The display gives the impression of a “waterfall” as the data flows across the screen in successive scans
[Speaker Notes: If you can, run DigiPan or Fldigi or some other spectrum display software.]

---
Third Party Traffic
All FCC rules about third-party messages apply to digital transmissions
This includes all information included in email, digital images, or web pages transmitted via Amateur Radio
Commercial messages such as advertisements or pertaining to your business may not be transmitted via Amateur Radio
[Speaker Notes: Notes area]

---
Interfering Signals
Symptoms of Interference:
Failure to connect
Frequent retries or transmission delays during data transfer, progress slow or erratic
Timeouts or dropped connections – in cases of strong or persistent interference, the number of requested retransmissions may exceed a preset limits
[Speaker Notes: Explain how the skip zone or shadowing can create the “hidden transmitter” problem in which a pair of stations can each hear a third station but cannot hear each other. If you think you may have interference causing problems – listen to the received audio or carefully monitor the waterfall display.]

---
Interfering Signals
Remember, the interference may be accidental or the other station may not hear your signal at all
Use a different frequency
Aim directional antennas in another direction
[Speaker Notes: If you have a beam, try finding a heading that minimizes signal strength of the interference. Off the side often works well while still providing enough signal strength to and from the desired station that the contact can be completed.]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
A. The station initiating the contact must be under local or remote control
B. The interrogating transmission must be made by another automatically controlled station
C. No third party traffic maybe be transmitted
D. The control operator of the interrogating station must hold an Extra Class license
  FCC Rule: [97.221] G1E03

---
What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
A. The station initiating the contact must be under local or remote control
B. The interrogating transmission must be made by another automatically controlled station
C. No third party traffic maybe be transmitted
D. The control operator of the interrogating station must hold an Extra Class license
  FCC Rule: [97.221] G1E03

---
Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet?
Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet?
A. Locally controlled station
B. Robotically controlled station
C. Automatically controlled digital station
D. Fail-safe digital station
  FCC Rule: [97.221] G1E11

---
Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet?
A. Locally controlled station
B. Robotically controlled station
C. Automatically controlled digital station
D. Fail-safe digital station
  FCC Rule: [97.221] G1E11

---
Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication?
Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication?
A. Under no circumstances
B. When messages are encrypted
C. When messages are not encrypted
D. When under automatic control
  FCC Rule: [97.115] G1E12

---
Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication?
A. Under no circumstances
B. When messages are encrypted
C. When messages are not encrypted
D. When under automatic control
  FCC Rule: [97.115] G1E12

---
On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
A. On any band segment where digital operation is permitted
B. Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
C. Only in the non-phone Extra Class segments of the bands
D. Anywhere in the 1.25-meter or shorter wavelength bands, and in specified segments of the 80-meter through 2-meter bands
  FCC Rule: [97.221, 97.305] G1E13

---
On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
A. On any band segment where digital operation is permitted
B. Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
C. Only in the non-phone Extra Class segments of the bands
D. Anywhere in the 1.25-meter or shorter wavelength bands, and in specified segments of the 80-meter through 2-meter bands
  FCC Rule: [97.221, 97.305] G1E13

---
What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission?
What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All of these choices are correct
  G2E03

---
What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission?
A. Frequent retries or timeouts
B. Long pauses in message transmission
C. Failure to establish a connection between stations
D. All of these choices are correct
  G2E03

---
Which of the following is a way to establish contact with a digital messaging system gateway station?
Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Send an email to the system control operator
B. Send QRL in Morse code
C. Respond when the station broadcasts its SSID
D. Transmit a connect message on the station’s published frequency
  G2E10

---
Which of the following is a way to establish contact with a digital messaging system gateway station?
A. Send an email to the system control operator
B. Send QRL in Morse code
C. Respond when the station broadcasts its SSID
D. Transmit a connect message on the station’s published frequency
  G2E10

---
Which of the following describes a waterfall display?
Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity
  G2E12

---
Which of the following describes a waterfall display?
A. Frequency is horizontal, signal strength is vertical, time is intensity
B. Frequency is vertical, signal strength is intensity, time is horizontal
C. Frequency is horizontal, signal strength is intensity, time is vertical
D. Frequency is vertical, signal strength is horizontal, time is intensity
  G2E12

---
What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR?
What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set
  G8C06

---
What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR?
A. The checksum overflows
B. The connection is dropped
C. Packets will be routed incorrectly
D. Encoding reverts to the default character set
  G8C06