General License Course Chapter 7
General License Course
Chapter 7
Lesson Plan Module 28 –
Antenna Basics

---
Antenna Basics
Definitions:
Elements – conduction portion of an antenna that radiates or receives a signal
Polarization – refers to the orientation of the electric field radiated by the antenna
Feed point impedance – the ratio of RF voltage to current at an antenna’s feed point
Resonant – when its feed point impedance is completely resistive (no reactance)
Radiation pattern – a graph of the signal strength in every direction or vertical angle
2015 General License Course
[Speaker Notes: Spend a little extra time on antenna resonance noting that it only refers to having no reactance in the feed point impedance. It does not imply 50 ohms or matched conditions or anything else.]

---
Antenna Basics
Definitions:
Azimuthal pattern – signal strength in horizontal directions
Elevation pattern – signal strength in a vertical direction
Lobes – regions in the radiation pattern where the antenna is radiating a signal
Nulls – point at which radiation is at a minimum between lobes
Isotropic – antenna radiates equally in every possible direction (only a reference antenna)
[Speaker Notes: Have an example of radiation patterns from several common antennas.]

---
Antenna Basics
Omnidirectional – antenna radiates a signal of equal strength in every horizontal direction
Directional – antenna radiates preferentially in one or more directions
Gain – concentration of signal transmitted toward or received from a specific direction
Front-to-back ratio – ratio of gain in a forward direction to the opposite direction
Front-to-side ratio – ratio of gain in a forward direction to directions at right angles
Gain ratios are measured in dB
[Speaker Notes: Notes area]

---
dBd vs dBi
Antenna gain is specified in decibels (dB) with respect to an identified reference antenna
Gain with respect to an isotropic antenna is called dBi
Gain with respect to a dipole antenna’s maximum radiation is called dBd
Convert dBd to dBi by adding 2.15 dB and from dBi to dBd by subtracting 2.15 dB
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
How does antenna gain stated in dBi compare to gain stated in dBd for the same antenna?
How does antenna gain stated in dBi compare to gain stated in dBd for the same antenna?
A. dBi gain figures are 2.15 dB lower then dBd gain figures
B. dBi gain figures are 2.15 dB higher than dBd gain figures
C. dBi gain figures are the same as the square root of dBd gain figures multiplied by 2.15
D. dBi gain figures are the reciprocal of dBd gain figures + 2.15 dB
  G9C19

---
How does antenna gain stated in dBi compare to gain stated in dBd for the same antenna?
A. dBi gain figures are 2.15 dB lower then dBd gain figures
B. dBi gain figures are 2.15 dB higher than dBd gain figures
C. dBi gain figures are the same as the square root of dBd gain figures multiplied by 2.15
D. dBi gain figures are the reciprocal of dBd gain figures + 2.15 dB
  G9C19

---
What is meant by the terms dBi and dBd when referring to antenna gain?
What is meant by the terms dBi and dBd when referring to antenna gain?
A. dBi refers to an isotropic antenna, dBd refers to a dipole antenna
B. dBi refers to an ionospheric reflecting antenna, dBd refers to a dissipative antenna
C. dBi refers to an inverted-vee antenna, dBd refers to a downward reflecting antenna
D. dBi refers to an isometric antenna, dBd refers to a discone antenna
  G9C20

---
What is meant by the terms dBi and dBd when referring to antenna gain?
A. dBi refers to an isotropic antenna, dBd refers to a dipole antenna
B. dBi refers to an ionospheric reflecting antenna, dBd refers to a dissipative antenna
C. dBi refers to an inverted-vee antenna, dBd refers to a downward reflecting antenna
D. dBi refers to an isometric antenna, dBd refers to a discone antenna
  G9C20

---
General License Course
Chapter 7
Lesson Plan Module 29 –
Dipoles, Ground-planes & Random Wires

---
Dipoles
The dipole antenna is a straight conductor, usually ½ wavelengths long with a feed point in the middle
A dipole radiates strongest broadside to its axis and weakest off the ends
A figure-eight is the shape of the azimuth pattern for a dipole installed in free space (no ground)
The feed point impedance of a center-fed dipole is approximately 72  but varies depending on height
The feed point impedance increases as it is moved away from center
[Speaker Notes: Notes area]

---
Dipoles
[Speaker Notes: Show the points of high and low feed point impedance. Note that impedance is just the ratio of voltage to current. Where voltage is high, impedance is high and where current is high, impedance is low.]

---
Example antenna: 10 meter dipole.
Demonstrate the “AC OHMMETER” (Antenna analyzer)
Demonstrate the impedance at different points.
Explain definition of resonance ( no reactance )
Demonstration off center fed operation

---
Dipole
In free space, ½ wavelengths (λ) in feet equals 492 divided by frequency in MHz
Practical ½-wave dipoles are shorter than 492 / f because:
Actual thickness - wire looks longer electrically
Height above ground affects impedance, as do nearby conducting surfaces
Insulated wire makes it “look longer” also!!!
Center-fed dipoles are generally a good match to 50 or 75 Ω at common heights and on odd harmonics
[Speaker Notes: Example 1: What is the approximate length in feet of a ½-wave dipole resonant at 3.550 MHz? Free space length = 492/3.55 = 139 ft Pick the closest multiple choice answer (131 ft) Example 2: What is the approximate length in feet of a ½-wave dipole for 14.250 MHz? Free space length = 492/14.250 = 34.5 ft Pick the closest multiple choice answer (32 ft)]

---
Ground Planes (Verticals)
The basic ground plane antenna is λ/4 element over a ground plane, radiates omnidirectionally
Imagine one-half of a dipole with ground plane making up the missing half
Currents in the ground plane create the effect of an electrical image of the missing half, like an electrical mirror
The ground plane can be made from sheet metal or radial wires
[Speaker Notes: Notes area]

---
Ground Plane Vertical
Ground-mounted ground plane antennas have radial wires laid on the surface or buried within a few inches of the surface
Feed point impedance of a ground plane antenna is approximately 35  (half a dipole)
Drooping elevated radials from 30 to 45 degrees will raise the feed point impedance to approximately 50 
Ground plane antenna length is 246/freq. in MHz
[Speaker Notes: Example 3: What is the approximate length in feet of a ¼-wave ground plane antenna resonant at 28.5 MHz? Instead of 492/f use 246/f and pick the closest answer: 246/28.5 = 8.6 ft (closest question answer is 8 ft)]

---
Mobile HF Antennas
Mobile antennas for HF are often some form of a ground plane (vertical whip)
Electrical loading is a technique for shortening a mobile vertical and presenting a reasonable feed point impedance
A shortened antenna will have a smaller operating bandwidth without retuning and lower efficiency.
Screwdriver antennas with an adjustable coil are a good compromise between performance and convenience
[Speaker Notes: Height limits for vehicles make full-sized ¼-wave whips are infeasible for bands below 24 MHz. Also mechanically impractical. There are lots of techniques for making short antennas work reasonably well.]

---
Random Wires
Random wire antenna is just that: a random length of wire
Feed point impedance and radiation pattern is very unpredictable
Random wire antennas are connected through a matching network and then to the transmitter
Random wire antennas may result in significant RF currents and voltages on the station equipment and RF burns (if you don’t know what you are doing…..) They are my favorite type of antenna….
[Speaker Notes: Notes area]

---
Effects Of Height Above Ground
Below ½ wavelengths in height, the antenna’s feed point impedance steadily decreases until it is close to zero at ground level (Dental tower antenna was an example of this)
Above ½ wavelengths the impedance varies, eventually reaching a stable value at a height of several wavelengths
Height also effects the radiation pattern
Below ½ wavelengths, the dipole pattern is almost omnidirectional. Greater heights cause the pattern to develop lobes and nulls
[Speaker Notes: Notes area]

---
Effects of Polarization
Radio waves reflecting from the ground have lower losses when the polarization of the wave is parallel to the ground
Horizontal antennas have a lower ground reflection loss than a vertical
Ground-mounted vertical antennas are able to generate stronger signals at lower angles of radiation than horizontal antennas at low heights
Vertical antennas are often preferred for DX contacts where it’s impossible to erect tall towers and beams (Flagpole antenna works fine)
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What is the purpose of a capacitance hat on a mobile antenna?
What is the purpose of a capacitance hat on a mobile antenna?
A. To increase the power handling capacity of a whip antenna
B. To allow automatic band changing
C. To electrically lengthen a physically short antenna
D. To allow remote tuning
  G4E01

---
What is the purpose of a capacitance hat on a mobile antenna?
A. To increase the power handling capacity of a whip antenna
B. To allow automatic band changing
C. To electrically lengthen a physically short antenna
D. To allow remote tuning
  G4E01

---
What is the purpose of a corona ball on a HF mobile antenna?
What is the purpose of a corona ball on a HF mobile antenna?
A. To narrow the operating bandwidth of the antenna
B. To increase the "Q" of the antenna
C. To reduce the chance of damage if the antenna should strike an object
D. To reduce high voltage discharge from the tip of the antenna
  G4E02

---
What is the purpose of a corona ball on a HF mobile antenna?
A. To narrow the operating bandwidth of the antenna
B. To increase the "Q" of the antenna
C. To reduce the chance of damage if the antenna should strike an object
D. To reduce high voltage discharge from the tip of the antenna
  G4E02

---
What is one disadvantage of using a shortened mobile antenna as opposed to a full size antenna?
What is one disadvantage of using a shortened mobile antenna as opposed to a full size antenna?
A. Short antennas are more likely to cause distortion of transmitted signals
B. Short antennas can only receive circularly polarized signals
C. Operating bandwidth may be very limited
D. Harmonic radiation may increase
  G4E06

---
What is one disadvantage of using a shortened mobile antenna as opposed to a full size antenna?
A. Short antennas are more likely to cause distortion of transmitted signals
B. Short antennas can only receive circularly polarized signals
C. Operating bandwidth may be very limited
D. Harmonic radiation may increase
  G4E06

---
What is one disadvantage of a directly fed random-wire HF antenna?
What is one disadvantage of a directly fed random-wire HF antenna?
A. It must be longer than 1 wavelength
B. You may experience RF burns when touching metal objects in your station
C. It produces only vertically polarized radiation
D. It is more effective on the lower HF bands than on the higher bands
  G9B01

---
What is one disadvantage of a directly fed random-wire HF antenna?
A. It must be longer than 1 wavelength
B. You may experience RF burns when touching metal objects in your station
C. It produces only vertically polarized radiation
D. It is more effective on the lower HF bands than on the higher bands
2. if you simply use a balun properly, I don’t think you’ll ever have this problem…..
  G9B01

---
Which of the following is a common way to adjust the feed point impedance of a quarter wave ground plane vertical antenna to be approximately 50 ohms?
Which of the following is a common way to adjust the feed point impedance of a quarter wave ground plane vertical antenna to be approximately 50 ohms?
A. Slope the radials upward
B. Slope the radials downward
C. Lengthen the radials
D. Shorten the radials
  G9B02

---
Which of the following is a common way to adjust the feed point impedance of a quarter wave ground plane vertical antenna to be approximately 50 ohms?
A. Slope the radials upward
B. Slope the radials downward
C. Lengthen the radials
D. Shorten the radials
  G9B02

---
What happens to the feed point impedance of a ground plane antenna when its radials are changed from horizontal to sloping downward?
What happens to the feed point impedance of a ground plane antenna when its radials are changed from horizontal to sloping downward?
A. It decreases
B. It increases
C. It stays the same
D. It reaches a maximum at an angle of 45 degrees
  G9B03

---
What happens to the feed point impedance of a ground plane antenna when its radials are changed from horizontal to sloping downward?
A. It decreases
B. It increases
C. It stays the same
D. It reaches a maximum at an angle of 45 degrees
  G9B03

---
What is the radiation pattern of a dipole antenna in free space in the plane of the conductor?
What is the radiation pattern of a dipole antenna in free space in the plane of the conductor?
A. It is a figure-eight at right angles to the antenna
B. It is a figure-eight off both ends of the antenna
C. It is a circle (equal radiation in all directions)
D. It has a pair of lobes on one side of the antenna and a single lobe on the other side
  G9B04

---
What is the radiation pattern of a dipole antenna in free space in the plane of the conductor?
A. It is a figure-eight at right angles to the antenna
B. It is a figure-eight off both ends of the antenna
C. It is a circle (equal radiation in all directions)
D. It has a pair of lobes on one side of the antenna and a single lobe on the other side
  G9B04

---
How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna?
How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna?
A. If the antenna is too high, the pattern becomes unpredictable
B. Antenna height has no effect on the pattern
C. If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional
D. If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated
  G9B05

---
How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna?
A. If the antenna is too high, the pattern becomes unpredictable
B. Antenna height has no effect on the pattern
C. If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional
D. If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated
  G9B05

---
Where should the radial wires of a ground-mounted vertical antenna system be placed?
Where should the radial wires of a ground-mounted vertical antenna system be placed?
A. As high as possible above the ground
B. Parallel to the antenna element
C. On the surface of the Earth or buried a few inches below the ground
D. At the center of the antenna
  G9B06

---
Where should the radial wires of a ground-mounted vertical antenna system be placed?
A. As high as possible above the ground
B. Parallel to the antenna element
C. On the surface of the Earth or buried a few inches below the ground
D. At the center of the antenna
  G9B06

---
How does the feed point impedance of a 1/2 wave dipole antenna change as the antenna is lowered below 1/4 wave above ground?
How does the feed point impedance of a 1/2 wave dipole antenna change as the antenna is lowered below 1/4 wave above ground?
A. It steadily increases
B. It steadily decreases
C. It peaks at about 1/8 wavelength above ground
D. It is unaffected by the height above ground
  G9B07

---
How does the feed point impedance of a 1/2 wave dipole antenna change as the antenna is lowered below 1/4 wave above ground?
A. It steadily increases
B. It steadily decreases
C. It peaks at about 1/8 wavelength above ground
D. It is unaffected by the height above ground
  G9B07

---
How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends?
How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends?
A. It steadily increases
B. It steadily decreases
C. It peaks at about 1/8 wavelength from the end
D. It is unaffected by the location of the feed point
  G9B08

---
How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends?
A. It steadily increases
B. It steadily decreases
C. It peaks at about 1/8 wavelength from the end
D. It is unaffected by the location of the feed point
  G9B08

---
Which of the following is an advantage of a horizontally polarized as compared to a vertically polarized HF antenna?
Which of the following is an advantage of a horizontally polarized as compared to a vertically polarized HF antenna?
A. Lower ground reflection losses
B. Lower feed point impedance
C. Shorter Radials
D. Lower radiation resistance
  G9B09

---
Which of the following is an advantage of a horizontally polarized as compared to a vertically polarized HF antenna?
A. Lower ground reflection losses
B. Lower feed point impedance
C. Shorter Radials
D. Lower radiation resistance
  G9B09

---
What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz?
What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz?
A. 8 feet
B. 16 feet
C. 24 feet
D. 32 feet
  G9B10

---
What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz?
A. 8 feet
B. 16 feet
C. 24 feet
D. 32 feet
  G9B10

---
What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz?
What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz?
A. 42 feet
B. 84 feet
C. 131 feet
D. 263 feet
  G9B11

---
What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz?
A. 42 feet
B. 84 feet
C. 131 feet
D. 263 feet
  G9B11

---
What is the approximate length for a 1/4 wave vertical antenna cut for 28.5 MHz?
What is the approximate length for a 1/4 wave vertical antenna cut for 28.5 MHz?
A. 8 feet
B. 11 feet
C. 16 feet
D. 21 feet
  G9B12

---
What is the approximate length for a 1/4 wave vertical antenna cut for 28.5 MHz?
A. 8 feet
B. 11 feet
C. 16 feet
D. 21 feet
  G9B12

---
General License Course
Chapter 7
Lesson Plan Module 30 –
Yagi Antennas

---
How Yagis Work
Yagi – the most popular directional antenna
Yagi antennas reduce interference: signals, noise from unwanted directions
Rear and sides by more than 20 dB
The Yagi is an array antenna with multiple elements
Array antennas create a maximum field strength in a specific direction (main or major lobe)
[Speaker Notes: Notes area]

---
How Yagis Work
Yagi elements:
Driven – element connected to the feed line
Parasitic – one or more elements not connected to the feed line that influence the antenna’s radiated and receive pattern
Parasitic arrays – energy from the driven element induces a current to flow in the parasitic elements which is reradiated as part of the antenna’s total signal
[Speaker Notes: Notes area]

---
Yagi Structure & Function
A Yagi antenna has a driven element and at least one parasitic element
Driven element – about the same as a resonant dipole
Director elements – reinforce signals in a single main lobe (shorter than the driven element)
Reflectors – cancel signals to the rear (longer than the driven element)
Front-to-back ratio is the ratio of signal strength at the peak of the radiation pattern’s major lobe to that in exactly the opposite direction
[Speaker Notes: Also describe front-to-side and front-to-rear ratios.]

---
Yagi Structure
The simplest Yagi is a two-element antenna with a driven element (DE) and either a reflector (usually) or a director.
DE is approx. a λ/2 dipole
Reflector element is about 5% longer than the driven element and placed behind the DE by 0.15-0.2 λ
Director element is about 5% shorter than the driven element and placed ahead of the DE by 0.15-0.2 λ
[Speaker Notes: The Yagi works by the fields from the DE and the reflectors and directors combining to focus energy in the desired direction. The focusing action results from the combination of: time delays from the DE to the other elements the additional phase change caused by the parasitic elements being longer (inductive) or shorter (capacitive) than resonant, and the 180-degree phase shift for energy that is re-radiated by the parasitic elements When all of these effects are accounted for, the result is that the antenna becomes directional on both transmit and receive.]

---
Design Tradeoffs
Primary element design variables: length, spacing along the boom, thickness
Placement and length of the elements affects gain, tuning, and pattern
Longer boom with a fixed number of directors increases gain
Larger diameter elements reduces SWR and increases SWR bandwidth
Antenna modeling software used to optimize the antenna design
[Speaker Notes: Notes area]

---
Impedance Matching
Many Yagi designs have a feed point impedance of 20-25 ohms requiring matching
Gamma matching is a popular technique
Section of parallel conductor transmission line using the driven element as one of its conductors
A mechanical advantage - the driven element doesn’t have to be insulated from the boom
Tuning by adjusting length of the transmission line or a series capacitor
[Speaker Notes: Mention other techniques – hairpin or beta match, omega match, transmission line stubs. Also possible to design Yagi to have a 50Ω feed point impedance using computer techniques, becoming more popular.]

---
Practice Questions
[Speaker Notes: Notes area]

---
Which HF antenna would be the best to use for minimizing interference?
Which HF antenna would be the best to use for minimizing interference?
A. A quarter-wave vertical antenna
B. An isotropic antenna
C. A directional antenna
D. An omnidirectional antenna
  G2D11

---
Which HF antenna would be the best to use for minimizing interference?
A. A quarter-wave vertical antenna
B. An isotropic antenna
C. A directional antenna
D. An omnidirectional antenna
  G2D11

---
Which of the following would increase the bandwidth of a Yagi antenna?
Which of the following would increase the bandwidth of a Yagi antenna?
A. Larger diameter elements
B. Closer element spacing
C. Loading coils in series with the element
D. Tapered-diameter elements
  G9C01

---
Which of the following would increase the bandwidth of a Yagi antenna?
A. Larger diameter elements
B. Closer element spacing
C. Loading coils in series with the element
D. Tapered-diameter elements
  G9C01

---
What is the approximate length of the driven element of a Yagi antenna?
What is the approximate length of the driven element of a Yagi antenna?
A. 1/4 wavelength
B. 1/2 wavelength
C. 3/4 wavelength
D. 1 wavelength
  G9C02

---
What is the approximate length of the driven element of a Yagi antenna?
A. 1/4 wavelength
B. 1/2 wavelength
C. 3/4 wavelength
D. 1 wavelength
  G9C02

---
Which statement about a three-element, single-band Yagi antenna is true?
Which statement about a three-element, single-band Yagi antenna is true?
A. The reflector is normally the shortest element
B. The director is normally the shortest element
C. The driven element is the longest element
D. Low feed point impedance increases bandwidth
  G9C03

---
Which statement about a three-element, single-band Yagi antenna is true?
A. The reflector is normally the shortest element
B. The director is normally the shortest element
C. The driven element is the longest element
D. Low feed point impedance increases bandwidth
  G9C03

---
Which statement about a three-element, single-band Yagi antenna is true?
A. The reflector is normally the longest element
B. The director is normally the longest element
C. The reflector is normally the shortest element
D. All of the elements must be the same length
  G9C04

---
Which statement about a three-element, single-band Yagi antenna is true?
A. The reflector is normally the longest element
B. The director is normally the longest element
C. The reflector is normally the shortest element
D. All of the elements must be the same length
  G9C04

---
How does increasing boom length and adding directors affect a Yagi antenna?
How does increasing boom length and adding directors affect a Yagi antenna?
A. Gain increases
B. Beamwidth increases
C. Front to back ratio decreases
D. Front to side ratio decreases
  G9C05

---
How does increasing boom length and adding directors affect a Yagi antenna?
A. Gain increases
B. Beamwidth increases
C. Front to back ratio decreases
D. Front to side ratio decreases
  G9C05

---
What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector?
What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector?
A. The driven element must be fed with a balun transformer
B. There must be an open circuit in the driven element at the point opposite the feed point
C. The reflector element must be approximately 5 percent shorter than the driven element
D. The reflector element must be approximately 5 percent longer than the driven element
  G9C06

---
What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector?
A. The driven element must be fed with a balun transformer
B. There must be an open circuit in the driven element at the point opposite the feed point
C. The reflector element must be approximately 5 percent shorter than the driven element
D. The reflector element must be approximately 5 percent longer than the driven element
  G9C06

---
What does “front-to-back ratio” mean in reference to a Yagi antenna?
What does “front-to-back ratio” mean in reference to a Yagi antenna?
A. The number of directors versus the number of reflectors
B. The relative position of the driven element with respect to the reflectors and directors
C. The power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction
D. The ratio of forward gain to dipole gain
  G9C07

---
What does “front-to-back ratio” mean in reference to a Yagi antenna?
A. The number of directors versus the number of reflectors
B. The relative position of the driven element with respect to the reflectors and directors
C. The power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction
D. The ratio of forward gain to dipole gain
  G9C07

---
What is meant by the “main lobe” of a directive antenna?
What is meant by the “main lobe” of a directive antenna?
A. The magnitude of the maximum vertical angle of radiation
B. The point of maximum current in a radiating antenna element
C. The maximum voltage standing wave point on a radiating element
D. The direction of maximum radiated field strength from the antenna
  G9C08

---
What is meant by the “main lobe” of a directive antenna?
A. The magnitude of the maximum vertical angle of radiation
B. The point of maximum current in a radiating antenna element
C. The maximum voltage standing wave point on a radiating element
D. The direction of maximum radiated field strength from the antenna
  G9C08

---
Which of the following is a Yagi antenna design variable that could be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth?
Which of the following is a Yagi antenna design variable that could be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth?
A. The physical length of the boom
B. The number of elements on the boom
C. The spacing of each element along the boom
D. All of these choices are correct
  G9C10

---
Which of the following is a Yagi antenna design variable that could be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth?
A. The physical length of the boom
B. The number of elements on the boom
C. The spacing of each element along the boom
D. All of these choices are correct
  G9C10

---
What is the purpose of a gamma match used with Yagi antennas?
What is the purpose of a gamma match used with Yagi antennas?
A. To match the relatively low feed point impedance to 50 ohms
B. To match the relatively high feed point impedance to 50 ohms
C. To increase the front-to-back ratio
D. To increase the main lobe gain
  G9C11

---
What is the purpose of a gamma match used with Yagi antennas?
A. To match the relatively low feed point impedance to 50 ohms
B. To match the relatively high feed point impedance to 50 ohms
C. To increase the front-to-back ratio
D. To increase the main lobe gain
  G9C11

---
Which of the following is an advantage of using a gamma match for impedance matching of a Yagi antenna to 50 ohm coax feed line?
Which of the following is an advantage of using a gamma match for impedance matching of a Yagi antenna to 50 ohm coax feed line?
A. It does not require that the elements be insulated from the boom
B. It does not require any inductors or capacitors
C. It is useful for matching multiband antennas
D. All of these choices are correct
  G9C12

---
Which of the following is an advantage of using a gamma match for impedance matching of a Yagi antenna to 50 ohm coax feed line?
A. It does not require that the elements be insulated from the boom
B. It does not require any inductors or capacitors
C. It is useful for matching multiband antennas
D. All of these choices are correct
  G9C12

---
General License Course
Chapter 7
Lesson Plan Module 31 –
Loop Antennas

---
Loop Antennas
Loops are one wavelength or more in circumference (circular, square, triangular)
Quad (Delta) – square (triangular) with λ/4 (λ/3) sides
Loops can be mounted vertically or horizontally
Strongest signal is broadside to a 1λ loop, about the same gain as a dipole
Horizontal loops radiate straight up at fundamental, lower angles on harmonics, with horizontal polarization
[Speaker Notes: Notes area]

---
Quad or Delta Loop Beams
A two element Quad or Delta loop beam operates similarly to and has about the same gain as a 3-element Yagi
Reflectors 5% longer in circumference than the driven element
Attaching the feed point to the bottom or top of a quad results in horizontal polarization
Attaching the feed point to the side of a quad results in vertical polarization
Front-to-back and side is generally less than for a Yagi
[Speaker Notes: Notes area]

---
Practice Questions
[Speaker Notes: Notes area]

---
What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector?
A. The driven element must be fed with a balun transformer
B. There must be an open circuit in the driven element at the point opposite the feed point
C. The reflector element must be approximately 5 percent shorter than the driven element
D. The reflector element must be approximately 5 percent longer than the driven element
  G9C06

---
What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector?
A. The driven element must be fed with a balun transformer
B. There must be an open circuit in the driven element at the point opposite the feed point
C. The reflector element must be approximately 5 percent shorter than the driven element
D. The reflector element must be approximately 5 percent longer than the driven element
  G9C06

---
Approximately how long is each side of the driven element of a quad antenna?
Approximately how long is each side of the driven element of a quad antenna?
A. 1/4 wavelength
B. 1/2 wavelength
C. 3/4 wavelength
D. 1 wavelength
  G9C13

---
Approximately how long is each side of the driven element of a quad antenna?
A. 1/4 wavelength
B. 1/2 wavelength
C. 3/4 wavelength
D. 1 wavelength
  G9C13

---
How does the forward gain of a two-element quad antenna compare to the forward gain of a three-element Yagi antenna?
How does the forward gain of a two-element quad antenna compare to the forward gain of a three-element Yagi antenna?
A. About 2/3 as much
B. About the same
C. About 1.5 times as much
D. About twice as much
  G9C14

---
How does the forward gain of a two-element quad antenna compare to the forward gain of a three-element Yagi antenna?
A. About 2/3 as much
B. About the same
C. About 1.5 times as much
D. About twice as much
  G9C14

---
Approximately how long is each side of the reflector element of a quad antenna?
Approximately how long is each side of the reflector element of a quad antenna?
A. Slightly less than 1/4 wavelength
B. Slightly more than 1/4 wavelength
C. Slightly less than 1/2 wavelength
D. Slightly more than 1/2 wavelength
  G9C15

---
Approximately how long is each side of the reflector element of a quad antenna?
A. Slightly less than 1/4 wavelength
B. Slightly more than 1/4 wavelength
C. Slightly less than 1/2 wavelength
D. Slightly more than 1/2 wavelength
  G9C15

---
How does the gain of a two-element delta-loop beam compare to the gain of a two-element quad antenna?
How does the gain of a two-element delta-loop beam compare to the gain of a two-element quad antenna?
A. 3 dB higher
B. 3 dB lower
C. 2.54 dB higher
D. About the same
  G9C16

---
How does the gain of a two-element delta-loop beam compare to the gain of a two-element quad antenna?
A. 3 dB higher
B. 3 dB lower
C. 2.54 dB higher
D. About the same
  G9C16

---
Approximately how long is each leg of a symmetrical delta-loop antenna?
Approximately how long is each leg of a symmetrical delta-loop antenna?
A. 1/4 wavelength
B. 1/3 wavelength
C. 1/2 wavelength
D. 2/3 wavelength
  G9C17

---
Approximately how long is each leg of a symmetrical delta-loop antenna?
A. 1/4 wavelength
B. 1/3 wavelength
C. 1/2 wavelength
D. 2/3 wavelength
  G9C17

---
What happens when the feed point of a quad antenna of any shape is moved from the midpoint of the top or bottom to the midpoint of either side?
What happens when the feed point of a quad antenna of any shape is moved from the midpoint of the top or bottom to the midpoint of either side?
A. The polarization of the radiated signal changes from horizontal to vertical
B. The polarization of the radiated signal changes from vertical to horizontal
C. There is no change in polarization
D. The radiated signal becomes circularly polarized
  G9C18

---
What happens when the feed point of a quad antenna of any shape is moved from the midpoint of the top or bottom to the midpoint of either side?
A. The polarization of the radiated signal changes from horizontal to vertical
B. The polarization of the radiated signal changes from vertical to horizontal
C. There is no change in polarization
D. The radiated signal becomes circularly polarized
  G9C18

---
General License Course
Chapter 7
Lesson Plan Module 32 –
Specialized Antennas

---
Specialized Antennas
NVIS (Near-Vertical Incidence Sky-wave) – antenna radiates mostly straight up to the ionosphere where it’s reflected back down to Earth over a wide area
Pattern covers a geographic area of only a few hundred kilometers across
Used for disaster communications
Typically a simple λ/2 dipole
The best height is between 1⁄10 and ¼ wavelengths above ground
[Speaker Notes: Notes area]

---
Specialized Antennas
Stacked Antennas – a pair of identical antennas stacked above or beside each other to increase gain
Vertical stacking increases gain and narrows the elevation beamwidth
Most vertical stacks are about ½ wavelength to 1 wavelength apart
dBi – relative to isotropic
dBd – relative to a dipole (dBd = dBi – 2.15)
[Speaker Notes: Manufacturer’s should specify what the reference is when stating gain specifications – isotropic or dipole]

---
Specialized Antennas
Stacking 2 beams ½ wavelength apart increases gain by 3 dB
Gain another 3 dB by stacking 4 beam antennas
Stacking narrows the pattern beamwidth
[Speaker Notes: Notes area]

---
Specialized Antennas
Log Periodics – are designed to have consistent radiation pattern and SWR across a wide (up to 10:1) frequency range
Short elements are active at higher frequencies
Longer elements are active at lower frequencies
Log periodic antennas less gain or front-to-back ratio than Yagi antennas
The length and spacing of the elements increases logarithmically from one end to the other
[Speaker Notes: Log periodics are good choices when only one antenna can be installed to cover a wide frequency range, such as all five ham bands from 20-10 meters or a TV antenna.]

---
Specialized Antennas
Beverage antenna – receiving antenna
Beverage antennas are very inefficient but do a good job of rejecting noise
A Beverage antenna is a long (1λ or longer), low wire (less than 20 ft high) pointed in a preferred signal direction
The Beverage works by rejecting more noise than signal (traveling wave antenna)
[Speaker Notes: Stress that the goal of the Beverage is to reduce noise, not necessarily increase gain. The result is an improved signal-to-noise ratio.]

---
Multiband Antennas
A half-wave dipole antenna can be used on its odd harmonics without a tuner (radiate harmonics)
Trapped dipole is a common multiband antenna (40/80 meter dipole)
The traps act as electrical switches to isolate parts of the antenna
Act as inductors or capacitors below or above the resonant frequency
Triband Yagi (10-15-20 meters) trapped or separate elements for each frequency range
[Speaker Notes: Notes area]

---
You can make traps fairly easily using RG58 coax and
an interesting way to wire them….I’ve made quite
a few.

---
Practice Questions
[Speaker Notes: Notes area]

---
What is meant by the terms dBi and dBd when referring to antenna gain?
A. dBi refers to an isotropic antenna, dBd refers to a dipole antenna
B. dBi refers to an ionospheric reflecting antenna, dBd refers to a dissipative antenna
C. dBi refers to an inverted-vee antenna, dBd refers to a downward reflecting antenna
D. dBi refers to an isometric antenna, dBd refers to a discone antenna
  G9C20

---
What is meant by the terms dBi and dBd when referring to antenna gain?
A. dBi refers to an isotropic antenna, dBd refers to a dipole antenna
B. dBi refers to an ionospheric reflecting antenna, dBd refers to a dissipative antenna
C. dBi refers to an inverted-vee antenna, dBd refers to a downward reflecting antenna
D. dBi refers to an isometric antenna, dBd refers to a discone antenna
  G9C20

---
What does the term NVIS mean as related to antennas?
What does the term NVIS mean as related to antennas?
A. Nearly Vertical Inductance System
B. Non-Varying Indicated SWR
C. Non-Varying Impedance Smoothing
D. Near Vertical Incidence sky-wave
  G9D01

---
What does the term NVIS mean as related to antennas?
A. Nearly Vertical Inductance System
B. Non-Varying Indicated SWR
C. Non-Varying Impedance Smoothing
D. Near Vertical Incidence sky-wave
  G9D01

---
Which of the following is an advantage of an NVIS antenna?
Which of the following is an advantage of an NVIS antenna?
A. Low vertical angle radiation for working stations out to ranges of several thousand kilometers
B. High vertical angle radiation for working stations within a radius of a few hundred kilometers
C. High forward gain
D. All of these choices are correct
  G9D02

---
Which of the following is an advantage of an NVIS antenna?
A. Low vertical angle radiation for working stations out to ranges of several thousand kilometers
B. High vertical angle radiation for working stations within a radius of a few hundred kilometers
C. High forward gain
D. All of these choices are correct
  G9D02

---
At what height above ground is an NVIS antenna typically installed?
At what height above ground is an NVIS antenna typically installed?
A. As close to 1/2 wavelength as possible
B. As close to one wavelength as possible
C. Height is not critical as long as it is significantly more than 1/2 wavelength
D. Between 1/10 and 1/4 wavelength
  G9D03

---
At what height above ground is an NVIS antenna typically installed?
A. As close to 1/2 wavelength as possible
B. As close to one wavelength as possible
C. Height is not critical as long as it is significantly more than 1/2 wavelength
D. Between 1/10 and 1/4 wavelength
  G9D03

---
What is the primary purpose of antenna traps?
What is the primary purpose of antenna traps?
A. To permit multiband operation
B. To notch spurious frequencies
C. To provide balanced feed point impedance
D. To prevent out of band operation
  G9D04

---
What is the primary purpose of antenna traps?
A. To permit multiband operation
B. To notch spurious frequencies
C. To provide balanced feed point impedance
D. To prevent out of band operation
  G9D04

---
What is an advantage of vertical stacking of horizontally polarized Yagi antennas?
What is an advantage of vertical stacking of horizontally polarized Yagi antennas?
A. It allows quick selection of vertical or horizontal polarization
B. It allows simultaneous vertical and horizontal polarization
C. It narrows the main lobe in azimuth
D. It narrows the main lobe in elevation
  G9D05

---
What is an advantage of vertical stacking of horizontally polarized Yagi antennas?
A. It allows quick selection of vertical or horizontal polarization
B. It allows simultaneous vertical and horizontal polarization
C. It narrows the main lobe in azimuth
D. It narrows the main lobe in elevation
  G9D05

---
How does the gain of two 3-element horizontally polarized Yagi antennas spaced vertically 1/2 wavelength apart typically compare to the gain of a single 3-element Yagi?
How does the gain of two 3-element horizontally polarized Yagi antennas spaced vertically 1/2 wavelength apart typically compare to the gain of a single 3-element Yagi?
A. Approximately 1.5 dB higher
B. Approximately 3 dB higher
C. Approximately 6 dB higher
D. Approximately 9 dB higher
  G9C09

---
How does the gain of two 3-element horizontally polarized Yagi antennas spaced vertically 1/2 wavelength apart typically compare to the gain of a single 3-element Yagi?
A. Approximately 1.5 dB higher
B. Approximately 3 dB higher
C. Approximately 6 dB higher
D. Approximately 9 dB higher
  G9C09
Double the “volume” of an antenna and the gain goes
up by 3 db. You’ll see the same thing with parabolics.

---
Which of the following is an advantage of a log periodic antenna?
Which of the following is an advantage of a log periodic antenna?
A. Wide bandwidth
B. Higher gain per element than a Yagi antenna
C. Harmonic suppression
D. Polarization diversity
  G9D06

---
Which of the following is an advantage of a log periodic antenna?
A. Wide bandwidth
B. Higher gain per element than a Yagi antenna
C. Harmonic suppression
D. Polarization diversity
  G9D06

---
Which of the following describes a log periodic antenna?
Which of the following describes a log periodic antenna?
A. Length and spacing of the elements increase logarithmically from one end of the boom to the other
B. Impedance varies periodically as a function of frequency
C. Gain varies logarithmically as a function of frequency
D. SWR varies periodically as a function of boom length
  G9D07

---
Which of the following describes a log periodic antenna?
A. Length and spacing of the elements increase logarithmically from one end of the boom to the other
B. Impedance varies periodically as a function of frequency
C. Gain varies logarithmically as a function of frequency
D. SWR varies periodically as a function of boom length
  G9D07

---
Why is a Beverage antenna not used for transmitting?
Why is a Beverage antenna not used for transmitting?
A. Its impedance is too low for effective matching
B. It has high losses compared to other types of antennas
C. It has poor directivity
D. All of these choices are correct
  G9D08

---
Why is a Beverage antenna not used for transmitting?
A. Its impedance is too low for effective matching
B. It has high losses compared to other types of antennas
C. It has poor directivity
D. All of these choices are correct
  G9D08

---
Which of the following is an application for a Beverage antenna?
Which of the following is an application for a Beverage antenna?
A. Directional transmitting for low HF bands
B. Directional receiving for low HF bands
C. Portable direction finding at higher HF frequencies
D. Portable direction finding at lower HF frequencies
  G9D09

---
Which of the following is an application for a Beverage antenna?
A. Directional transmitting for low HF bands
B. Directional receiving for low HF bands
C. Portable direction finding at higher HF frequencies
D. Portable direction finding at lower HF frequencies
  G9D09

---
Which of the following describes a Beverage antenna?
Which of the following describes a Beverage antenna?
A. A vertical antenna
B. A broad-band mobile antenna
C. A helical antenna for space reception
D. A very long and low directional receiving antenna
  G9D10

---
Which of the following describes a Beverage antenna?
A. A vertical antenna
B. A broad-band mobile antenna
C. A helical antenna for space reception
D. A very long and low directional receiving antenna
  G9D10

---
Which of the following is a disadvantage of multiband antennas?
Which of the following is a disadvantage of multiband antennas?
A. They present low impedance on all design frequencies
B. They must be used with an antenna tuner
C. They must be fed with open wire line
D. They have poor harmonic rejection
  G9D11

---
Which of the following is a disadvantage of multiband antennas?
A. They present low impedance on all design frequencies
B. They must be used with an antenna tuner
C. They must be fed with open wire line
D. They have poor harmonic rejection
  G9D11

---
General License Course
Chapter 7
Lesson Plan Module 33 –
Feed Lines

---
Types of Feed Lines
lowest loss
[Speaker Notes: Notes area]

---
Feed Lines
Characteristic impedance (Z0) is determined by the geometry of the feed line conductors and the material and distance between them
The most common impedances of coax that amateurs use are 50  and 75 
Open wire feed line has impedances from 300 to 600 Ω
TV-type twin lead has a characteristic impedance of 300 
[Speaker Notes: Notes area]

---
Feed Lines
Forward power – power traveling toward a load or antenna
Reflected power – power reflected from an impedance mismatch at the load or antenna
Standing waves – interference wave pattern in a feed line from forward and reverse power
Standing wave ratio (SWR) ratio between the peak and minimum voltage of the wave pattern
SWR equals ratio of load or antenna Z and Z0 of the feed line, whichever is greater than 1
Short or open: SWR = ∞ and all power reflected
[Speaker Notes: Notes area]

---
Calculating SWR
Example 5: What is the SWR in a 50  feed line connected to a 200  load?
SWR = 200/50 = 4:1
Example 6: What is the SWR in a 50  feed line connected to a 10  load?
SWR = 50/10 = 5:1
Example 7: What standing wave ratio will result from the connection of a 50  feed line to a non-reactive load having a 50  impedance?
SWR = 50/50 = 1:1
[Speaker Notes: Notes area]

---
Calculating SWR
Example 8: What should be the SWR if you feed a vertical antenna that has a 25  feed point impedance with 50  coaxial cable?
SWR = 50/25 = 2:1
Example 9: What would be the SWR if you feed an antenna that has a 300  feed point impedance with 50  coaxial cable?
SWR = 300/50 = 6:1
[Speaker Notes: Notes area]

---
Feed Lines
Impedance matching – matching the feed line and load (antenna) eliminates standing waves
Performed at the transmitter to match antenna system impedance to that of the transmitter
[Speaker Notes: Stress that when the impedance matching is performed at the transmitter, the SWR in the feed line is unchanged.]

---
Feed Line Loss
Loss is measured in dB /100 ft of cable
Loss increases with frequency
Small coax has higher loss at a given frequency
[Speaker Notes: Note that because SWR results in power being reflected and making multiple trips through the line before being transferred to the antenna, high SWR means more signal loss.]

---
Practice Questions
[Speaker Notes: Notes area]

---
What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms?
What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms?
A. Balanced modulator
B. SWR Bridge
C. Antenna coupler or antenna tuner
D. Q Multiplier
  G4A06

---
What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms?
A. Balanced modulator
B. SWR Bridge
C. Antenna coupler or antenna tuner
D. Q Multiplier
  G4A06

---
Which of the following factors determine the characteristic impedance of a parallel conductor antenna feed line?
Which of the following factors determine the characteristic impedance of a parallel conductor antenna feed line?
A. The distance between the centers of the conductors and the radius of the conductors
B. The distance between the centers of the conductors and the length of the line
C. The radius of the conductors and the frequency of the signal
D. The frequency of the signal and the length of the line
  G9A01

---
Which of the following factors determine the characteristic impedance of a parallel conductor antenna feed line?
A. The distance between the centers of the conductors and the radius of the conductors
B. The distance between the centers of the conductors and the length of the line
C. The radius of the conductors and the frequency of the signal
D. The frequency of the signal and the length of the line
  G9A01

---
What are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations?
What are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations?
A. 25 and 30 ohms
B. 50 and 75 ohms
C. 80 and 100 ohms
D. 500 and 750 ohms
  G9A02

---
What are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations?
A. 25 and 30 ohms
B. 50 and 75 ohms
C. 80 and 100 ohms
D. 500 and 750 ohms
  G9A02

---
What is the characteristic impedance of flat ribbon TV type twinlead?
What is the characteristic impedance of flat ribbon TV type twinlead?
A. 50 ohms
B. 75 ohms
C. 100 ohms
D. 300 ohms
  G9A03

---
What is the characteristic impedance of flat ribbon TV type twinlead?
A. 50 ohms
B. 75 ohms
C. 100 ohms
D. 300 ohms
  G9A03

---
What might cause reflected power at the point where a feed line connects to an antenna?
What might cause reflected power at the point where a feed line connects to an antenna?
A. Operating an antenna at its resonant frequency
B. Using more transmitter power than the antenna can handle
C. A difference between feed line impedance and antenna feed point impedance
D. Feeding the antenna with unbalanced feed line
  G9A04

---
What might cause reflected power at the point where a feed line connects to an antenna?
A. Operating an antenna at its resonant frequency
B. Using more transmitter power than the antenna can handle
C. A difference between feed line impedance and antenna feed point impedance
D. Feeding the antenna with unbalanced feed line
  G9A04

---
How does the attenuation of coaxial cable change as the frequency of the signal it is carrying increases?
How does the attenuation of coaxial cable change as the frequency of the signal it is carrying increases?
A. Attenuation is independent of frequency
B. Attenuation increases
C. Attenuation decreases
D. Attenutation reaches a maximum at approximately 18 MHz
  G9A05

---
How does the attenuation of coaxial cable change as the frequency of the signal it is carrying increases?
A. Attenuation is independent of frequency
B. Attenuation increases
C. Attenuation decreases
D. Attenutation reaches a maximum at approximately 18 MHz
  G9A05

---
In what units is RF feed line loss usually expressed?
In what units is RF feed line loss usually expressed?
A. Ohms per 1000 feet
B. Decibels per 1000 feet
C. Ohms per 100 feet
D. Decibels per 100 feet
  G9A06

---
In what units is RF feed line loss usually expressed?
A. Ohms per 1000 feet
B. Decibels per 1000 feet
C. Ohms per 100 feet
D. Decibels per 100 feet
  G9A06

---
What must be done to prevent standing waves on an antenna feed line?
What must be done to prevent standing waves on an antenna feed line?
A. The antenna feed point must be at DC ground potential
B. The feed line must be cut to a length equal to an odd number of electrical quarter wavelengths
C. The feed line must be cut to a length equal to an even number of physical half wavelengths
D. The antenna feed point impedance must be matched to the characteristic impedance of the feed line
  G9A07

---
What must be done to prevent standing waves on an antenna feed line?
A. The antenna feed point must be at DC ground potential
B. The feed line must be cut to a length equal to an odd number of electrical quarter wavelengths
C. The feed line must be cut to a length equal to an even number of physical half wavelengths
D. The antenna feed point impedance must be matched to the characteristic impedance of the feed line
  G9A07

---
If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, what is the resulting SWR on the feed line?
If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, what is the resulting SWR on the feed line?
A. 1 to 1
B. 5 to 1
C. Between 1 to 1 and 5 to 1 depending on the characteristic impedance of the line
D. Between 1 to 1 and 5 to 1 depending on the reflected power at the transmitter
  G9A08

---
If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, what is the resulting SWR on the feed line?
A. 1 to 1
B. 5 to 1
C. Between 1 to 1 and 5 to 1 depending on the characteristic impedance of the line
D. Between 1 to 1 and 5 to 1 depending on the reflected power at the transmitter
  G9A08

---
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance?
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance?
A. 4:1
B. 1:4
C. 2:1
D. 1:2
  G9A09

---
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance?
A. 4:1
B. 1:4
C. 2:1
D. 1:2
  G9A09

---
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 10 ohm impedance?
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 10 ohm impedance?
A. 2:1
B. 50:1
C. 1:5
D. 5:1
  G9A10

---
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 10 ohm impedance?
A. 2:1
B. 50:1
C. 1:5
D. 5:1
  G9A10

---
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 50 ohm impedance?
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 50 ohm impedance?
A. 2:1
B. 1:1
C. 50:50
D. 0:0
  G9A11

---
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 50 ohm impedance?
A. 2:1
B. 1:1
C. 50:50
D. 0:0
  G9A11

---
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 25 ohm impedance?
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 25 ohm impedance?
A. 2:1
B. 2.5:1
C. 1.25:1
D. You cannot determine SWR from impedance values
  G9A12

---
What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 25 ohm impedance?
A. 2:1
B. 2.5:1
C. 1.25:1
D. You cannot determine SWR from impedance values
  G9A12

---
What standing wave ratio will result when connecting a 50 ohm feed line to an antenna that has a purely resistive 300 ohm feed point impedance?
What standing wave ratio will result when connecting a 50 ohm feed line to an antenna that has a purely resistive 300 ohm feed point impedance?
A. 1.5:1
B. 3:1
C. 6:1
D. You cannot determine SWR from impedance values
  G9A13

---
What standing wave ratio will result when connecting a 50 ohm feed line to an antenna that has a purely resistive 300 ohm feed point impedance?
A. 1.5:1
B. 3:1
C. 6:1
D. You cannot determine SWR from impedance values
  G9A13

---
What is the interaction between high standing wave ratio (SWR) and transmission line loss?
What is the interaction between high standing wave ratio (SWR) and transmission line loss?
A. There is no interaction between transmission line loss and SWR
B. If a transmission line is lossy, high SWR will increase the loss
C. High SWR makes it difficult to measure transmission line loss
D. High SWR reduces the relative effect of transmission line loss
  G9A14

---
What is the interaction between high standing wave ratio (SWR) and transmission line loss?
A. There is no interaction between transmission line loss and SWR
B. If a transmission line is lossy, high SWR will increase the loss
C. High SWR makes it difficult to measure transmission line loss
D. High SWR reduces the relative effect of transmission line loss
  G9A14

---
What is the effect of transmission line loss on SWR measured at the input to the line?
What is the effect of transmission line loss on SWR measured at the input to the line?
A. The higher the transmission line loss, the more the SWR will read artificially low
B. The higher the transmission line loss, the more the SWR will read artificially high
C. The higher the transmission line loss, the more accurate the SWR measurement will be
D. Transmission line loss does not affect the SWR measurement
  G9A15

---
What is the effect of transmission line loss on SWR measured at the input to the line?
A. The higher the transmission line loss, the more the SWR will read artificially low
B. The higher the transmission line loss, the more the SWR will read artificially high
C. The higher the transmission line loss, the more accurate the SWR measurement will be
D. Transmission line loss does not affect the SWR measurement
  G9A15