## Slide 1: CHAPTER 2
Radio and Signal
Fundamentals

## Slide 2: Background and concepts

## Slide 3: Wavelength vs Frequency
The distance a radio wave travels in one cycle is called wavelength
The number of cycles per second is frequency
The maximum displacement of wave from reference value is amplitude
One Wavelength
Time
V+
V-
0V
One Cycle
Amplitude

## Slide 4: Frequency to Wavelength Conversion
300
Freq (MHz)
Wavelength =
To convert from frequency to wavelength in meters:
Frequency and wavelength are inversely proportional – as one increases, the other decreases
Longer (wavelength) Lower (frequency)

## Slide 5: Units of Measure
Power | Watt
Resistance | Ohm
Voltage | Volt
Current | Ampere
Frequency | Hertz

## Slide 6
109 106 103 102 101 100 10-1 10-2 10-3 10-6 10-9
G M k h da d c m µ n
giga mega kilo hecto deca deci centi milli micro nano
Metric Units of Measure
Gigahertz | 1,000,000,000
Megahertz | 1,000,000
Kilohertz | 1,000
Hertz | 1
Ampere | 1
Milliampere | 0.001
Microampere | 0.000001
Nanoampere | 0.000000001
Billions
Millions
Thousands
Hundreds
Tens
Tenths
Thousandths
Hundredths
Millionths
Billionths
Notes: Note the shift in decimal places. This is standard metric notation. 1 Gigahertz is 1 Billion Hertz and a Nanoampere is 1 Billionth of an Ampere.

## Slide 7: Voltage, Current, Resistance
+
-
Voltage
Current
Resistance (Load)
You need a circuit for electricity to flow
Components of a circuit: Source, Conductors, Load, Sink (Ground)
Notes: Voltage is also called Electromotive Force and is an electrical “pressure”. Current is a measure of the flow of electrons (volume) from the negative to positive poles. The load presents resistance to the flow of electrons. Voltage is measured across the positive and negative poles (in parallel) to measure the difference in “pressure”. To measure the electron flow, the meter must be placed in-line (in series) with the flow.
Direct Current (DC) is a constant voltage source that causes current to flow in only one direction and has a positive and negative pole – like a battery. Alternating Current is what is available in the wall and the constantly changing polarity causes current to alternate directions.

## Slide 8: Radio Spectrum
Medium Wave (MF) | Short Wave (HF) | Very High Frequency (VHF) | Ultra High Frequency (UHF)
AM Broadcast
540
1630
TV 2-6
54
88
FM Broadcast
108
TV 7-13
174
216
TV 14-69
470
806
300 kHz
3 MHz
30 MHz
300 MHz
3 GHz
Frequency
1 Km
100 m
10 m
1 m
10 cm
Wavelength
Major Amateur Bands in Amber

## Slide 9: Sample Emission Modes
Mode | Type | Bandwidth | Content
CW | Telegraphy | 10 Hz | Text Data
SSB | Telephony | 2800 Hz | Voice
AM | Telephony | 6 kHz | Voice
FM | Telephony | 5-15 kHz | Voice
SSTV / Fax | Image | 2800 Hz | Image
ATV | Image | 6 MHz | Image
PSK31 | Data | 31 Hz | Text Data
RTTY | Data | 250 Hz | Text Data
Pactor (I, II, III) | Data | 500-2800 Hz | Binary Data
AX.25 Packet | Data | 10-20 kHz | Binary Data

## Slide 10: Amplitude Modulation
An unmodulated RF
carrier wave
A carrier wave amplitude
modulated (AM) with a simple audio tone
Notes: Note the identical sidebands. They peak and dip together.

## Slide 11: Amplitude Modulation
An unmodulated RF
carrier requires narrow
bandwidth
Modulation of the carrier
creates sidebands. This
requires more bandwidth.
Transmitter power is spread across this bandwidth

## Slide 12: AM and SSB
The carrier contains no
audio information.
The sidebands contain
duplicate audio information
By filtering out the carrier and one sideband,
we save spectrum and concentrate our RF
energy into a narrower bandwidth. SSB is
therefore more efficient.

## Slide 13: Frequency Modulation
Unmodulated carrier, full power at all times
Waveform of modulating signal
Modulated carrier with frequency deviation and constant amplitude
“Over modulation” called “over deviation” on FM, causes the signal to become wider and potentially cause adjacent channel interference

## Slide 14: Common required Bandwidth
CW – 5-10Hz
Phone / Voice
  SSB - 2-3 kHz
  AM – 4-6 kHz
  FM – 5-15 kHz
Digital
  PSK31 – 31 Hz
  RTTY – 250 Hz
Slow Scan TV – 3KHz
Fast Scan TV – 6Mhz

## Slide 15: Amateur Television Signal
A 6 MHz ATV video channel with the video carrier 1.25 MHz up from the lower edge. The color subcarrier is at 3.58 MHz and the sound subcarrier at 4.5 MHz above the video carrier.
The Luminance, Chrominance and Audio carriers are visible in the spectrum plot at left

## Slide 16: T5B01 How many milliamperes is 1.5 amperes?
  A. 15 milliamperes
  B. 150 milliamperes
  C. 1,500 milliamperes
  D. 15,000 milliamperes

## Slide 17: T5B01 How many milliamperes is 1.5 amperes?
  A. 15 milliamperes
  B. 150 milliamperes
C. 1,500 milliamperes
  D. 15,000 milliamperes

## Slide 18: T5B02 What is another way to specify a radio signal frequency of 1,500,000 hertz?
  A. 1500 kHz
  B. 1500 MHz
  C. 15 GHz
  D. 150 kHz

## Slide 19: T5B02 What is another way to specify a radio signal frequency of 1,500,000 hertz?
A. 1500 kHz
  B. 1500 MHz
  C. 15 GHz
  D. 150 kHz

## Slide 20: T5B03 How many volts are equal to one kilovolt?
  A. One one-thousandth of a volt
  B. One hundred volts
  C. One thousand volts
  D. One million volts

## Slide 21: T5B03 How many volts are equal to one kilovolt?
  A. One one-thousandth of a volt
  B. One hundred volts
C. One thousand volts
  D. One million volts

## Slide 22: T5B04 How many volts are equal to one microvolt?
  A. One one-millionth of a volt
  B. One million volts
  C. One thousand kilovolts
  D. One one-thousandth of a volt

## Slide 23: T5B04 How many volts are equal to one microvolt?
A. One one-millionth of a volt
  B. One million volts
  C. One thousand kilovolts
  D. One one-thousandth of a volt

## Slide 24: T5B05 Which of the following is equivalent to 500 milliwatts?
  A. 0.02 watts
  B. 0.5 watts
  C. 5 watts
  D. 50 watts

## Slide 25: T5B05 Which of the following is equivalent to 500 milliwatts?
  A. 0.02 watts
B. 0.5 watts
  C. 5 watts
  D. 50 watts

## Slide 26: T5B06 If an ammeter calibrated in amperes is used to measure a 3000-milliampere current, what reading would it show?
  A. 0.003 amperes
  B. 0.3 amperes
  C. 3 amperes
  D. 3,000,000 amperes

## Slide 27: T5B06 If an ammeter calibrated in amperes is used to measure a 3000-milliampere current, what reading would it show?
  A. 0.003 amperes
  B. 0.3 amperes
C. 3 amperes
  D. 3,000,000 amperes

## Slide 28: T5B07 If a frequency readout calibrated in megahertz shows a reading of 3.525 MHz, what would it show if it were calibrated in kilohertz?
  A. 0.003525 kHz
  B. 35.25 kHz
  C. 3525 kHz
  D. 3,525,000 kHz

## Slide 29: T5B07 If a frequency readout calibrated in megahertz shows a reading of 3.525 MHz, what would it show if it were calibrated in kilohertz?
  A. 0.003525 kHz
  B. 35.25 kHz
C. 3525 kHz
  D. 3,525,000 kHz

## Slide 30: T5B08 How many microfarads are 1,000,000 picofarads?
  A. 0.001 microfarads
  B. 1 microfarad
  C. 1000 microfarads
  D. 1,000,000,000 microfarads

## Slide 31: T5B08 How many microfarads are 1,000,000 picofarads?
  A. 0.001 microfarads
B. 1 microfarad
  C. 1000 microfarads
  D. 1,000,000,000 microfarads

## Slide 32: T5B12 Which of the following frequencies is equal to 28,400 kHz?
A. 28.400 MHz
B. 2.800 MHz
C. 284.00 MHz
D. 28.400 kHz

## Slide 33: T5B12 Which of the following frequencies is equal to 28,400 kHz?
A. 28.400 MHz
B. 2.800 MHz
C. 284.00 MHz
D. 28.400 kHz

## Slide 34: T5B13 If a frequency readout shows a reading of 2425 MHz, what frequency is that in GHz?
A. 0.002425 GHZ
B. 24.25 GHz
C. 2.425 GHz
D. 2425 GHz

## Slide 35: T5B13 If a frequency readout shows a reading of 2425 MHz, what frequency is that in GHz?
A. 0.002425 GHZ
B. 24.25 GHz
C. 2.425 GHz
D. 2425 GHz

## Slide 36: T3B01 What is the name for the distance a radio wave travels during one complete cycle?
  A. Wave speed
  B. Waveform
  C. Wavelength
  D. Wave spread

## Slide 37: T3B01 What is the name for the distance a radio wave travels during one complete cycle?
  A. Wave speed
  B. Waveform
C. Wavelength
  D. Wave spread

## Slide 38: T3B04 How fast does a radio wave travel through free space?
  A. At the speed of light
  B. At the speed of sound
  C. Its speed is inversely proportional to its wavelength
  D. Its speed increases as the frequency increases

## Slide 39: T3B04 How fast does a radio wave travel through free space?
A. At the speed of light
  B. At the speed of sound
  C. Its speed is inversely proportional to its wavelength
  D. Its speed increases as the frequency increases

## Slide 40: T3B05 How does the wavelength of a radio wave relate to its frequency?
  A. The wavelength gets longer as the frequency increases
  B. The wavelength gets shorter as the frequency increases
  C. There is no relationship between wavelength and frequency
  D. The wavelength depends on the bandwidth of the signal

## Slide 41: T3B05 How does the wavelength of a radio wave relate to its frequency?
  A. The wavelength gets longer as the frequency increases
B. The wavelength gets shorter as the frequency increases
  C. There is no relationship between wavelength and frequency
  D. The wavelength depends on the bandwidth of the signal

## Slide 42: T3B06 What is the formula for converting frequency to approximate wavelength in meters?
A. Wavelength in meters equals frequency in hertz multiplied by 300
B. Wavelength in meters equals frequency in hertz divided by 300
C. Wavelength in meters equals frequency in megahertz divided by 300
D. Wavelength in meters equals 300 divided by frequency in megahertz

## Slide 43: T3B06 What is the formula for converting frequency to approximate wavelength in meters?
A. Wavelength in meters equals frequency in hertz multiplied by 300
B. Wavelength in meters equals frequency in hertz divided by 300
C. Wavelength in meters equals frequency in megahertz divided by 300
D. Wavelength in meters equals 300 divided by frequency in megahertz

## Slide 44: T3B07 What property of radio waves is often used to identify the different frequency bands?
  A. The approximate wavelength
  B. The magnetic intensity of waves
  C. The time it takes for waves to travel one mile
  D. The voltage standing wave ratio of waves

## Slide 45: T3B07 What property of radio waves is often used to identify the different frequency bands?
A. The approximate wavelength
  B. The magnetic intensity of waves
  C. The time it takes for waves to travel one mile
  D. The voltage standing wave ratio of waves

## Slide 46: T3B08 What are the frequency limits of the VHF spectrum?
  A. 30 to 300 kHz
  B. 30 to 300 MHz
  C. 300 to 3000 kHz
  D. 300 to 3000 MHz

## Slide 47: T3B08 What are the frequency limits of the VHF spectrum?
  A. 30 to 300 kHz
B. 30 to 300 MHz
  C. 300 to 3000 kHz
  D. 300 to 3000 MHz

## Slide 48: T3B09 What are the frequency limits of the UHF spectrum?
  A. 30 to 300 kHz
  B. 30 to 300 MHz
  C. 300 to 3000 kHz
  D. 300 to 3000 MHz

## Slide 49: T3B09 What are the frequency limits of the UHF spectrum?
  A. 30 to 300 kHz
  B. 30 to 300 MHz
  C. 300 to 3000 kHz
D. 300 to 3000 MHz

## Slide 50: T3B10 What frequency range is referred to as HF?
  A. 300 to 3000 MHz
  B. 30 to 300 MHz
  C. 3 to 30 MHz
  D. 300 to 3000 kHz

## Slide 51: T3B10 What frequency range is referred to as HF?
  A. 300 to 3000 MHz
  B. 30 to 300 MHz
C. 3 to 30 MHz
  D. 300 to 3000 kHz

## Slide 52: T3B11 What is the approximate velocity of a radio wave as it travels through free space?
  A. 3000 kilometers per second
  B. 300,000,000 meters per second
  C. 300,000 miles per hour
  D. 186,000 miles per hour

## Slide 53: T3B11 What is the approximate velocity of a radio wave as it travels through free space?
  A. 3000 kilometers per second
B. 300,000,000 meters per second
  C. 300,000 miles per hour
  D. 186,000 miles per hour

## Slide 54: T5A12 What term describes the number of times per second that an alternating current reverses direction?
  A. Pulse rate
  B. Speed
  C. Wavelength
  D. Frequency

## Slide 55: T5A12 What term describes the number of times per second that an alternating current reverses direction?
  A. Pulse rate
  B. Speed
  C. Wavelength
D. Frequency

## Slide 56: T5C05 What is the unit of frequency?
  A. Hertz
  B. Henry
  C. Farad
  D. Tesla

## Slide 57: T5C05 What is the unit of frequency?
A. Hertz
  B. Henry
  C. Farad
  D. Tesla

## Slide 58: T5C06 What does the abbreviation “RF” refer to?
A. Radio frequency signals of all types
B. The resonant frequency of a tuned circuit
C. The real frequency transmitted as opposed to the apparent frequency
D. Reflective force in antenna transmission lines

## Slide 59: T5C06 What does the abbreviation “RF” refer to?
A. Radio frequency signals of all types
B. The resonant frequency of a tuned circuit
C. The real frequency transmitted as opposed to the apparent frequency
D. Reflective force in antenna transmission lines

## Slide 60: T1B09 Why should you not set your transmit frequency to be exactly at the edge of an amateur band or sub-band?
  A. To allow for calibration error in the transmitter frequency display
  B. So that modulation sidebands do not extend beyond the band edge
  C. To allow for transmitter frequency drift
  D. All of these choices are correct

## Slide 61: T1B09 Why should you not set your transmit frequency to be exactly at the edge of an amateur band or sub-band?
  A. To allow for calibration error in the transmitter frequency display
  B. So that modulation sidebands do not extend beyond the band edge
  C. To allow for transmitter frequency drift
D. All of these choices are correct

## Slide 62: T2B05 What determines the amount of deviation of an FM signal?
  A. Both the frequency and amplitude of the modulating signal
  B. The frequency of the modulating signal
  C. The amplitude of the modulating signal
  D. The relative phase of the modulating signal and the carrier

## Slide 63: T2B05 What determines the amount of deviation of an FM signal?
  A. Both the frequency and amplitude of the modulating signal
  B. The frequency of the modulating signal
C. The amplitude of the modulating signal
  D. The relative phase of the modulating signal and the carrier

## Slide 64: T2B06 What happens when the deviation of an FM transmitter is increased?
  A. Its signal occupies more bandwidth
  B. Its output power increases
  C. Its output power and bandwidth increases
  D. Asymmetric modulation occurs

## Slide 65: T2B06 What happens when the deviation of an FM transmitter is increased?
A. Its signal occupies more bandwidth
  B. Its output power increases
  C. Its output power and bandwidth increases
  D. Asymmetric modulation occurs

## Slide 66: T2B07 What could cause your FM signal to interfere with stations on nearby frequencies?
A. Microphone gain too high, causing over-deviation
B. SWR too high
C. Incorrect CTCSS Tone
D. All of these choices are correct

## Slide 67: T2B07 What could cause your FM signal to interfere with stations on nearby frequencies?
A. Microphone gain too high, causing over-deviation
B. SWR too high
C. Incorrect CTCSS Tone
D. All of these choices are correct

## Slide 68: T8A01 Which of the following is a form of amplitude modulation?
  A. Spread-spectrum
  B. Packet radio
  C. Single sideband
  D. Phase shift keying

## Slide 69: T8A01 Which of the following is a form of amplitude modulation?
  A. Spread-spectrum
  B. Packet radio
C. Single sideband
  D. Phase shift keying

## Slide 70: T8A02 What type of modulation is most commonly used for VHF packet radio transmissions?
  A. FM
  B. SSB
  C. AM
  D. Spread Spectrum

## Slide 71: T8A02 What type of modulation is most commonly used for VHF packet radio transmissions?
A. FM
  B. SSB
  C. AM
  D. Spread Spectrum

## Slide 72: T8A03 Which type of voice mode is most often used for long-distance (weak signal) contacts on the VHF and UHF bands?
A. FM
B. DRM
C. SSB
D. PM

## Slide 73: T8A03 Which type of voice mode is most often used for long-distance (weak signal) contacts on the VHF and UHF bands?
A. FM
B. DRM
C. SSB
D. PM

## Slide 74: T8A04 Which type of modulation is most commonly used for VHF and UHF voice repeaters?
  A. AM
  B. SSB
  C. PSK
  D. FM

## Slide 75: T8A04 Which type of modulation is most commonly used for VHF and UHF voice repeaters?
  A. AM
  B. SSB
  C. PSK
D. FM

## Slide 76: T8A05 Which of the following types of emission has the narrowest bandwidth?
  A. FM voice
  B. SSB voice
  C. CW
  D. Slow-scan TV

## Slide 77: T8A05 Which of the following types of emission has the narrowest bandwidth?
  A. FM voice
  B. SSB voice
C. CW
  D. Slow-scan TV

## Slide 78: T8A06 Which sideband is normally used for 10 meter HF, VHF and UHF single-sideband communications?
  A. Upper sideband
  B. Lower sideband
  C. Suppressed sideband
  D. Inverted sideband

## Slide 79: T8A06 Which sideband is normally used for 10 meter HF, VHF and UHF single-sideband communications?
A. Upper sideband
  B. Lower sideband
  C. Suppressed sideband
  D. Inverted sideband

## Slide 80: T8A07 What is the primary advantage of single sideband over FM for voice transmissions?
  A. SSB signals are easier to tune
  B. SSB signals are less susceptible to interference
  C. SSB signals have narrower bandwidth
  D. All of these choices are correct

## Slide 81: T8A07 What is the primary advantage of single sideband over FM for voice transmissions?
  A. SSB signals are easier to tune
  B. SSB signals are less susceptible to interference
C. SSB signals have narrower bandwidth
  D. All of these choices are correct

## Slide 82: T8A08 What is the approximate bandwidth of a single sideband voice signal?
  A. 1 kHz
  B. 3 kHz
  C. 6 kHz
  D. 15 kHz

## Slide 83: T8A08 What is the approximate bandwidth of a single sideband voice signal?
  A. 1 kHz
B. 3 kHz
  C. 6 kHz
  D. 15 kHz

## Slide 84: T8A09 What is the approximate bandwidth of a VHF repeater FM phone signal?
A. Less than 500 Hz
B. About 150 kHz
C. Between 10 and 15 kHz
D. Between 50 and 125 kHz

## Slide 85: T8A09 What is the approximate bandwidth of a VHF repeater FM phone signal?
A. Less than 500 Hz
B. About 150 kHz
C. Between 10 and 15 kHz
D. Between 50 and 125 kHz

## Slide 86: T8A10 What is the typical bandwidth of analog fast-scan TV transmissions on the 70 cm band?
  A. More than 10 MHz
  B. About 6 MHz
  C. About 3 MHz
  D. About 1 MHz

## Slide 87: T8A10 What is the typical bandwidth of analog fast-scan TV transmissions on the 70 cm band?
  A. More than 10 MHz
B. About 6 MHz
  C. About 3 MHz
  D. About 1 MHz

## Slide 88: T8A11 What is the approximate maximum bandwidth required to transmit a CW signal?
  A. 2.4 kHz
  B. 150 Hz
  C. 1000 Hz
  D. 15 kHz

## Slide 89: T8A11 What is the approximate maximum bandwidth required to transmit a CW signal?
  A. 2.4 kHz
B. 150 Hz
  C. 1000 Hz
  D. 15 kHz

## Slide 90: T1F09 What type of amateur station simultaneously retransmits the signal of another amateur station on a different channel or channels?
  A. Beacon station
  B. Earth station
  C. Repeater station
  D. Message forwarding station

## Slide 91: T1F09 What type of amateur station simultaneously retransmits the signal of another amateur station on a different channel or channels?
  A. Beacon station
  B. Earth station
C. Repeater station
  D. Message forwarding station

## Slide 92: T7A02 What is a transceiver?
A. A type of antenna switch
B. A unit combining the functions of a transmitter and a receiver
C. A component in a repeater which filters out unwanted interference
D. A type of antenna matching network

## Slide 93: T7A02 What is a transceiver?
A. A type of antenna switch
B. A unit combining the functions of a transmitter and a receiver
C. A component in a repeater which filters out unwanted interference
D. A type of antenna matching network