## Slide 1: SAFETY
Radio Frequency
Electrical
Tower

## Slide 2
Common sense!
Hot! Don’t touch!

## Slide 3: Common Sense RF Safety Guidelines
Contain RF Radiation to the Antenna
.Don’t Operate Transmitters or Amplifiers with
Covers and Shielding Removed
.Keep People Away from Antennas with
. High- Power Operation

## Slide 4: Maximum Permissible Exposure

## Slide 6: Non-thermal Effects
“In conclusion, the data do not support the finding that exposures to RF fields is a causal agent for any type of cancer”
“Although the data base has grown substantially over the past decades, much of the information concerning nonthermal effects is generally inconclusive, incomplete and sometimes contradictory. Studies of human populations have not demonstrated and reliably effected end point”
Radio Frequency and ELF Electromagnetic Energies: A Handbook for Health Professionals

## Slide 7: T0A01 Which of the following is a safety hazard of a 12-volt storage battery?
  A. Touching both terminals with the hands can cause electrical shock
  B. Shorting the terminals can cause burns, fire, or an explosion
  C. RF emissions from the battery
  D. All of these choices are correct

## Slide 8: T0A01 Which of the following is a safety hazard of a 12-volt storage battery?
  A. Touching both terminals with the hands can cause electrical shock
B. Shorting the terminals can cause burns, fire, or an explosion
C. RF emissions from the battery
D. All of these choices are correct

## Slide 9: T0A02 How does current flowing through the body cause a health hazard?
  A. By heating tissue
  B. It disrupts the electrical functions of cells
  C. It causes involuntary muscle contractions
  D. All of these choices are correct

## Slide 10: T0A02 How does current flowing through the body cause a health hazard?
  A. By heating tissue
  B. It disrupts the electrical functions of cells
  C. It causes involuntary muscle contractions
D. All of these choices are correct

## Slide 11: T0A03 What is connected to the green wire in a three-wire electrical AC plug?
  A. Neutral
  B. Hot
  C. Safety ground
  D. The white wire

## Slide 12: T0A03 What is connected to the green wire in a three-wire electrical AC plug?
  A. Neutral
  B. Hot
C. Safety ground
  D. The white wire

## Slide 13: T0A06 What is a good way to guard against electrical shock at your station?
  A. Use three-wire cords and plugs for all AC powered equipment
  B. Connect all AC powered station equipment to a common safety ground
  C. Use a circuit protected by a ground-fault interrupter
  D. All of these choices are correct

## Slide 14: T0A06 What is a good way to guard against electrical shock at your station?
  A. Use three-wire cords and plugs for all AC powered equipment
  B. Connect all AC powered station equipment to a common safety ground
  C. Use a circuit protected by a ground-fault interrupter
D. All of these choices are correct

## Slide 15: T0A07 Which of these precautions should be taken when installing devices for lightning protection in a coaxial cable feed line?
A. Include a parallel bypass switch for each protector so that it can be switched out of the circuit when running high power
B. Include a series switch in the ground line of each protector to prevent RF overload from inadvertently damaging the protector
C. Keep the ground wires from each protector separate and connected to station ground
D. Ground all of the protectors to a common plate which is in turn connected to an external ground

## Slide 16: T0A07 Which of these precautions should be taken when installing devices for lightning protection in a coaxial cable feed line?
A. Include a parallel bypass switch for each protector so that it can be switched out of the circuit when running high power
B. Include a series switch in the ground line of each protector to prevent RF overload from inadvertently damaging the protector
C. Keep the ground wires from each protector separate and connected to station ground
D. Ground all of the protectors to a common plate which is in turn connected to an external ground

## Slide 17: T0A08 What safety equipment should always be included in home-built equipment that is powered from 120V AC power circuits?
  A. A fuse or circuit breaker in series with the AC "hot" conductor
  B. An AC voltmeter across the incoming power source
  C. An inductor in series with the AC power source
  D. A capacitor across the AC power source

## Slide 18: T0A08 What safety equipment should always be included in home-built equipment that is powered from 120V AC power circuits?
A. A fuse or circuit breaker in series with the AC "hot" conductor
  B. An AC voltmeter across the incoming power source
  C. An inductor in series with the AC power source
  D. A capacitor across the AC power source

## Slide 19: T0A11 What kind of hazard might exist in a power supply when it is turned off and disconnected?
A. Static electricity could damage the grounding system
B. Circulating currents inside the transformer might cause damage
C. The fuse might blow if you remove the cover
D. You might receive an electric shock from the charged stored in large capacitors

## Slide 20: T0A11 What kind of hazard might exist in a power supply when it is turned off and disconnected?
A. Static electricity could damage the grounding system
B. Circulating currents inside the transformer might cause damage
C. The fuse might blow if you remove the cover
D. You might receive an electric shock from the charged stored in large capacitors

## Slide 21: T0B10 Which of the following is true concerning grounding conductors used for lightning protection?
  A. Only non-insulated wire must be used
  B. Wires must be carefully routed with precise right-angle bends
  C. Sharp bends must be avoided
  D. Common grounds must be avoided

## Slide 22: T0B10 Which of the following is true concerning grounding conductors used for lightning protection?
  A. Only non-insulated wire must be used
  B. Wires must be carefully routed with precise right-angle bends
C. Sharp bends must be avoided
  D. Common grounds must be avoided

## Slide 23: T0B11 Which of the following establishes grounding requirements for an amateur radio tower or antenna?
  A. FCC Part 97 Rules
  B. Local electrical codes
  C. FAA tower lighting regulations
  D. Underwriters Laboratories' recommended practices

## Slide 24: T0B11 Which of the following establishes grounding requirements for an amateur radio tower or antenna?
  A. FCC Part 97 Rules
B. Local electrical codes
  C. FAA tower lighting regulations
  D. Underwriters Laboratories' recommended practices

## Slide 25: T0B12 Which of the following is good practice when installing ground wires on a tower for lightning protection?
  A. Put a loop in the ground connection to prevent water damage to the ground system
  B. Make sure that all bends in the ground wires are clean, right angle bends
  C. Ensure that connections are short and direct
  D. All of these choices are correct

## Slide 26: T0B12 Which of the following is good practice when installing ground wires on a tower for lightning protection?
  A. Put a loop in the ground connection to prevent water damage to the ground system
  B. Make sure that all bends in the ground wires are clean, right angle bends
C. Ensure that connections are short and direct
  D. All of these choices are correct

## Slide 27: T0C01 What type of radiation are VHF and UHF radio signals?
  A. Gamma radiation
  B. Ionizing radiation
  C. Alpha radiation
  D. Non-ionizing radiation

## Slide 28: T0C01 What type of radiation are VHF and UHF radio signals?
  A. Gamma radiation
  B. Ionizing radiation
  C. Alpha radiation
D. Non-ionizing radiation

## Slide 29: T0C02 Which of the following frequencies has the lowest Maximum Permissible Exposure limit?
  A. 3.5 MHz
  B. 50 MHz
  C. 440 MHz
  D. 1296 MHz

## Slide 30: T0C02 Which of the following frequencies has the lowest Maximum Permissible Exposure limit?
  A. 3.5 MHz
B. 50 MHz
  C. 440 MHz
  D. 1296 MHz

## Slide 31: T0C03 What is the maximum power level that an amateur radio station may use at VHF frequencies before an RF exposure evaluation is required?
  A. 1500 watts PEP transmitter output
  B. 1 watt forward power
  C. 50 watts PEP at the antenna
  D. 50 watts PEP reflected power

## Slide 32: T0C03 What is the maximum power level that an amateur radio station may use at VHF frequencies before an RF exposure evaluation is required?
  A. 1500 watts PEP transmitter output
  B. 1 watt forward power
C. 50 watts PEP at the antenna
  D. 50 watts PEP reflected power

## Slide 33: T0C04 What factors affect the RF exposure of people near an amateur station antenna?
  A. Frequency and power level of the RF field
  B. Distance from the antenna to a person
  C. Radiation pattern of the antenna
  D. All of these choices are correct

## Slide 34: T0C04 What factors affect the RF exposure of people near an amateur station antenna?
  A. Frequency and power level of the RF field
  B. Distance from the antenna to a person
  C. Radiation pattern of the antenna
D. All of these choices are correct

## Slide 35: T0C05 Why do exposure limits vary with frequency?
  A. Lower frequency RF fields have more energy than higher frequency fields
  B. Lower frequency RF fields do not penetrate the human body
  C. Higher frequency RF fields are transient in nature
  D. The human body absorbs more RF energy at some frequencies than at others

## Slide 36: T0C05 Why do exposure limits vary with frequency?
  A. Lower frequency RF fields have more energy than higher frequency fields
  B. Lower frequency RF fields do not penetrate the human body
  C. Higher frequency RF fields are transient in nature
D. The human body absorbs more RF energy at some frequencies than at others

## Slide 37: T0C06 Which of the following is an acceptable method to determine that your station complies with FCC RF exposure regulations?
  A. By calculation based on FCC OET Bulletin 65
  B. By calculation based on computer modeling
  C. By measurement of field strength using calibrated equipment
  D. All of these choices are correct

## Slide 38: T0C06 Which of the following is an acceptable method to determine that your station complies with FCC RF exposure regulations?
  A. By calculation based on FCC OET Bulletin 65
  B. By calculation based on computer modeling
  C. By measurement of field strength using calibrated equipment
D. All of these choices are correct

## Slide 39: T0C07 What could happen if a person accidentally touched your antenna while you were transmitting?
  A. Touching the antenna could cause television interference
  B. They might receive a painful RF burn
  C. They might develop radiation poisoning
  D. All of these choices are correct

## Slide 40: T0C07 What could happen if a person accidentally touched your antenna while you were transmitting?
  A. Touching the antenna could cause television interference
B. They might receive a painful RF burn
  C. They might develop radiation poisoning
  D. All of these choices are correct

## Slide 41: T0C08 Which of the following actions might amateur operators take to prevent exposure to RF radiation in excess of FCC-supplied limits?
  A. Relocate antennas
  B. Relocate the transmitter
  C. Increase the duty cycle
  D. All of these choices are correct

## Slide 42: T0C08 Which of the following actions might amateur operators take to prevent exposure to RF radiation in excess of FCC- supplied limits?
A. Relocate antennas
  B. Relocate the transmitter
  C. Increase the duty cycle
  D. All of these choices are correct

## Slide 43: T0C09 How can you make sure your station stays in compliance with RF safety regulations?
  A. By informing the FCC of any changes made in your station
  B. By re-evaluating the station whenever an item of equipment is changed
  C. By making sure your antennas have low SWR
  D. All of these choices are correct

## Slide 44: T0C09 How can you make sure your station stays in compliance with RF safety regulations?
  A. By informing the FCC of any changes made in your station
B. By re-evaluating the station whenever an item of equipment is changed
  C. By making sure your antennas have low SWR
  D. All of these choices are correct

## Slide 45: T0C10 Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
A. It affects the average exposure of people to radiation
B. It affects the peak exposure of people to radiation
C. It takes into account the antenna feed line loss
D. It takes into account the thermal effects of the final amplifier

## Slide 46: T0C10 Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
A. It affects the average exposure of people to radiation
B. It affects the peak exposure of people to radiation
C. It takes into account the antenna feed line loss
D. It takes into account the thermal effects of the final amplifier

## Slide 47: T0C11 What is the definition of duty cycle during the averaging time for RF exposure?
  A. The difference between the lowest power output and the highest power output of a transmitter
  B. The difference between the PEP and average power output of a transmitter
  C. The percentage of time that a transmitter is transmitting
  D. The percentage of time that a transmitter is not transmitting

## Slide 48: T0C11 What is the definition of duty cycle during the averaging time for RF exposure?
  A. The difference between the lowest power output and the highest power output of a transmitter
  B. The difference between the PEP and average power output of a transmitter
  C. The percentage of time that a transmitter is transmitting
  D. The percentage of time that a transmitter is not transmitting

## Slide 49: T0C12 How does RF radiation differ from ionizing radiation (radioactivity)?
A. RF radiation does not have sufficient energy to cause genetic damage
B. RF radiation can only be detected with an RF dosimeter
C. RF radiation is limited in range to a few feet
D. RF radiation is perfectly safe

## Slide 50: T0C12 How does RF radiation differ from ionizing radiation (radioactivity)?
A. RF radiation does not have sufficient energy to cause genetic damage
B. RF radiation can only be detected with an RF dosimeter
C. RF radiation is limited in range to a few feet
D. RF radiation is perfectly safe

## Slide 51: T0C13 If the averaging time for exposure is 6 minutes, how much power density is permitted if the signal is present for 3 minutes and absent for 3 minutes rather than being present for the entire 6 minutes?
A. 3 times as much
B. 1/2 as much
C. 2 times as much
D. There is no adjustment allowed for shorter exposure times

## Slide 52: T0C13 If the averaging time for exposure is 6 minutes, how much power density is permitted if the signal is present for 3 minutes and absent for 3 minutes rather than being present for the entire 6 minutes?
  A. 3 times as much
  B. 1/2 as much
C. 2 times as much
  D. There is no adjustment allowed for shorter exposure times

## Slide 53: T0B01 When should members of a tower work team wear a hard hat and safety glasses?
  A. At all times except when climbing the tower
  B. At all times except when belted firmly to the tower
  C. At all times when any work is being done on the tower
  D. Only when the tower exceeds 30 feet in height

## Slide 54: T0B01 When should members of a tower work team wear a hard hat and safety glasses?
  A. At all times except when climbing the tower
  B. At all times except when belted firmly to the tower
C. At all times when any work is being done on the tower
  D. Only when the tower exceeds 30 feet in height

## Slide 55: T0B02 What is a good precaution to observe before climbing an antenna tower?
  A. Make sure that you wear a grounded wrist strap
  B. Remove all tower grounding connections
  C. Put on a climbing harness and safety glasses
  D. All of the these choices are correct

## Slide 56: T0B02 What is a good precaution to observe before climbing an antenna tower?
  A. Make sure that you wear a grounded wrist strap
  B. Remove all tower grounding connections
C. Put on a climbing harness and safety glasses
  D. All of the these choices are correct

## Slide 57: T0B03 Under what circumstances is it safe to climb a tower without a helper or observer?
  A. When no electrical work is being performed
  B. When no mechanical work is being performed
  C. When the work being done is not more than 20 feet above the ground
  D. Never

## Slide 58: T0B03 Under what circumstances is it safe to climb a tower without a helper or observer?
  A. When no electrical work is being performed
  B. When no mechanical work is being performed
  C. When the work being done is not more than 20 feet above the ground
D. Never

## Slide 59: T0B04 Which of the following is an important safety precaution to observe when putting up an antenna tower?
  A. Wear a ground strap connected to your wrist at all times
  B. Insulate the base of the tower to avoid lightning strikes
  C. Look for and stay clear of any overhead electrical wires
  D. All of these choices are correct

## Slide 60: T0B04 Which of the following is an important safety precaution to observe when putting up an antenna tower?
  A. Wear a ground strap connected to your wrist at all times
  B. Insulate the base of the tower to avoid lightning strikes
C. Look for and stay clear of any overhead electrical wires
  D. All of these choices are correct

## Slide 61: T0B05 What is the purpose of a gin pole?
  A. To temporarily replace guy wires
  B. To be used in place of a safety harness
  C. To lift tower sections or antennas
  D. To provide a temporary ground

## Slide 63: T0B05 What is the purpose of a gin pole?
  A. To temporarily replace guy wires
  B. To be used in place of a safety harness
C. To lift tower sections or antennas
  D. To provide a temporary ground

## Slide 64: T0B06 What is the minimum safe distance from a power line to allow when installing an antenna?
  A. Half the width of your property
  B. The height of the power line above ground
  C. 1/2 wavelength at the operating frequency
  D. So that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires

## Slide 65: T0B06 What is the minimum safe distance from a power line to allow when installing an antenna?
  A. Half the width of your property
  B. The height of the power line above ground
  C. 1/2 wavelength at the operating frequency
D. So that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires

## Slide 66: T0B07 Which of the following is an important safety rule to remember when using a crank-up tower?
  A. This type of tower must never be painted
  B. This type of tower must never be grounded
  C. This type of tower must never be climbed unless it is in the fully retracted position
  D. All of these choices are correct

## Slide 67: T0B07 Which of the following is an important safety rule to remember when using a crank-up tower?
  A. This type of tower must never be painted
  B. This type of tower must never be grounded
C. This type of tower must never be climbed unless it is in the fully retracted position
  D. All of these choices are correct

## Slide 68: T0B08 What is considered to be a proper grounding method for a tower?
  A. A single four-foot ground rod, driven into the ground no more than 12 inches from the base
  B. A ferrite-core RF choke connected between the tower and ground
  C. Separate eight-foot long ground rods for each tower leg, bonded to the tower and each other
  D. A connection between the tower base and a cold water pipe

## Slide 69: T0B08 What is considered to be a proper grounding method for a tower?
  A. A single four-foot ground rod, driven into the ground no more than 12 inches from the base
  B. A ferrite-core RF choke connected between the tower and ground
C. Separate eight-foot long ground rods for each tower leg, bonded to the tower and each other
  D. A connection between the tower base and a cold water pipe

## Slide 70: T0B09 Why should you avoid attaching an antenna to a utility pole?
  A. The antenna will not work properly because of induced voltages
  B. The utility company will charge you an extra monthly fee
  C. The antenna could contact high-voltage power wires
  D. All of these choices are correct

## Slide 71: T0B09 Why should you avoid attaching an antenna to a utility pole?
  A. The antenna will not work properly because of induced voltages
  B. The utility company will charge you an extra monthly fee
C. The antenna could contact high-voltage power wires
  D. All of these choices are correct